## Slide 1: WF on 60GHz beam switching
Apple
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic Meeting, April 12th – 20th, 2021
Agenda Item: 8.12.4.1
R4-2105413

## Slide 2: Background
The following issues related to 60 GHz beam switching have been summarized in the related email discussion [9]:
  Issue 1-1: UE Switching from DL to UL and UL to DL
  Issue 1-2: UE Switching TX and RX beams
  Issue 1-3: Minimum duration between beam switches
  Issue 1-4: gNB beam switching
  Issue 1-5: Reply LS out to RAN1

## Slide 3: Issue 1-1: UE Switching from DL to UL and UL to DL
Way Forward
  Based on 7 companies’ support of Option 1, and 4 companies’ support of an option other than 1, the value of [7 us] is taken as a starting point
    The following will be further discussed:
      Cell coverages and system overhead aspects
      System throughput aspects
      Whether an optional capability of a faster switching time is feasible
      Other considerations are not precluded
Proposal | Companies supporting
Option 1: 7us, 13792 Tc | MediaTek, CATT, Charter, Qualcomm, Apple, Huawei, Xiaomi
Option 2: depends on cell phase sync and transients | ZTE, Ericsson
Option 3: 3 us | Intel
Option 4 (new): evaluate improvement over FR2 | Nokia

## Slide 4: Issue 1-2: UE Switching TX and RX beams
Way Forward
  Evaluations of potential improvement over FR2 are encouraged by the next meeting
Proposal | Companies supporting
Option 1: Re-use FR 2 assumption (200 ns) | MediaTek, Qualcomm, Apple
Option 2: 100 ns | Charter
Option 3: 50 ns | Ericsson, Nokia, Intel
Option 4: 20 ns | 
Option 5 (new): FFS | ZTE, Sony, Huawei, Xiaomi

## Slide 5: Issue 1-3: Minimum duration between beam switches
Way Forward
  The value of [5 us] is taken as a starting point
  Evaluations are encouraged by the next meeting to either confirm the value or to define a new values based on the companies’ analysis
Proposal | Companies supporting
Option 1: 4.5us | Qualcomm
Option 2: 5us | Huawei
Option 2 (new): FFS | MediaTek

## Slide 6: Issue 1-4: gNB beam switching
Way Forward
  Because no clear preference has emerged, evaluations are encouraged by the next meeting
Proposal | Companies supporting
Option 1: 59 us max (typo?) | Charter
Option 2: 100 ns | CATT
Option 3: 20 ns | ZTE
Option 4 (new): 50 ns | Ericsson, Nokia
Option 5 (new): More analysis needed | Huawei

## Slide 7: Issue 1-5: Reply LS out to RAN1
Way Forward
  send an LS to RAN1 with final agreements (most likely, next meeting)
Parameter | Value
UE Switching from DL to UL and UL to DL | 
UE Switching TX and RX beams | 
Minimum duration between beam switches | 
gNB beam switching | 

## Slide 8: References
Ref | T-doc | Company | Title
[1] | R4-2107271 | Huawei, HiSilicon Technologies Co. Ltd | On 60GHz beam switching
[2] | R4-2106909 | Apple | On open loop TPC and transient requirements for NR in the 52.6 - 71 GHz frequency range
[3] | R4-2104805 | CATT | Discussion on the reply LS on beam switching gap
[4] | R4-2105138 | Ericsson | Reply LS to RAN1: LS on beam switching gap for 60 GHz band
[5] | R4-2106591 | ZTE Corporation | Discussion on switching delay for 52.6-71GHz
[6] | R4-2107191 | Nokia, Nokia Shanghai Bell | On UE Tx RF aspects for a NR band in the range 52.6GHz – 71GHz
[7] | R4-2107210 | Qualcomm Incorporated | 60GHz UE switching times
[8] | R4-2107342 | Intel Corporation | UE RF Tx requirements for NR extension to 71GHz
[9] | R4-2105211 | Moderator (Qualcomm) | Email discussion summary for [98-bis-e][138] NR_ext_to_71GHz_Part_2