## Slide 1: WF on UE RF requirements for DL 1024QAM
Ericsson, [CATT, Huawei, HiSilicon, CMCC, China Unicom, Nokia, Nokia Shanghai Bell, Qualcomm]
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2105416 Electronic Meeting, 12th – 20th of April, 2021

## Slide 2: EVM evaluation parameters
Proceed with option 3: Further discuss and align link level simulation assumptions w.r.t parameters and their values
  Use parameters in R4-2104726 as a starting point
  Suggested modifications of R4-2104726
    Rx EVM range 1%-2% 0.5%-2.0%
    Tx EVM range 0.5%-2.0%
    CBW=100MHz, SCS=30kHz, fc=4GHz (assuming TDD midband).
    CBW=50MHz, SCS=15kHz fc=2GHz (assuming FDD lowband).
    Precoding: Keep only random precoding (there is no big impact of follow PMI on performance for scenario with 2 Tx)
    HARQ: Maximum number of HARQ transmission = 4 with RV sequence {0,2,3,1}
    BS antenna configuration: We can keep only 2 Tx case
    UE antenna configuration: Probably we also can check performance for 2 Rx UE
    PDSCH configuration: Type A mapping, Start symbol 2, Duration 12 (for D slots)
    Other parameters not precluded
Discussion (and possible agreement) on above bullets will be captured in the final version of the WF as an input to next meeting
Moderator (after 2nd round): Suggests to continue the above discussion on Link level parameters at next meeting due to the ongoing parallel parameter discussion for the Base Station. No agreement at this stage. This is also reflected in the 2nd round summary.
  The input above is kept in the WF as background information.
  It shall be noted that the BS side of the W.I. has agreed to use R4-2104726 as a basis (but use a wider bandwidth), captured in WF (R4-2106121)

## Slide 3: Maximum input level
Agree on the proposal provided:
  Use a 0dB relaxation for 1024QAM compared to 256QAM
  Introduce an appropriate note in the Maximum input tables in 38.101-1 referring to new RMCs defined in annex A (RMCs to be settled during performance part of the WI).

## Slide 4: Work split for impacted TS
To be settled in 2nd round
No agreement on this part sine no one volunteerd for TS38.101-1, to be continued at the next meeting:
  As information the rapporteurs suggested the shown matrix (it has been partly filled for the BS Specs, highlighted in green):
Spec number | Responsible
38.101-1 | Huawei
38.104 | Huawei
38.141-1 | ZTE
38.141-2 | Ericsson
37.104 | CATT
37.141 | ZTE
35.105 | CATT
37.145-1 | CATT
37.145-2 | Nokia

## Slide 5: Related papers
R4-2104726, CATT, “Link level simulation results for 1024QAM for NR FR1”
R4-2104727, CATT, “System level simulation results for 1024QAM for NR FR1” (Tdoc not available and hence withdrawn)
R4-2106858, Ericsson, Nokia, Nokia Shanghai Bell, “Work plan for DL 1024QAM for NR FR1”
R4-2104729, CATT, “Discussion on UE RX RF requirements for 1024QAM for NR FR1”
R4-2106489, Huawei, HiSilicon, CMCC, China Unicom, “RX EVM for support of 1024QAM”
R4-2106688, Ericsson, “UE Requirement Overview and Impact for 1024 QAM”