## Slide 1: WF on phase continuity and power consistency for PUCCH and PUSCH repetition
Huawei, HiSilicon
R4-2105418
3GPP TSG-RAN WG4 #98bis-e
April 12 – 20, 2021
Electronic meeting

## Slide 2: WF1: Non-zero un-scheduled gap
Issue 1-1-1: Non-zero un-scheduled gap
  Proposals
    Option 1: Feasible
    Option 2: Deprioritize non-zero gap scenario
Issue 1-1-1A: Length of un-scheduled gap
  Proposals
    Option 1: Less than 14 OFDM symbols
    Option 2: Up to 14 OFDM symbols
Agreement:
  RAN4 confirms the phase can be maintained when there is non-zero un-scheduled gap in-between the PUSCH or PUCCH repetition
  Further study on following issues:
    Whether off power requirement can be met on the un-scheduled symbols
    The length of non-zero un-scheduled gap

## Slide 3: WF2: Non-zero gap with other signals/channels
Issue 1-1-2: Non-zero gap with other signals/channels for the UE
  Proposals
    Option 1: Not consider these scenarios
    Option 2: A guard period before returning to the repetitions should be defined, and the length including the guard period of the other channel in between two repetitions is less than 14 symbols.
  Agreement:
    RAN4 confirms the phase can be maintained when there is non-zero gap with other signals/channels in-between the PUSCH or PUCCH repetition if the other signals/channels scheduled during the gap have the same transmission setting with the repetitions, i.e. the same antenna port, RB allocation, transmission power
    Further study on following issue:
      Whether phase continuity can be maintained if the other signals/channels power in-between the repetitions can be different with the power of repetition or if PRB content of the channels/signals in between can be different

## Slide 4: WF3: CA and DC scenarios
Issue 1-1-3: PUCCH/PUSCH repetition under CA and DC scenarios
  Proposals
    Option 1: RAN4 to further check the use case and the necessity to consider phase continuity and power consistency for UL repetition under CA and DC scenarios.
  Agreement:
    Keep the RAN4 agreements in the reply LS approved in the last meeting, and leave the decision on the applicable use cases to RAN1.

## Slide 5: WF4: Phase drift mitigation methods like PT-RS insertion
Issue 1-1-4: Phase drift mitigation methods like PT-RS insertion for FR1 and FR2
  Proposals
    Study the phase continuity for non-contiguous and contiguous transmissions and implementation phase drift issues in the context of mitigations methods like PT-RS insertion for FR1 and FR2.
  Agreement:
    leave the decision on the PTRS insertion to RAN1.

## Slide 6: WF5: DL slot(s) in-between repetition
Issue 1-1-5: DL slot(s) in-between repetition
  Proposals
    Use different antennas/panels for UL and DL traffic during the JCE window
  Agreement:
    RAN4 further study on the feasibility of phase continuity when there is DL slot(s) in-between repetitions

## Slide 7: WF6: phase continuity tolerance
Issue 1-2-1: Amount of phase change from UE implementation aspect
  Proposals
    The amount of phase change allowed for the UE when phase between two repetitions is considered to be contiguous shall be less than 160 degrees.
Issue 1-2-1: Quantification of the acceptable/required tolerance
  Proposals
    To estimate the required tolerance of the phase continuity and amplitude consistency from link performance perspective
Agreement:
  RAN4 to evaluate the required tolerance of the phase continuity and amplitude consistency from link performance simulation:
    RAN4 to provide simulation assumption in the next meeting
    Initial simulation result is also encouraged to be provided in the next meeting

## Slide 8: Reference
[1] R4-2104580, “Discussion on phase continuity and power consistency for UL repetition”, MTK
[2] R4-2104955, “On non-zero gap between adjacent transmissions for PUCCH and PUSCH repetition”, China Telecom
[3] R4-2106918, “Discussion on phase continuity for PUSCH and PUCCH repetitions ”, Interdigital
[4] R4-2107273, “on phase continuty for multiple transmissions”, Huawei, HiSilicon
[5] R4-2107366, “Phase continuity over the gap in tx”, Qualcomm
[6] R4-2104702, “UE configuration for enhanced Joint Channel Estimation in TDD”, Sony