## Slide 1: WF on coexistence with other services
Ericsson (moderator)
3GPP TSG-RAN WG4 Meeting #98-bis-e
Electronic meeting, 12 – 20 April 2021
R4-2105421

## Slide 2: Background
This WF contains
agreements made regarding coexistence with RAS and DTV
possible items for further study at subsequent meetings
the agreements made at this meeting should be captured in the TR 38.860 “Study on extended 600MHz NR band”, companies invited to submit TPs to v0.2.0 of the TR

## Slide 3: Protection of RAS (BS)
For the frequency arrangements B1, B2 and B2a, it is agreed that
no BS spurious emissions limits be specified for protection of RAS;
protection of RAS is up to each Administration

## Slide 4: Protection of DTV (BS)
For the frequency arrangements B1, B2 and B2a it is agreed that
no specific limits to be specified for protection of DTV, rely on the general BS spurious emissions limits
Items for further study, e.g.
discuss the frequency separation between the lower edge of an NR band (DL) and DTV considered feasible for coexistence for each frequency arrangement, e.g.
  consider/reuse the FCC frequency separation (7 MHz) for protection of Broadcast
  or if this should be left for Administrations

## Slide 5: Protection from DTV (UE)
No agreement on introduction of blocking requirement(s) for protection from DTV for either B1 or B2
Items for further study, e.g.
rejection achievable in the DL at a specific frequency separation between the NR band and DTV for the frequency arrangements
  without discussing any specific blocking requirement for protection from DTV
UE blocking by DTV Channel 36 in the US, may impair the possibility to reuse some 600MHz extended filters options for B71/n71
need for protection from DTV below 608 MHz

## Slide 6: References
R4-2105479, ” Email discussion summary for [98-bis-e][142] FS_NR_600MHz_ext”, Moderator (Ericsson)
R4-2105423, TR 38.860 v0.2.0, ”Study on extended 600MHz NR band”