## Slide 1: WF on frequency arrangements for further study and corresponding UE filter configurations
Qualcomm Incorporated, Ericsson, Huawei, SparkNZ
R4-2105422
3GPP TSG-RAN WG4 #98bis-e
April 12th ‒ 20th, 2021
Electronic Meeting

## Slide 2: Filter configuration for B1
683 – 703 MHz UL / 612 – 652 MHz DL. Tx/Rx separation gap is 11MHz
  Full-band filter is preferred by most companies
  Full band filter is judged to be technically feasible [1], [2] but the blocking to DTV channel 36 may be worse than that of Band 71
Split-band preferred by some companies
  Interested companies are invited to provide technical evaluation of B1 split filter implementation
WF -> Full band filter for B1 is deemed to be technically feasible with possible degradation for the Rx blocking to Ch36
  A full band filter over the entire frequency range may exhibit higher worst case Tx and Rx insertion loss. However, all 3GPP defined Band n71 requirements (except Rx blocking to Ch36) are expected to be met. The additional insertion loss may also be recovered using more advanced semiconductor processes and design techniques.

## Slide 3: Filter configuration for B2
Split filter (35 MHz + 35 MHz)
  663 – 698 MHz UL / 617 – 652 MHz DL (Band n71 filter) (Dup 1)
  668 – 703 MHz UL / 622 – 657 MHz DL (Dup 2)
  The split filter has been judged to be technical feasible [2], [3]
    Both filters must be newly designed (cannot reuse n71 filter as-is) [2]
    Some REFSENS degradation may happen for the frequency close to the low edge of Dup 2 Tx [2]
    Degradation of the DL upper 5MHz band protection and blocking performance needs to be accommodated [3]
  It is not precluded to discuss upper channel BW restriction to enable better performance - lower cost/size option with a smaller BW in the upper duplexer
Full band filter expected to be challenging – companies are invited to evaluate feasibility
  Some companies indicated already that full band duplexer with 6 MHz gap may not be feasible with current filter implementation [2]
WF -> Split band (35 MHz + 35 MHz) filter for B2 is deemed to be technically feasible with possible degradation to UE coexistence and blocking at the upper end of the DL band

## Slide 4: Filter configuration for B2a
Option B2a consists of two bands, Band n71 (as-is) and Band nyyy [4]
  Technical evaluation of Band nyyy filter has not been presented, though it is expected to be largely similar to “split filter B2” option with perhaps slightly better performance due to narrower passband
All companies except for one preferred to focus on Option B1 and B2 according to the guidance provided by AWG [5]
  “The two-band approach is not the current priority of AWG”
WF -> Option B2a is deprioritized

## Slide 5: Annex: Optional filter configurations
The following additional filter configurations may also be considered for further evaluation
  B1 (prioritized by AWG)
    Split filter with 35 MHz + 35 MHz
  B2 (prioritized by AWG)
    Split filter with 35 MHz + 30 MHz
    Split filter with 35 MHz + 25 MHz
    Full band filter
  B2a
    Split filter with 35 MHz (Band n71) + 30 MHz (Band nyyy)

## Slide 6: References
[1] R4-2107348, “Filtering for extended 600 MHz band,” Qualcomm Incorporated
[2] R4-2107301, “Feasibility analysis of 600MHz duplexer,” Huawei, HiSilicon
[3] R4-2104817, “Discussion on Extended 600MHz Band Implementation Options,” Skyworks Solutions, Inc.
[4] R4-2104891, “TP on band plan for 600 MHz,” Apple
[5] R4-2105105, “FREQUENCY ARRANGEMENTS FOR IMT IN THE BAND 470 – 703 MHZ,” Reply LS from APT Wireless Group