## Slide 1: Way Forward on maintenance of Direct SCell activation and SCell dormancy
Ericsson, ...
3GPP TSG-RAN WG4 Meeting #98bis-e
Electronic Meeting, April 12 – 20, 2021
R4-2105738
Document for: Approval

## Slide 2: Background
Companies provided contributions in the following areas to RAN4#98bis-e:
  Core requirement maintenance for Direct SCell activation
  Performance requirement maintenance for SCell dormancy
Agreements pertaining to above contributions are captured in the present WF
Further background can be found in R4-2105807 or revision thereof.

## Slide 3: Agreements in RAN4#98bis-e (1/5) Core requirement maintenance – Direct SCell activation
Agreement:
  For branching of delay requirements, the following shall replace condition on measCycleSCell for known SCell in FR1:[Issue 1-1-1, 1-1-2]
  TFirstSSB+ 5ms, if the measurement period is at most [1280]ms,
  TFirstSSB_MAX + Trs + 5ms, if the measurement period is longer than [1280]ms.
  Implemented in draft CR R4-2105739 or revision thereof.

## Slide 4: Agreements in RAN4#98bis-e (2/5) Core requirement maintenance – Direct SCell activation
Agreement:
  For definition of known SCell in FR1, the following shall apply: [Issue 1-1-3]
    The definition of know SCell in NR FR1 shall be based on the same definition in LTE:
      The SCell is known provided the following conditions are met for the Scell:
        During the last 5 seconds before the reception of the direct Scell configuration command:
        the UE has sent a valid measurement report for the Scell being directly activated or directly hibernated, and
        the Scell being directly activated or directly hibernated remains detectable according to the cell identification conditions specified in section 8.3.3.2,
        Scell being directly activated or directly hibernated also remains detectable during the Scell activation delay according to the cell identification conditions specified in section 8.3.3.2
      Otherwise, the Scell is unknown.
    The wording shall be adapted to NR FR1.
    The time during which conditions shall be fulfilled for cell to be considered to be known shall be left within brackets, e.g. [5] seconds.
  Implemented in draft CR R4-2105740 or revision thereof.

## Slide 5: Agreements in RAN4#98bis-e (3/5) Core requirement maintenance – Direct SCell activation
Agreement:
Regarding applicability of delay requirements, the following is to be added to the clause on Direct SCell addition: [Issue 1-2-1]
    “If the RRC reconfiguration message for direct SCell activation also configures PSCell addition or PSCell change, the direct SCell activation delay may be longer than the requirements defined in this clause.
    ”
  Implemented in draft CR R4-2105741 or revision thereof.

## Slide 6: Agreements in RAN4#98bis-e (4/5) Performance requirement maintenance – SCell dormancy
Agreement:
  For definition of Dormant BWP configuration, the following agreement was made: [Issue 2-1-1]
    No need to introduce a new BWP configuration for dormant BWP. Existing BWP configurations can be reused.
Agreement:
  For definition of CORESET for testing of dormancy switching triggered after initial 3 OFDM symbols: [Issue 2-1-3]
    Introduce new CORESET RMC for 15kHz and 30kHz with PDCCH after the first 3 OFDM symbol.
  Implemented in draft CR R4-2106996.

## Slide 7: Agreements in RAN4#98bis-e (5/5) Performance requirement maintenance – SCell dormancy
Agreement:
Regarding whether scheduling or non-scheduling DCI shall be specified in SCell dormancy test cases: [Issue 2-1-2]
  Leave the choice of scheduling/non-scheduling DCI to RAN5.

## Slide 8: For RAN4#99-e
  Companies to confirm value [1280]ms in delay requirement for direct SCell activation of known SCell in FR1
  Companies to confirm value [5]s in definition of known cell for direct SCell activation in FR1