## Slide 1: 3GPP TSG-RAN WG4 Meeting #98-bis-e Electronic Meeting, 12 – 20 April, 2021
Intel
WF on R17 NR MG enhancements – Pre-configured MG
R4-2105791

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
Open after 1st round

## Slide 3: Others
FFS: unified abbreviation of pre-configured measurement gap:
  Option 1: P-MG
  Option 2: Pre-MG
Timeline consideration:
  2nd phase can be started after the group reaches agreements on basic pre-configured MG configuration and (de)activation mechanism for single CC BWP switching case (e.g. from RAN4#100e )

## Slide 4: Using scenarios
Pre-configured MG for SSB measurements shall be configured.
FFS whether the pre-configured MG shall be configured for PRS measurement:
  Option 1. Yes
  Option 2. No
FFS whether the pre-configured MG shall be configured for CSI-RS L3 measurement:
  Option 1. Yes
  Option 2. No

## Slide 5: Using scenarios
Focus on the scenarios with the pre-configured MG for single CC BWP switching scenario.
FFS whether to define pre-configured MG for multiple CC BWP switching scenario for NR-CA case
  Consider this in 2nd stage.
Whether the pre-configured gaps shall be considered as a part of multiple concurrent gap patterns framework
  Consider this in 2nd stage.

## Slide 6: Configuration procedure(1)
Pre-configured MG(s) are configured per UE or per FR
  FFS if pre-configured MGs can be additionally configured per BWP
How pre-configured MGs can be configured:
  The common configuration parameters of pre-configured MG (e.g. MGRP, MGL, etc) which are same as these of Rel16 legacy MG can be configured by the similar way as the Rel16 legacy MGs
  FFS on the specific configuration parameters for the new aspects of pre-configured MG to be introduced,
    One single bit (or flag) per BWP to indicate whether the pre-configured MG is ON or OFF when that BWP becomes active
    Others are not precluded.

## Slide 7: Configuration procedure(2)
FFS whether the pre-configured MG is activated or not after configuration completed
  Option 1: Activated by default
  Option 2: Not activated by default until being activated.
  Option 3 Status of pre-configured MG is not fixed (no default status):
  Option 3a: Whether pre-configured MG activated or not depends on whether reference signal to measure is within the active BWP or not.
  Option 3b: Network signals the status (activated or deactivated) when pre-configured MG is configured
FFS on whether MG configuration can be changed after BWP switching
  Option 1: Yes
  Option 2: No
FFS on relation of pre-configured MG pattern and with the current RRC configured MG
  Opiton 1.
    The already configured P-MGP is transformed into legacy MGP (with same MGL/MGRP) if the UE is configured to measure on any carrier (e.g. inter-RAT) which always need gaps for performing the measurement.
    Network can transform an already configured P-MGP into legacy MGP with same MGL/MGRP or vice versa without deconfiguring the P-MGP
  Others

## Slide 8: Activation/Deactivation procedures
The conditions to activate/de-activate the Pre-configured MG are:
  BWP switching
  For activation decision, MO configured can perform gapless measurement before BWP switching but not after BWP switching. For deactivation decision, MO configured can perform gapwith measurement before BWP switching but can not after BWP switching.
  Other conditions are not precluded
FFS on whether NW can fully control the pre-configured MG being activated/deactivated
FFS on how pre-configured MGs can be activated/deactivated:
  Option 1 Autonomously/implicitly triggered by condition change
  Option1a Autonomously triggered by BWP switching DCI/timer but explicitly directed according to the pre-configured ON/OFF state/bit for the target BWP
  Option 2: If the use case of MG pattern change following BWP switch is considered, to activate/deactivate the pre-configured MG by the network indication
FFS on evaluation on MG activation/deactivation mechanism

## Slide 9: RRM requirements with Pre-configured MGs
FFS on activation/deactivation delay
  Option 1: No separated activation delay for the pre-configured MG activation/deactivation
  Option 2: some transition time (T) shall be included in the pre-configured MG activation/deactivation time.
  Option 2a
    MG deactivation delay of [Y]ms is defined from the DCI of BWP switch is received to the earliest time instant when MG can be aborted.
    MG activation delay of [X]ms is defined from the completion of target BWP activation to the earliest time instant when a MG can be entered.
    No requirements shall be defined for the measurements within the gaps during [Y] and/or [X]ms
  Option 2b The pre-configured delay includes BWP switch delay with additional validation time. The validation time is 20ms.
  Others
FFS on measurement period for the measurements with the pre-configured MGs
FFS on transitions between gapless and gap-based measurement procedures during ongoing measurements
  Option 1:
    RAN4 is to investigate the maximum number of transitions (N1,max) allowed for switching from gapless measurement procedure to gap-based measurement procedure during the ongoing measurement.
    RAN4 is to investigate the maximum number of transitions (N2,max) allowed for switching from gap-based measurement procedure to gapless measurement procedure during the ongoing measurement
  Option2 : No need
FFS on scheduling restriction during pre-configured MGs when not used
  Option 1: If the UE is measuring without pre-configured gaps and no other frequency layer which needs gaps is configured then the UE can be scheduled during the pre-configured gaps while meeting existing scheduling restriction requirements defined in TS 38.133
  Option 1a: Existing scheduling restriction for RRM measurement without MG applies when pre-configured MG is deactivated
FFS on UE behavior after deactivation of pre-configured MG

## Slide 10: Gap patterns for pre-configured MGs
Number of pre-configured MG patterns:
  A single pre-configured MG is considered for the case of non-concurrent MG scenarios.
  FFS if more pre-configured MGs shall be considered for the multiple concurrent MG scenarios
FFS on MG patterns used for the pre-configured MG mechanism
  Option 1: The existing gap patterns (0~23) in Rel16 can be reused for the pre-configured MG.
  Option 2: The existing gap patterns (0~25) in Rel16 can be reused for the pre-configured MG.
Pre-configured MG pattern applicability
  If the gap patterns which can be used as the pre-configured gap are reused from Rel16, the same applicability(per-UE/per-FR) shall follow the rules defined in Rel16 also

## Slide 11: Signalling
RAN4 can send LS to RAN2 for defining the signaling and configuration/reconfiguration procedures when principles/mechanisms of configuration, activation/deactivation, supported patterns etc., for pre-configured MGs are agreed in RAN4.