## Slide 1
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2106098
Electronic Meeting, 12th – 20th April, 2020
Agenda Item: 8.6.3
WF on UE demodulation for FR1 HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-2103876 WF on UE demodulation for FR1 HST, RAN4#98-e

## Slide 3: PDSCH requirements for CA scenarios
  Transmission schemes
    For HST-DPS, considering DPS with both one and two active TCI(s). Reuse the applicability rule between the two DPS schemes from single carrier
  Special slot configuration
    PDSCH is not scheduled on ‘S’ slots under HST-SFN propagation condition for HST CA requirements

## Slide 4: PDSCH requirements for CA scenarios
  SCS configuration and applicability rules for SCS configuration
    Option 1: Do not introduce requirements in HST for FDD 15KHz + TDD 15KHz CA and TDD 15 kHz + TDD 30 kHz CA. If UE supports both FDD 15 kHz + TDD 30 kHz and FDD 15 kHz + FDD 15 kHz CA duplex modes, apply requirements only to the first one (i.e. use the same applicability rule on CA duplex mode for HST CA as CA CQI requirements).
    Option 2: Introduce requirements in HST for FDD 15 kHz + TDD 15 kHz CA and TDD 15 kHz + TDD 30 kHz CA, and the applicability rule between CA scenario with TDD 15 kHz SCS and CA scenario with TDD 30 kHz SCS specified in Rel-16 can be reused
    Option 3: Do not introduce requirements in HST for FDD 15 kHz + TDD 15 kHz CA and TDD 15 kHz + TDD 30 kHz CA, and no applicability rule for FDD 15 kHz + FDD 15 kHz CA, TDD 30 kHz + TDD 30 kHz CA and FDD 15 kHz + TDD 30 kHz CA (i.e. not to reuse CA CQI applicability rule to PDSCH CA normal demodulation requirements)

## Slide 5: PDSCH requirements for CA scenarios
  Applicability rule for HST-SFN joint transmission scheme and DPS transmission scheme
    Option 1: If UE supports demodulationEnhancement-r16, only HST-SFN JT requirements shall apply, otherwise HST-DPS requirements shall apply for CA.
    Option 2: Define applicability rule that UE has passed DPS CA requirements can skip SFN CA requirements
    Option 3: Define two UE capabilities for HST-DPS CA and HST-SFN CA, UE perform the test only when UE supports it. if UE supports both
      Option 3a: Test both schemes
      Option 3b: Test one scheme
        If UE has passed HST-DPS CA tests, HST-SFN CA tests can be skipped
        If UE has passed HST-SFN CA tests, HST-DPS CA tests can be skipped

## Slide 6: PDSCH requirements for CA scenarios
  Network-assisted signalling
    Existing HST network assisted signaling can cover CA scenario
  UE capability signalling
    Option 1: Existing UE capability can cover CA scenario
    Option 2: Define UE capability signaling for UE supporting HST-SFN CA and HST-DPS CA
  Applicability rule between single carrier and CA
    Discuss applicability rule between single carrier and CA later based on the conclusion of applicability rule for HST-SFN joint transmission scheme and DPS transmission scheme.

## Slide 7: PDSCH requirements for CA scenarios
  FFS whether to update the HST-DPS channel model
    FFS on adding path loss and propagation delay for transmitted signal from each RRH.
    FFS on clarification of propagation conditions for SSB, TRS(second TCI state) transmitted from the second nearest RRH
      Option 1: Add clarification on another Doppler frequency for this link comparing to the signal from the nearest RRH.
      Option 2: Add clarification on another Doppler frequency, propagation delay and Rx power comparing to the signal from the nearest RRH.
  FFS whether HST PDSCH CA requirements can be release independent from Rel-15

## Slide 8: Enhanced transmission schemes
  Option 1: Do not define requirements for transmission scheme 2
  Option 2: Continue Evaluation of transmission scheme 2
    Companies are suggested to provide the performance evaluation of transmission scheme 2 (i.e., multi-DCI based transmission scheme) for following cases
      Case 1: Fix the MCS along the track
      Case 2: Vary the MCS along the track
    Note: To vary SNR along the track consider HST-SFN channel model from TS 38.101-4 without normalization, i.e.

## Slide 9: Enhanced transmission schemes
  Reference performance for comparison
    Option 1: mDCI-based transmission vs. HST-SFN joint transmission
    Option 2: mDCI-based transmission vs. HST-DPS
    Other options are not precluded
  Evaluation criteria
    Option 1: Max achievable throughput across all scheduled TB
      Different train locations and SNR points should be analyzed
    Option 2: SNR at 70% @max achievable throughput
    Option 3: Max supported Doppler frequency
    Other options are not precluded