## Slide 1: WF on Demodulation requirement for FR2 HST
Samsung
3GPP TSG-RAN WG4 Meeting #98b-e
Electronic,12th April– 20th April 2021 Agenda Item: 8.7.5
R4-2106102 Document for: Approval

## Slide 2: Background
      Agreed WFs for FR2 HST WI in previous meetings
  R4-2017828, “WF on NR support for HST in FR2”, Samsung. RAN4#97-e meeting
  R4-2103240, “WF on Deployment Scenario and UE RF Requirement for FR2 HST”, Samsung. RAN4#98-e meeting

## Slide 3: Maximum Speed

## Slide 4: Maximum Speed feasibility study and requested RS configuration for Uplink
It is feasible to support maximum speed with 350km for uplink with PTRS or DMRS+PTRS configuration used for frequency offset tracking with 120KHz SCS
Configure PTRS during the PUSCH demodulation test
DMRS+PTRS configuration for PUSCH demodulation requirement with single-tap channel model
  Option 1: 1 DMRS +PTRS (L=1,K=2)
  Option 2: 1+1 DMRS +PTRS (L=1,K=2)
  Option 3: 1+1+1 DMRS+PTRS(L=1, K=2)

## Slide 5: Maximum Speed feasibility study and requested RS configuration for Downlink
Companies' observation on Maximum Speed feasibility, companies can further check until next meeting
  It is feasible to support maximum speed with 350km/h for downlink with TRS (4 symbol interval)for frequency offset tracking under unidirectional RRH deployment with 120KHz SCS
  It is feasible to support maximum speed with 350km/h for downlink with TRS( 4 symbol interval) +SSB for frequency offset tracking under unidirectional and bi-directional RRH deployment with 120KHz SCS
  It is feasible to support maximum speed with 350km/h for downlink with TRS (4 symbol interval)+PTRS (L=1,K=2) for frequency offset tracking under bi-directional RRH deployment with 120KHz SCS
  It is feasible to support maximum speed with 350km/h for downlink with PTRS or DMRS(1+1+1)+PTRS(L=1,K=2) configuration used for frequency offset tracking under single tap propagation conditions with 120KHz SCS
Configure PTRS during the PDSCH demodulation test
RS as baseline for frequency offset tracking to support 350km/h
  Option 1: SSB+TRS
  Option 2:
    SSB+TRS+PTRS for bi-directional deployment
    SSB+TRS for unidirectional deployment
  Other options are not precluded
DMRS configuration for PDSCH demodulation requirement
  Option 1: 1 DMRS
  Option 2: 1+1+1 DMRS

## Slide 6: Maximum Doppler Calculation
Carrier frequency for Doppler frequency calculation
  30GHz

## Slide 7: UE demodulation requirements

## Slide 8: Test Scope
Test scope of DL requirements
  Only define PDSCH demodulation performance requirements in Rel-17 FR HST WI
Requirement for scenario A or B
  Option 1: Define PDSCH demodulation performance requirements only with one deployment scenario (A or B)
  Option 2:Define PDSCH demodulation performance requirements with the worst cases of two scenarios
  Option 3:Define PDSCH demodulation performance requirements with both scenarios if needed
  Consider output of FR2 HST Deployment scenarios discussion whether to cover scenario A and/or B
Requirement for uni-and bi-directional RRH deployment scenarios
  FFS to define both PDSCH demodulation requirements for uni- and bi-directional RRH deployment scenarios
  FFS to define the test applicability rule if both PDSCH demodulation requirements for uni-and bi-directional RRH deployment scenarios are defined
  Consider output of FR2 HST Deployment scenarios discussion whether to cover uni- and/or bi-directional RRH deployment

## Slide 9: Test Scope
Transmission schemes
  No PDSCH requirement with SFN joint transmission scheme in Rel-17 FR2 HST WI
  DPS transmission schemes
    DPS transmission scheme in Uni-directional RRH deployment scenario
      Option 1: scheme 1a
      Option 2: scheme 1b
      Option 3: both scheme 1a and scheme 1b
    DPS transmission scheme in bi-directional RRH deployment scenario
      Option 1: scheme 1a
      Option 2: scheme 1b
      Option 3: both scheme 1a and scheme 1b
  FFS on PDSCH requirements of HST single tap

## Slide 10: Test Setup
SCS and BW
  Option 1: 120KHz with 100MHz
  Option 2: 120KHz with 200MHz
UE frequency error
  FFS on considering the impact of UE frequency error on DL demodulation performance

## Slide 11: Basic simulation assumption
Option 1
Other options are not precluded
Parameter | Value
Maximum Doppler | [9596Hz]
Channel model | [single-tap], [DPS]
CBW/SCS | [200MHz/120kHz]
PDSCH mapping | Type A, start symbol 1, duration 13
DMRS | [1+1+1]
PTRS | KPTRS=2, LPTRS=1
Antenna configuration | [2x2]
MCS | [17]
Test metric | 70% of maximum throughput

## Slide 12: UE demodulation test

## Slide 13: Testability issues for FR2 HST UE
RAN4 to discuss on the impact of the assumption of a static UE and single probe OTA chambers on the FR2 high speed train demodulation test design
  Option 1: Assumption two probes in chamber, as RRM assumption with 2AOA tests
  Option 2: Assume static UE and single Probe. Combine RRM and Demod requirements as a single feature to support HST FR2 operation
  Option 3: Study an approach with taking into account continuous UE movement from RRH to RRH
FFS keep into account the testability of high power devices inside OTA chambers, for the definition of radiated demodulation requirements for FR2 HST

## Slide 14: BS demodulation requirements

## Slide 15: Test Scope
Test scope of UL requirements
  Only define the following BS demodulation performance requirements in Rel-17 FR HST WI
    PUSCH
    UL timing adjustment
    PRACH

## Slide 16: Test Scope
Requirement for scenario A or B
  Option 1: Define PUSCH demodulation requirements based on the worst case scenario
  Option 2: Define PUSCH demodulation requirements only with one deployment scenario (A or B)
  Option 3: Define PUSCH demodulation requirements for both two scenarios if needed
  Consider output of FR2 HST Deployment scenarios discussion whether to cover scenario A and/or B

## Slide 17: Test Scope
Requirement for uni- and bi-directional RRH deployment scenarios
  FFS to define both PUSCH demodulation requirements for uni-and bi-directional RRH deployment scenarios
  FFS to define the test applicability rule if both PUSCH demodulation requirements for uni-and bi-directional RRH deployment scenarios are defined
  Consider output of FR2 HST Deployment scenarios discussion whether to cover uni- and/or bi-directional RRH deployment

## Slide 18: Test Setup for PUSCH requirements
Waveform
  Only CP-OFDM
SCS&BW
  Option 1: 120KHz SCS with 50MHz, 100MHz or 200MHz
  Option 2: 120KHz SCS with 100MHz
  Option 3: 120KHz SCS with 200MHz
Antenna Configuration
  1Tx2Rx Low
Resource mapping type: type B
Length of data symbol
  Option 1: 9
  Option 2: 10
MCS
  Option 1: MCS16
  Option 2: MCS16 and MCS17
  Other options are not precluded

## Slide 19: Test Setup for UL timing adjustment requirement
Test Scenario
  Scenario Y
Simulation Assumption for scenario Y
  Option 1
  Other options are not precluded
Parameter | Value
Channel Model | Stationary UE: AWGN, Moving UE: AWGN
UE speed | 350 km/h
CP length | Normal
A | 1.25 μs
Δω | 1.04 s-1
MCS | 16
CBW | 200MHz
PUSCH resource allocation | 0 to 65 RB for moving UE, 66 to 131 for stationary UE
SRS resource allocation | last symbol in slot #3 in radio frames, CSRS = 33, BSRS =0, for 132 RB

## Slide 20: Test setup for PRACH
PRACH format
  only C2
  Channel
  AWGN
Frequency offset
  Option 1: align the Doppler value with PUSCH
  Option 2: 9722Hz with 350km/h at 30GHz carrier frequency
Test Preamble Configuration for Ncs
  Option 1: Ncs=0
  Option 2: Ncs=69
  Other options are not precluded

## Slide 21: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2104681 | HST FR2 BS demodulation aspects | Ericsson
R4-2105028 | Maximum Supported Speed from Demod perspective for FR2 HST | Samsung
R4-2105029 | View on UE demodulation requirement for Rel-17 FR2 HST | Samsung
R4-2105030 | View on BS demodulation requirement for Rel-17 FR2 HST | Samsung
R4-2106435 | Analysis on max supported speed for HST FR2 demodulation requirements | Intel Corporation
R4-2106436 | View on UE demodulation requirements for HST FR2 | Intel Corporation
R4-2106437 | View on BS demodulation requirements for HST FR2 | Intel Corporation
R4-2106473 | Preliminary observations on FR2 HST UE Demod Performance Test | Qualcomm Incorporated
R4-2106780 | On FR2 HST BS demodulation requirements | Nokia, Nokia Shanghai Bell
R4-2106829 | Discussion on general issues for NR FR2 HST demodulation requirements | Huawei, HiSilicon
R4-2106830 | Discussion on UE demodulation requirements for FR2 HST | Huawei, HiSilicon
R4-2106831 | Discussion on BS demodulation requirements for FR2 HST | Huawei, HiSilicon
R4-2106865 | HST single tap channel profile for unidirectional deployment | Ericsson
R4-2106866 | UE demodulation requirements for HST FR2 | Ericsson
R4-2106916 | On HST FR2 Maximum Supported Speed from Demodulation Perspective | Nokia, Nokia Shanghai Bell

## Slide 22: Reference
[1] R4-2106146, “Email discussion summary for [98-bis-e][322] NR_HST_FR2_Scenarios_Demod”, Samsung