## Slide 1: WF on 5G NR UE Application Layer Data Throughput Performance
Qualcomm
3GPP TSG-RAN4 Meeting #98bis-e
Electronic Meeting, Apr 12th – Apr 20th 2021
Agenda item: 9.5
R4-2106122
Document for: Approval

## Slide 2: Simulation Results Alignment Criteria
Alignment Results Criteria
  Option 1: Absolute throughput span within X% of average throughput across companies at a given SNR.
    Decide X based on simulation results. Possible values of X = [5]% or [10]%.
  Option 2: SNR G±Gspan can be reached for the T% of maximum throughput
    Maximum throughput is derived with TBS corresponding to CQI index 15 with rank 2 for 2Rx/4Rx UE.
    Decide G based on simulation results. Candidate option is G = [2.5] dB.
Additional Criteria
  CQI and RI reporting statistics span to aid with alignment.
  Interested companies can also provide decode success rate.

## Slide 3: Simulation Assumptions - I
RAN4 should only evaluate the physical layer throughput.
Application of reported CQI/PMI/RI
  TE schedules the PDSCH transport block, rank, and precoding slot by slot, according to the reported CQI/PMI/RI.
Test Metric
  Absolute Physical Layer Throughput.

## Slide 4: Simulation Assumptions - II
Throughput calculation
  SS collects ACK, NACK and statDTX from the UE and records the time, elapsed from the beginning of the test. The payload size, received by the UE and acknowledged towards the SS, is determined according to TS38.214 Clause 5.1.3.2, where the MCS index is derived from the coding rate indicated by the reported CQI according to TS38.214 Clause 5.2.2.1, and the number of layers is set according to the reported RI. Throughput can be calculated in the SS by multiplying the payload size with the number of ACKs and dividing the accumulated payload in kilobits by the time in seconds, elapsed from the beginning of the test, being associated to the following ratio: ACK / (ACK+NACK + DTX).

## Slide 5: Simulation Assumptions - III
Receiver Type
  MMSE-IRC receiver, i.e., same as existing CSI reporting tests.
Focus on single-carrier scenario in this SI.

## Slide 6: Requirements Definition
If it is found to be feasible to define requirements for link adaptation (LA) physical layer throughput:
  Set the physical layer throughput requirements:
    Option 1: By multiplying the averaged throughput by Y (%), e.g., Y=95% or 90%.
    Option 2: Use methodology from PDSCH demodulation requirements with fixed RMC (i.e. average of impairments results + X dB margin).
  Whether to update LA throughput requirements in each release can be discussed in Plenary during planning for each release.

## Slide 7: Test Parameters - I
SNR Points for FR1
  Option 1: 0-30 dB
  Option 2: 0:2:20 dB (baseline)
SNR Points for FR2
  0:2:16 dB.

## Slide 8: Test Parameters - II
CSI Reporting
  Aperiodic for both FR1 and FR2.
PMI Codebook
  CodebookSubsetRestriction is set so that all the possible Type-I single panel PMI matrices are allowed.
  If there is large span in simulation results, CodebookSubsetRestriction of 010011 can be considered.

## Slide 9: Test Parameters - III
Channel Model for FR1
  TDLA30-5
  Higher Doppler scenarios can be further discussed in WI phase.
Channel Model for FR2
  TDLA30-35
  TDLD30 channel model can be further discussed in WI phase.

## Slide 10: Test Parameters -IV
Other Parameters are same as below RI tests in 38.101-4:
    FR1 2 RX: Table 6.4.2.1-1 (Test 1) and Table 6.4.2.2-1 (Test 1)
    FR1 4 RX: Table 6.4.3.1-1 (Test 1) and Table 6.4.3.2-1 (Test 1)
    FR2: Table 8.4.2.2-1 (Test 1)

## Slide 11: Simulation Results
Companies are encouraged to provide the following based on simulation assumptions (slides 3-5) and test parameters (slides 6-10):
  For each SNR point:
    Absolute Physical Layer Throughput
    CQI and RI statistics (At least Median CQI and Median RI)
    Interested companies can also submit decode success rate.