## Slide 1
3GPP TSG-RAN WG4 Meeting #98-bis-e R4-2107082
Electronic Meeting, 12 Apr. - 20 Apr., 2021
Agenda Item: 8.9.1
Considerations on study phase conclusions for R17 RLM BFD relaxation
vivo

## Slide 2: Conclusions
On power saving gain:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    With FTP model is considered with DRX of 40 ms, if L1 measurement intervals for RRM are also extended K times
      For FR1 SSB-based RLM/BFD relaxation, at least [3] sources show that the power saving gain is [8.7%] to [16.4%] for K=2, [13%] to [20.5%] for K=4, and [15.1%] to [25.8%] for K=8.
      For FR2 CSI-RS based RLM/BFD relaxation, one source shows that the power saving gain is [15.6%] for K=2, [21.8%] for K=4.
    By extending only RLM/BFD measurement interval without reducing RRM measurement samples within RRM measurement period
      At least 2 sources show minimal or no power saving gain.
      Note: Number of RRM measurement samples within RRM measurement period is up to UE implementations
  Therefore, it is concluded that the beneficial scenarios for R17 RLM BFD relaxation is
    When L1 measurement interval for RLM/BFD/RRM can be extended, i.e. number of samples can be reduced, which means SINR is high enough and mobility is low enough, and
    When FTP traffic or Voip traffic is considered, and
    When DRX cycle length is not longer than [80] ms, and
    It is more beneficial if PDCCH-WUS is configured

## Slide 3: Conclusions
On mobility impact:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    Regarding increased RLF latency, for FR1 SSB-based RLM OOS relaxation,
      with mobility of 3 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8 with 95% probability.
        The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.
      with mobility of 30 km/h, at least 2 sources show that the increased latency is less than 40ms for K=2, less than 120ms for K=4, and less than 280ms for K=8 with 95% probability.
        The increase is less than 2.5% for K=2, less than 7.5% when K=4 and less than 17.5% when K=8, as T310 = 1000ms and N310 = 1.

## Slide 4: Conclusions
On mobility impact:
  Based on simulation results submitted for RAN4#98e and RAN4 #98-bis-e meeting, it can be observed that
    Regarding delta SINR, for FR1 SSB-based RLM OOS relaxation,
      with mobility of 3 km/h, at least [3] sources show that the delta SINR is [1.3] dB to [2]dB for K=2 , [2.6] dB for K=4, [less than 8dB] for K=8.
      with mobility of 30 km/h, at least [3] sources show that the delta SINR is [2.8] dB to [4.6]dB for K=2 , [5.1] to [6.2] dB for K=4, [7.4] to [8.8] dB for K=8.
    Regarding delta SINR, for FR2 CSI-RS-based RLM OOS relaxation,
      with mobility of 3 km/h, at least [1] sources show that the delta SINR is [3.2] dB for K=2 , [3.8] dB for K=4, [4.2] dB for K=8.
      with UE rotation of 5 r/min, at least [1] sources show that the delta SINR is [4.9] dB for K=2.
  Therefore, the feasible scenarios for R17 RLM and BFD relaxation are
    When DRX cycle length is not longer than [80] ms, and
    When SINR is above a proper threshold, and
    Either
      when mobility state is below 30km/h for FR1, or,
      when UE rotation is less than 5 r/min and UE speed is less than 3km/h in FR2.

## Slide 5: Proposals on the work for RAN2
Send LS to RAN2 on above conclusions for the study phase, so as to trigger RAN2 work on the following details.
  Criteria which the UE is allowed to relax the RLM/BM requirements, including both serving cell quality and/or UE mobility criteria
  Criteria/mechanism which UE falls back to normal RLM/BM operation
  Network or UE to determine if the criteria for relaxation is fulfilled
  RRC signaling design

## Slide 6: Proposals on the work for RAN4
In the work phase, RAN4 should continues to work on the following objectives.
  Applicable DRX cycles for relaxation
  The threshold value and/or margins based on further evaluations
  Relaxation factor determination
  Relaxation of BM when not all serving cells in intra-band CA/DC meets relaxation criteria
  Other options, if RAN4 spec impacts are identified, are not precluded.