## Slide 1: WF on Transient period capability
Huawei, HiSilicon, []
R4-2107783
3GPP TSG-RAN WG4 #99-e
May 19 – 27, 2021
Electronic meeting

## Slide 2: Background
In [1], obvious EVM degradation caused by WOLA effect is raised up for -2us tpstart of 7us transient(15kHz), -0.5us tpstart of 2us transient(15kHz) , and minor EVM degradation observed for -0.5us tpstart of 2us transient(30kHz)
Tpstart with -2us and -2.7us(15kHz)
Tpstart with -0.5us and -0.7us(15kHz)
Tpstart with -0.5us and -0.7us(30kHz)

## Slide 3: Tpstart for 2s and 7s transient
Issue 1-1-1: tpstart for 2 s and 7s
Proposals
  Option 1: Adopt the following table:
  Option 2: To remove all the brackets and keep current agreements as proposed in R4-2111355
Recommended WF
  RAN4 to further study the impact on EVM measurement with -0.5 s and -2 s Tpstart adoption for 2 s and 7s transient, following aspects are encouraged to provide in next meeting:
    More comparable measurement input with different power change case, multiple TEs, etc.
Reported transient capability (us) | EVM definition | tpstart (µs) | SCS4
2 |  | [-0.7] | 15kHz or 30kHz5
4 |  | [-1] | 15kHz
7 |  | [-2.7] | 15kHz
NOTE 1: ,,and are defined in Annex F NOTE 2: is the EVM for a symbol right after a transition; is the EVM for a symbol right before a transition NOTE 3: tpstart denotes the start position of the EVM exclusion window as shown in Annex F.4 NOTE 4: SCS denotes the SCS that can be used in the conformance test NOTE 5: 30kHz shall be used in the conformance test unless the UE signals in supportedSubCarrierSpacingUL in FeatureSetPerCC that it only supports 15kHz in the corresponding band |  |  | 
Reported transient capability (us) | EVM definition | tpstart (µs) | SCS4
2 |  | [-0.7] | 15kHz or 30kHz5
4 |  | [-1] | 15kHz
7 |  | [-2.7] | 15kHz

## Slide 4
definition of for 7s UE transient
Issue 1-1-2: A typo on definition of for 7s UE transient period capability?
Proposals
  Option 1: For 7s reported transient period capability, adopt for verification at SCS 15kHz.
  Option 2: Keep current wording as it is:
Recommended WF
  Further check the higher one between for the symbol right after the transient with 7s reported transient
    Take option 1 if
    Take option 2 if is higher

## Slide 5
Reference
[1] R4-2111539, “Transient Period Capability Measurements”, Skyworks
[2] R4-2111355, “CR for TR 38.101-1 on shorter transient_r16”, Huawei, HiSilicon
[3] R4-2108857, “FFT window starting point values for EVM measurements for transient period capability”, Anritsu