## Slide 1: WF on DC_(n)71AA single UL
Skyworks, [MediaTek], […]
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, 19th -27th May 2021
R4-2107805

## Slide 2: Background: 98-bis WF[1] agreements Non-Contiguous NR-CA / EN-DC
WF[1] and CRs [2,3] are a first step start towards simplification, but there’s room for further improvements,
For example, ΔRIBNC test points for NC EN-DC could be further reduced to one pair of entries per band and per uplink (UL) aggressor channel bandwidth (CBW).
WF[1] and CR [2]
38.101-3 Rel-17.1.0

## Slide 3: Background: Further Simplification Opportunity #1
Observation (from P1 [4]): For NC EN-DC/NR-CA:
It may not be necessary to capture all pairs of ΔRIBNC test points. It is sufficient to specify only 1 pair of test points per UL CBW:
  Test Point 1) Specify the Wgap range for which the worst case (highest) ΔRIBNC is reached. This corresponds to the collision of the lowest victim’s CBW which experiences the greatest overlap with the lowest IMD order;
  Test Point 2): Specify the Wgap range for which the best case (lowest) ΔRIBNC is reached,
We also observe that this simplification has an impact on the core requirements text since sub-clause 7.3B.3.0 says “Unless otherwise stated, ΔRIB,c or ΔRIBNC is set to zero”. Implementation of opportunity 1 means this text needs to be modified.
For contiguous EN-DC/NR-CA:
It is sufficient to specify only 1 test point per UL CBW, the one that leads to the worst-case (highest) MSD:
  For each distinct Uplink Aggressor CBW, only specify the worst-case (highest) MSD test point. This corresponds to the collision of the lowest victim’s CBW which experiences the greatest overlap with the lowest IMD order;
38.101-3 Rel-17.1.0
Opportunity #1
Opportunity #1: using the example of DC_2A_n2A , reduction from 25 to 8 ΔRIBNC test points, ie (x3 reduction) by keeping only 1 pair per UL- CBW
38.101-3 Rel-17.1.0
Opportunity #1
Opportunity #1: using the example of DC_(n)5AA: reduction from 7 pairs to 4 pairs of MSD test points, by keeping only 1 worst-case MSD test point / CBW

## Slide 4: Background: Opp. #1 “Lowest victim CBW that leads to the highest MSD”
Illustration of adopting the smallest victim’s CBW that leads to the highest MSD using the DC_(n)71AA BCS2 test point candidates
For BCS 2 DC_(n)71AA, there are three E-UTRA Rx CBW candidates: 5,10,15 MHz CBW.
E-UTRA 5MHz: Test Point A) does not lead to worst case MSD (refer to bar graph)
        Note: the “*” refers to the measured 3.3dB and 5.5dB MSD levels using “small RB allocations” as agreed in WF [1].
E-UTRA 15MHz: Test Point C) leads to the greatest overlap with the lowest IM order but this test point does not lead to the worst case/highest MSD,
E-UTRA 15MHz: Test Point B) corresponds to the minimum victim’s CBW that has the greatest overlap with the lowest IM order and leads to the worst-case/highest MSD. It is sufficient to only adopt this test point.
Test point B) E-UTRA 10MHz CBW should be the RAN4 candidate
Test point A)
Test point B)
Test point C)

## Slide 5: Background: Further Simplification Opportunity #2
Observation: (from P2 [4])
It may not be necessary to capture ΔRIBNC for all mirror cases of swapping NR/LTE as Aggressor/Victim. Keeping ΔRIBNC only for the LTE anchor point should be sufficient since there is little difference in REFSENS levels between LTE and NR for a given CBW.
Opportunity 2 is also limited by core requirements text of sub-clause 7.3B.3.0 that says “Unless otherwise stated, ΔRIB,c or ΔRIBNC is set to zero”. Implementation of opportunity 2 means this text needs to be modified.
Opportunity #2: using the example of DC_3A_n3A , reduction from 44 to 13 ΔRIBNC test points,
by avoiding duplication of mirrored ΔRIBNC test points.
Table 7.3B.3.2-2
Table 7.3B.3.2-1
Table 7.3B.3.2-1 optimization

## Slide 6: WF on intra-band single UL MSD test points
Considering the tight time schedule of RAN4#99-e, we only propose optimization guidelines for the selection of contiguous ENDC single uplink MSD test points.
WF agreement:
For the selection of single UL REFSENS test points for future REL-17 combinations or for REL-17 new BCS requests of a legacy combination, adopt WF [1] agreement with the following clarification:
Intra-Band Contiguous:
For each distinct Uplink Aggressor CBW, only specify the worst-case (highest) MSD test point. This corresponds to the collision of the lowest victim’s CBW which experiences the greatest overlap with the lowest IMD order leading to highest MSD ;
Test points for which the anchor point MSD is less than 0.5 dB do not need to be specified;
Only specify single UL REFSENS test points where NR is the aggressor and LTE is the victim.

## Slide 7: Background on MSD Test Points for DC_(n)71AA
The selection of DC_(n)71AA single Uplink REFSENS test point is based on guidelines slide 6 as illustrated in slide 4.
Three companies provided MSD levels for each of the 4 selected test points [4,5,6].
It is proposed to adopt the average MSD level.
Note that the adoption of this WF’s guidelines leads to only 4 test points to cover three DC_(n)71AA BCSs (0,1,2). Some legacy combinations require up to 7 test points to cover only 1 BCS.
EN-DC configuration / channel allocations /MSD |  |  |  |  |  |  |  |  | 
EN-DC configuration | E-UTRA/NR band | FC (UL) | UL Channel bandwidth | UL allocation (LCRB) | FC (DL) | MediaTek [5] | Qualcomm [6] | Skyworks [4] | Average
 |  | (MHz) | (MHz) |  | (MHz) | (dB) | (dB) | (dB) | (dB)
DC_(n)71AAX | 71 | N/A | 10 | N/A | 642 | 19.7 | 23.9 | 20.3 | 21.3
 | n71 | 673 | 20 | [5 (RBstart = 0)] | 627 |  |  |  | [0]
DC_(n)71AAX | 71 | N/A | 15 | N/A | 639.5 | 5.5 | 7.2 | 3.4 | 5.4
 | n71 | 670.5 | 15 | [5 (RBstart = 0)] | 624.5 |  |  |  | [0]
DC_(n)71AAXX | 71 | 680.5 | 5 | N/A | 639.5 | 7.2 | 9.6 | 3.5 | 6.8
 | n71 | 670.5 | 151 | [5 (RBstart = 2)] | 627 |  |  |  | [0]
DC_(n)71AAXXX | 71 | 680.5 | 5 | N/A | 634.5 | 7.2 | 9.1 | 2.8 | 6.4
 | n71 | 670.5 | 15 | [5 (RBstart = 0) | 624.5 |  |  |  | [0]
NOTE 1:In accordance to BCS1, the NR uplink bandwidth is specified as in this table, but the corresponding NR downlink bandwidth is 5 MHz larger. |  |  |  |  |  |  |  |  | 
NOTE X: Applicable only to BCS 2. |  |  |  |  |  |  |  |  | 
NOTE XX: Applicable only to BCS 1. |  |  |  |  |  |  |  |  | 
NOTE XXX: Applicable to BCS 0. |  |  |  |  |  |  |  |  | 

## Slide 8: WF on DC_(n)71AA Single UL MSD Test Points
EN-DC configuration / channel allocations /MSD |  |  |  |  |  | 
EN-DC configuration | E-UTRA/NR band | FC (UL) (MHz) | UL Channel bandwidth (MHz) | UL allocation (LCRB) | FC (DL) (MHz) | MSD (dB)
DC_(n)71AAX | 71 | N/A | 10 | N/A | 642.0 | [21.3]
 | n71 | 673.0 | 20 | [5 (RBstart = 0)] | 627.0 | [0]
DC_(n)71AAX | 71 | N/A | 15 | N/A | 639.5 | [5.4]
 | n71 | 670.5 | 15 | [5 (RBstart = 0)] | 624.5 | [0]
DC_(n)71AAXX | 71 | 680.5 | 5 | N/A | 639.5 | [6.8]
 | n71 | 670.5 | 151 | [5 (RBstart = 2)] | 627.0 | [0]
DC_(n)71AAXXX | 71 | 680.5 | 5 | N/A | 634.5 | [6.4]
 | n71 | 670.5 | 15 | [5 (RBstart = 0) | 624.5 | [0]
NOTE 1: In accordance to BCS1, the NR uplink bandwidth is specified as in this table, but the corresponding NR downlink bandwidth is 5 MHz larger. NOTE X: Applicable only to BCS 2. NOTE XX: Applicable only to BCS 1. NOTE XXX: Applicable to BCS 0. |  |  |  |  |  | 
Agreement:
Based on the proposed guidelines and the MSD proposals in [4,5,6], adopt the following single uplink MSD test points for DC_(n)71AA in CR [7].

## Slide 9: REFERENCES
[1] R4-2105338, WF on single UL intra-band ENDC REFSENS Exceptions, 3GPP TSG-RAN WG4 #98bis-e, Electronic Meeting, Apr. 12-Apr. 20, 2021, Skyworks Solutions Inc., T-Mobile USA, CHHTL.
[2] R4-2111520, CR for 38.101-1-h10: Corrections to intra-band non-contiguous CA REFSENS, 3GPP TSG-RAN WG4 #99-e, Electronic Meeting, 19th-27th May 2021, Skyworks Solutions Inc., T-Mobile USA
[3] R4-2111522, CR for 38.101-3-g70: Corrections to intra-band non-contiguous EN-DC REFSENS, 3GPP TSG-RAN WG4 #99-e, Electronic Meeting, 19th-27th May 2021, Skyworks Solutions Inc., T-Mobile USA
[4] R4-2107626, Intra-Band Single Uplink REFSENS Simplification, 3GPP TSG-RAN WG4 #99-e, Electronic Meeting, 19th-27th May 2021, Skyworks Solutions Inc.
[5] R4-2109630, MSD for DC_(n)71AA BCS2, 3GPP TSG-RAN WG4 #99-e, Electronic Meeting, 19th-27th May 2021, MediaTek Inc.
[6] R4-2107642, Qualcomm’s MSD proposal presented in Rd1Sum [99e][116] NR_Baskets_P1, 3GPP TSG-RAN WG4 #99-e, Electronic Meeting, 19th-27th May 2021, Skyworks Solutions Inc.
[7] R4-2111488, Draft CR for 38.101-3: Introduction of DC_(n)71AA_BCS2, 3GPP TSG-RAN WG4 #99-e, Electronic Meeting, 19th-27th May 2021, T-Mobile USA, Skyworks Solutions Inc.

## Slide 10
Thanks!