## Slide 1: WF on REFSENS for Asymmetric Uplink Downlink
Huawei, HiSilicon, Skyworks […]
3GPP TSG-RAN WG4 Meeting #99-e R4-2107819 Electronic Meeting, 19– 27 May, 2021

## Slide 2: Status summary for 1st round discussion
 | Status summary
Sub-topic 1-1: REFSENS for Asymmetric Uplink Downlink | Status: Based on 1st round discussion, companies’ view is still diverse Option 1: Skyworks, MediaTek Option 2: Huawei, ZTE Option 3 (“best case” option): Qualcomm Recommendations for 2nd round: further discussion on the options above and capture the agreements in WF1.

## Slide 3: WF for Asymmetric Uplink Downlink
  Agreements
    To add a note in Table 5.3.5-1 to state that UE channel bandwidth is applicable only to downlink
    To add a new entry in "Table 5.3.6-1: FDD asymmetric UL and DL channel bandwidth combinations"
    To include the word “maximum” deviation definition to ΔFTX-RX
    For REFSENS the location of the TX channel BW in relation to the RX channel BW should be specified
  FFS on UL location with asymmetric Uplink Downlink
    Option 1: Middle case; keep existing duplex offset between center of RX and TX channel BWs
    Option 2: Best case; UL BW furthest from DL to align with 1UL/2DLCA

## Slide 4: Reference
R4-2110657 On asymmetric Uplink /Downlink scenarios Huawei, HiSilicon
R4-2111471 35MHz and 45MHz REFSENS Qualcomm Incorporated
R4-2111530 Remaining n8 n71 Asymmetric Uplink Downlink Requirements Skyworks Solutions Inc.