## Slide 1: WF on applicability and rules for simultaneous RxTx
Huawei, HiSilicon
R4-2107841
3GPP TSG-RAN WG4 #99-e
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
The following issues related to principles for simultaneous Rx/Tx capability have been discussed in RAN4#99-e meeting
    Issue 1-1: Applicability of simultaneous Rx/Tx capability for similar band combination
    Issue 1-2: Rules to decide simultaneous Rx/Tx capability for a band combination

## Slide 3: WF
Issue 1-1-1: Same simultaneous Rx/Tx capability can be applied for the corresponding band combination among NR CA, NR DC and NR EN-DC
Recommended WF
  Further check if same simultaneous Rx/Tx capability can be applied, also consider the discussion in WF on simultaneous Rx/Tx for synchronous /asynchronous NR-DC
  Same simultaneous Rx/Tx capability can be applied for the corresponding band combination among NR CA, NR DC and NR EN-DC

## Slide 4: WF
Issue 1-2-1: Simultaneous Rx/Tx capability for FR1+FR1 FDD-TDD band combination
Options
  Option 1: Mandatory support by default unless the specific problem is identified when specifying the specific combinations in the basket WID. To make sure the potential problem will not be missed check, case-by-case study can be applied if the frequency separation between the FDD band and the TDD band of the combination is smaller than a threshold or the frequencies are multiples of each other(IM/harmonics products from a band fall in the other band). Otherwise, the mandatory simultaneous Rx/Tx capability is applied without additional discussion.
  Option 2: Mandatory support. MSD requirements shall be defined for the combinations which have REFSENS degradation caused by IMD or harmonics
  Option 3: use MSD value or the harmonic / IMD order as the condition to choose band combinations for further discussion of the simultaneous RxTx
  Option 4: Discuss whether or not CA operation is workable in the case of simultaneous Rx/Tx capability is not supported for FR1+FR1 FDD-TDD CA band combination.
Recommended WF
  FFS (further views to be captured in 2nd round summary)

## Slide 5: WF
Issue 1-2-2: Simultaneous Rx/Tx capability for FR1+FR2 FDD-TDD band combination
Agreement
  The capability shall be mandatory if FR1 FDD band (<4GHz) is aggregated with FR2 TDD bands

## Slide 6: WF
Issue 1-2-3: Simultaneous Rx/Tx capability for FR1+FR2 TDD-TDD band combination
Options
  Option 1: Mandatory support
  Option 2: study case by case
Recommend WF
  Further discuss if mandatory support is acceptable with limitation that FR1 with the existing frequency range, i.e. 410 MHz – 7125 MHz.

## Slide 7: WF
Issue 1-2-4: Simultaneous Rx/Tx capability for FR2+FR2 TDD-TDD band combination
Options
  Option 1: discuss whether or not simultaneous Rx/Tx is feasible for this scenario
  Option 2: study case by case
Recommended WF
  Further discuss whether it is a feasible scenario based on available FR2 inter-band combinations

## Slide 8
Reference
[1] R4-2107944, Email discussion summary for [99-e][134] Simultaneous_RxTx