## Slide 1: WF on phase continuity and power consistency for PUCCH and PUSCH repetition
Huawei, HiSilicon, []
R4-2107881
3GPP TSG-RAN WG4 #99-e
May 19 – 27, 2021
Electronic meeting

## Slide 2: WF1: Non-zero un-scheduled gap in-between repetitions
To maintain phase continuity and power consistency across the PUSCH transmissions or PUCCH repetitions, the value of un-scheduled symbols in-between the repetitions up to 13OS is feasible (with some TBD phase tolerance):
  Whether maximum X can be 14OS or 1ms for different SCS FFS
  Further study if new RF requirements for UE during the gap are needed
For transmit power on the gap symbols that less than or equal to 1ms, RAN4 down select solution from following options:
  Option 1: define new transmit off power for gap symbols less than or equal to 1ms explicitly for Rel-17 coverage enhancement case
  Option 2: RAN4 do not introduce new transmit off power
  Option 3: The existing OFF power requirement apply to the un-scheduled gap

## Slide 3: WF2: Non-zero un-scheduled gap with other uplink transmissions
Scenario 1: if the other scheduled signals/channels during the non-zero gap have the same settings in antenna port, occupied PRBs and UL power than the repeated transmission signals/channels
  Whether it is beneficial to define a Guard period for scenario 1:
    Option 1: In the case of different channel in between two repetitions, a guard period before returning to the repetitions is defined. Length of guard period is Y is FFS but shall not exceed 2 symbols.
    Option 2: FFS. It is not clear why guard period can help make the phase aligned with before transmission.
Scenario 2: If the other scheduled signals/channels during the non-zero gap have the different settings in antenna port, occupied PRBs or UL power than the repeated transmission signals/channels
  Option 1: a guard period before returning to the repetitions is defined. Guard allows also different RBs and power levels for the other channels as agreed to be studied in the previous WF. Length of guard period is Y is FFS but shall not exceed 2 symbols.
  Option 2: Phase continuity and power consistency cannot be guaranteed.
  Option 3: Further investigation is needed
    If the phase discontinuity for non-zero gap with other uplink transmission is within such tolerance value, this case can be supported.

## Slide 4: WF3: TA adjustment impact on phase continuity
For RAN1 Question 1 on TPMI change and Question 2 on TA impact: there are transmission timing errors associated with TA adjustment and UE uplink timing autonomous adjustments. Transmission timing errors cause the phase change.
  For network commanded TA adjustments:
    It is known by both gNB side and UE side.
    FFS how to handle the transmission timing error in TA inaccuracy.
  For UE autonomous adjustments:
    FFS whether the autonomous adjustments can be handled by UE or BS and how to handle.

## Slide 5: WF4: Simulation assumption for the tolerance of phase continuity and amplitude consistency(1)
Both reference and compared cases shall include:
  RF impairment modelling:
    CFO: 0.1ppm, with one of the following cases
      Case1: the same frequency error cross repetition transmission
      Case2: the different frequency error across repetition transmission
Reference case shall include:
  No explicitly modelled Phase offset
  No Amplitude impairments - should consider relative power tolerance from existing specs
Compared case shall include:
  Explicit Phase offset:
    Option 1: Gaussian, std deviation (10°, 20°, 30°, 40°, 50°)
    Option 2: uniform distribution
      [-0°,0°], ~, [-90°,90°] for BPSK
      [-0°,0°], ~, [-40°,40°] for QPSK
      [-0°,0°], ~, [-10°,10°] for 16QAM
    Option 3: fixed values (10°, 20°, 30°, 40°, 50°,60°)
    Other option not precluded
  Whether Phase noise, FFS
  Explicit Amplitude offset:
    Option 1: fixed values : 0:0.5:2dB
    Option 2: ±0.7dB as the relative power tolerance from existing specs
    Other options not precluded
RAN4 to decide on the metric of the simulation, following option can be considered:
  Option 1: relative SNR gain due to JCE with phase discontinuity tolerance and amplitude inconsistency tolerance
  Option 2: TP gain due to JCE with phase discontinuity tolerance and amplitude inconsistency tolerance

## Slide 6: WF4: Simulation assumption for the tolerance of phase continuity and amplitude consistency(2)
Following assumption for PUSCH is initially aligned, encourage to down select if more than 1 configuration in one item
Parameter | Simulation assumption
Frequency and SCS | TDD FR1：4GHz and 30kHz, TDD FR2: 28GHz and 120kHz， FDD：700MHz and 15kHz
Bandwidth | 100MHz (TDD)，20MHz(FDD)
PUSCH duration | 14OS
Payload | 4PRB, and/or 15RB
waveform | CP-OFDM and/or DFT-s-OFDM
Channel model for link-level simulation | FR1: TDL-C (NLoS), 30 ns or 300 ns delay spread, medium correlation FR2: TDL-A (NLoS), 30 ns delay spread, medium correlation
UE velocity | 3, or [30] km/h, or 120km/h for FDD
Frequency hopping | With or without frequency hopping
HARQ | No HARQ

## Slide 7: WF4: Simulation assumption for the tolerance of phase continuity and amplitude consistency(2)
Assumptions for PUSCH repetition need further alignment
Parameter | C1 | c2 | c3 | c4
Frame structure for TDD | For TDD: DDDDDDDSUU (S: 6D:4G:4U) | TDD, with 1 UL slot or 2 consecutive UL slots |  | DDDSUDDSUU (S: 10D:2G:2U) for 4GHz
MCS | 3(251/1024) | MCS 4 | QPSK, 16QAM | MCS 4/MCS 2
Number of antenna elements for BS | 1Rx |  | 2Rx at BS | 4Rx
Antenna configuration | 1x1 Low | 1T4R, 1T2R for FR2 | 1Tx at UE | 1Tx
Repetitions for joint channel estimation(available S or U) | TDD：2,3 FDD：2,4,8 | Up to 7 (actual) repetitions (i.e. 8 total transmissions), no re-transmissions |  FDD: 8, 16, 32 for PUSCH, 8 for PUCCH  TDD: 2 for PUSCH and PUCCH | 2 repetitions with JCE
PUSCH mapping type | Type A(Normal cyclic prefix, S=0,L=14) Type B(Repetitions for joint channel estimation TDD：1,2,3, FDD：1,2,4,8; Normal cyclic prefix, S=0,L=7) |  |  | 
DMRS configuration | Type 1 single-symbol DM-RS l0=2 dmrs-AdditionalPosition= pos0 | 2 DMRS symbols per slot | DMRS type 1 with single-symbol front-loaded, no additional DMRS | Type I, 2 DMRS symbol (one front- loaded and one additional), no multiplexing data

## Slide 8: WF4: Simulation assumption for the tolerance of phase continuity and amplitude consistency(3)
Assumptions for PUCCH repetition need further alignment
Parameter | C1 | c2 | c3
PUCCH format | Format 3: 11 bits UCI | format 1 | PUCCH format 3 with 11 bit payload
BLER | DTX to ACK probability: 1%. NACK to ACK probability: 0.1%. ACK missed detection probability: 1%. |  | 
DMRS configuration | No additional DM-RS (3,10) |  | 4 DMRS symbols per slot
SCS | 30kHz (TDD), 15kHz (FDD) |  | 30kHz (TDD), 15kHz (FDD)， 120kHz FR2
Repetitions for joint channel estimation(available S or U) | TDD：2,3 FDD：2,4,8 |  | Up to 7 repetitions (i.e. 8 total transmissions)
PUCCH duration | 14 OS | 14 OFDM symbols | 14 symbol PUCCH format 3 with 1 PRB
Number of PRBs | 1 PRB |  | 

## Slide 9: WF5: DL slot(s) in-between repetition
  RAN4 further study on the feasibility of phase continuity when there is DL slot(s) in-between repetitions

## Slide 10: Reference
[1] R4-2108800, “Phase continuity with the other channels in the gap”, Qualcomm
[2] R4-2109012, “Views on phase continuity and power consistency for PUSCH and PUCCH repetition”, Sony
[3] R4-2109263, “Further discussion on phase continuity for LS reply”, Interdigital
[4] R4-2109581, “On phase continuity and power consistency for PUCCH and PUSCH ”, China Telecom
[5] R4-2109743, “Phase continuity and power consistency for PUSCH and PUCCH repetition”, Nokia
[6] R4-2110611, “Discussion on reply LS on NR coverage enhancement”, ZTE
[7] R4-2110612, Discussion on phase discontinuity and power inconsistency tolerance across different repetitions, ZTE
[8] R4-2111156, Further analysis on PUSCH/PUCCH repetition impacts, MediaTek Inc.
[9] R4-2111194, Reply LS to RAN1 latest question on phase discontinuity, Ericsson
[10] R4-2111195, Simulation assumption for phase tolerance for PUSCH PUCCH repetition, Ericsson
[11] R4-2111385, on phase continuty for multiple transmissions, Huawei, HiSilicon
[12] R4-2111386, simulation assumption for phase tolerance Cov_enh, Huawei, HiSilicon
[13] R4-2109743 Phase continuity and power consistency for PUSCH and PUCCH repetition, Nokia, Nokia Shanghai Bell