## Slide 1: WF on NR-U maintenance-related topics
Qualcomm Incorporated
R4-2107980
3GPP TSG-RAN WG4 #99-e
May 19th ‒ 27th, 2021
Electronic Meeting

## Slide 2: Intra-cell guardband for wideband operation
Agreement
  For DL, UE requirements apply when zero-width guard bands are configured and all RB sets within the channel are scheduled and available for DL transmission at the gNB
  For UL
    RAN4 only defines UE RF requirements in Rel-16 for contiguous RB-sets in the UL
    Requirements apply with nominal intra-cell guard bands (Table 5.3.3-2) on the edges of RB-sets transmitted inside the channel for those RB-sets adjacent to a non-transmitted RB-set
    Requirements apply with nominal intra-cell guard bands configured in between adjacent RB-sets to be transmitted, but the RB’s within these guard bands are scheduled to be transmitted.

## Slide 3: Other agreements
NOTE 14: This band is applicable in the USA only subject to FCC Report and Order FCC 20-51
  This note shall be modified to be more general since Band n96 is becoming available in other countries.
The NR-U Rx requirements for maximum input level and spurious emissions shall be added to the specifications.