## Slide 1: WF on NR MIMO OTA
vivo, CAICT
3GPP TSG-RAN WG4 Meeting #99-e R4-2108085
Electronic Meeting, May 19-27, 2021
Agenda item: 9.1.1
Document for: Approval

## Slide 2: Channel model
FR1 BS beam selection for channel modelling
  Update the rule for beam selection:
    For 4x4 MIMO OTA, two strongest transmitting beams from a pre-defined beam grid are selected for each FR1 channel model. These beams should have different azimuth directions and can provide the highest receive power for UE.
  Define the beam directions for each channel model in the spec.
    For CDL-C UMa, the beam directions are:
      Beam 1: Azimuth: -7.27°, Elevation:-10°
      Beam 2: Azimuth: -21.82°, Elevation:-10°
    For CDL-C UMi, the beam direction is :
      Beam 1: Azimuth: -7.27°, Elevation:-10°
FR2 BS antenna element
  For BS antenna element polarization for FR2, use  polarized antenna model with 45˚ slant angle.

## Slide 3: Test Method
FR2 blocking issue
  Adopt the improved three-step approach as defined in R4-21110843 (Two additional test points are required)
  Further check whether FR2 blocking issue can be properly quantified by the above approach and make decisions on August RAN4 meeting
Positioning ambiguities
  Without re-positioning approach: The turntable implementing the rotation in q shall match the intended DUT q for P0 Orientation 1 :
  re-positioning approach: The relative orientation between the DUT and the probes for P0 Orientation 2 shall be the same the relative orientation between DUT and probes as for P0 Orientation 1

## Slide 4: Channel model validation
Update the FR1 power validation frequency
  Stick to sub-bands grouping approach, select the proposed band in Table 1 for power validation.
  The TP to capture the new center frequency for FR1 power validation is agreed in [R4-2108615].
gNB Beams Usage Criteria for Channel model validation
  Keep both beam specific and beam simultaneous approach for validation procedure in the TR at this stage.
  Further down selection may be needed after we make decision on how to define the pass/fail limit of channel model validation.
Reference curve for Channel model validation
  Reference figure for FR2 PSP
    Choose theoretical PAS as reference

## Slide 5: FR1 Channel model validation
Reference curve for FR1 CDL-C Uma and UMi
  Framework on alignment of reference channel model curves
    Option 1: CE vendors provide a harmonized version
    Option 2: CE vendors provide individual results, averaging approach can be considered to generate the reference curve
  Comparison of CM reference curves for FR1 from the three companies (KS, Spirent, CMCC) are presented in Annex A of R4-2108619.
  The reference curves of CDL-C UMa should be stabilized and decided in Aug. meeting, a check point for offline alignment among companies before August is encouraged. (V/H should be decided )
  reference channel model curves for FR1
    Spatial correlation approach used for validation purpose
      both beam specific and beam simultaneous should be provided for alignment purpose
      Select beam simultaneous approach to generate a new reference curve based on the method used in R4-2108753

## Slide 6: Framework on perf. requirement
FR1 Framework on performance requirement
  Framework on FR1 MIMO OTA requirements including a set of guidelines for laboratories alignment activities is agreed in R4-2108617.

## Slide 7: FR2 simulation campaign
Framework
  RAN4 to adopt two-step approach in R4-2110796 to align the simulation and provide the simulation results for FR2 MIMO OTA.
FR2 Simulated activity
  how to emulate the gap between measurement and simulation
    TE/CE vendors are encouraged to provide the variation range for AoA/ZoA, PAS, power, delay, etc. those impacting by 6 probes in the chamber. (Pending on further feedback and input from TE/CE vendors)
  Example variation range of PDP, doppler, etc
    CE/TE vendors to provide the variation range of PDP, doppler, etc, those impacting by 6 probes in addition to the information on PAS
  UE antenna assumptions (only for simulation alignment)
  UE antenna array: two panels 1x4 patches
  UE antenna parameters and Beam forming: Follow TR 38.803
  Polarization alignment: polarization aligned between UE and TE
  CDL realization
    FFS how to realize CDL channel model into simulation

## Slide 8: Next steps
  Further Discuss the pass/fail limit and reference figure of channel model validation
  Further discuss the Maximum downlink RS-EPRE for FR2
  Further discuss FR2 blocking issue
  Further discuss FR2 simulation activity
  Further discuss whether RAN4 should consider the case that more than 18 points can not reach 70%TP for FR2 MIMO OTA