## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e Electronic Meeting, May 19th – 27th, 2021
Huawei, HiSilicon
Way forward on overhead consideration for multiplexing UCI and PTRS on PUSCH
R4-2108503

## Slide 2: Background
The “Total number of bits per slot” and “Total symbols per slot” in the FRC table includes the overhead of CSI part 1, CSI part 2 and PT-RS for the following requirements:
  8.2.3 and 11.2.1.4 Requirements for UCI multiplexed on PUSCH in both TS 38.104 and TS 38.141-1
  11.2.2 Requirements for BS type 2-O with PT-RS configured in both TS 38.104 and TS 38.141-2
It is causing confusion for the FRC of PUSCH

## Slide 3: Agreement
Consider the overhead of UCI for channel bits calculation
  Consider the REs taken up by CSI part 1 and CSI part 2 in the “bits per slot” and “REs per slot” calculation.
    Option 1:
      The FRC should only take into account the REs that are taken up by PUSCH payload data and exclude REs taken up by CSI part 1 and CSI part 2.
      Update the FRC, if required.
      Add a note to explain that “bits per slot” and “REs per slot” does not include the REs taken up by CSI part 1 and CSI part 2.
    Option 2:
      The FRC should take into account all the REs that are taken up by PUSCH, including REs taken up by CSI part 1 and CSI part 2.
      Update the FRC, if required.
      Add a note to explain that “bits per slot” and “REs per slot” does include the REs taken up by CSI part 1 and CSI part 2.
    Option 3: Update FRCs to include two rows for “bits per slot” and “REs per slot” each; one including CSI and one excluding CSI.
    Other options not precluded
Consider the overhead of PT-RS for “bits per slot” and “REs per slot” calculation and update the corresponding FRCs.
    Update FRCs to include two rows for “bits per slot” and “REs per slot” each; one including PT-RS and one excluding PT-RS.
Prepare CRs to update the related FRCs for next meeting as per further discussion