## Slide 1: WF on other RF conducted requirements and power related requirements
CMCC
3GPP TSG-RAN WG4 Meeting # 99-e R4-2108630
Electronic Meeting, May 19-27, 2021

## Slide 2: WF on conducted output power
Wait for the conclusion of class definition before defining DL and UL FR1 output power

## Slide 3: WF on radiated output power
For DL, EIRP accuracy requirement is necessary and further check whether it’s gain accuracy or power accuracy.
For DL, it is approved to simplify directional requirements with the assumption of fixed antenna gain. The details are FFS and further check whether a single measurement direction instead of 5 is sufficient.
For UL, define TRP and EIRP requirements for FR2. The details of output power are FFS and wait for the conclusion of class definition.

## Slide 4: WF on ALC requirements
No dedicated requirements for FR2 ALC.
Certain RF requirements should be met with a reasonable over powered input signal to verify ALC for both FR1 and FR2
The detail of ALC verification is FFS

## Slide 5: WF on frequency stability requirements
The frequency deviation of the output signal with respect to the input signal shall be no more than ±0.01 for both FR1 and FR2.

## Slide 6: WF on EVM requirements
EVM may be declared, or declared from a set of limits or have a single limit.
If there would be a set of limits, the set EVM limits are the same for DL and UL (except for low EVM levels associated with 256QAM).
Whether the same declaration would be made for DL and UL is FFS.
Whether EVM is directly associated to modulation orders is FFS.
256 QAM needs further discussion.

## Slide 7: WF on REFSENSE related requirements
No REFSENSE requirement is need and further discuss whether following requirements are necessary or not.
  define output power level with no input signal during ON period
  minimum input level
  NF

## Slide 8: WF on input IMD requirements
For general IMD requirement, the first interference signal is CW. FFS about the second one, taking into consideration of how to reflect the real field conditions and how to capture any variations over frequency. For the second interference type,
  Option 1: one CW signal that is swept in frequency to reflect frequency variation
  Option 2: modulated signal with the carrier bandwidth to reflect the real field conditions
For co-located and co-existence IMD requirements it is suggested to take E-UTRA repeater spec as the baseline. Baseline here means that the power in the pass band shall not increase with more than 10 dB at the output of the repeater as measured in the centre of the pass band, compared to the level obtained without interfering signals applied. Further check whether the same interference types, interference level and interference frequency offset as in E-UTRA repeater spec are still applicable.

## Slide 9: WF on ACRR requirements
ACRR requirements should be defined for NR repeater and the details are FFS.
Further discuss the interference source assumption for ACRR requirements
  Option 1: nearby interferer source closer to the repeater than donor BS.
  Option 2: interferer source with the same power and same distance as donor BS.

## Slide 10: WF on out of band gain requirements
take E-UTRA repeater spec as the baseline and baseline here means that we need to double check that the levels are robust enough considering following aspects and tighten the levels if needed.
  Amplification of unwanted emissions from co-located equipment outside of the passband
  Amplification and distortion of other operators’ carriers just outside of the passband
  Amplification of unwanted emissions from other equipment inside of the passband
  The impact of amplifying other operators’ carriers if they are inside the passband
For co-location out of band gain requirements, manufacturer shall declare the operating bands with which co-location is possible