## Slide 1: Way Forward for [313]NTN_Soltions_Part2
JIN Yiran
Moderator, Samsung

## Slide 2: Outline
This document provides proposed way forward based on the outcomes of “Email discussion summary for [99e][313] NTN_Solutions_Part2”
See R4-2108700
Recommended WFs in “orange” are those not agreed yet.

## Slide 3: Way Forward - Scenarios
Agree to remove NR/NB-IoT Indoor scenarios.
FR1: 2GHz |  |  | Set 1 |  |  | Set 22 |  |  | HAPS
 |  |  | GEO | LEO 600km | LEO 1200km | GEO | LEO 600km | LEO 1200km | 
NR / NB-IoT | Rural |  | X | X | X | X | X | X | FFS
 | Urban macro |  | X | X | X | X | X | X | FFS
 | Dense Urban |  | X | X | X | X | X | X | FFS
NTN1 | GEO3 | Set 1 | X | X | X | N/A | N/A | N/A | FFS
 | LEO 1200km |  | X | X | X | N/A | N/A | N/A | FFS
 | LEO 600km |  | X | X | X | N/A | N/A | N/A | FFS
 | GEO | Set 22 | N/A | N/A | N/A | X | X | X | FFS
 | LEO 1200km |  | N/A | N/A | N/A | X | X | X | FFS
 | LEO 600km |  | N/A | N/A | N/A | X | X | X | FFS
Note 1: Start with Earth Fixed beam first, Earth Moving Beams could be further discussed Note 2: Use Set 1 satellite antenna as the starting point for co-existence study. Set 2 might be used if any worst case in associate with Set 2 is found. Note 3: GEO and LEO only operate at adjacent channel. Note 4: Use GEO and LEO@600km when TN is victim. |  |  |  |  |  |  |  |  | 

## Slide 4: Way Forward - Interference Table
RAN4 adopts a phase-by-phase approach to conduct co-existence study based on the table below.
The table has been updated based on last RAN4 meeting agreement.
No. | Combination | Aggressor | Victim | Notes | Study Phase
1 | TN with NTN | TN DL | NTN DL |  | Phase 1
2 | TN with NTN | TN UL | NTN UL |  | Phase 1
3 | TN with NTN | NTN DL | TN DL |  | Phase 1
4 | TN with NTN | NTN UL | TN UL |  | Phase 1
5 | TN with NTN | NTN UL | TN DL | Applicable for satellite operating in S band, e.g. coexistence with n34 TDD. | Phase 1
6 | TN with NTN | TN DL | NTN UL | Applicable for satellite operating in S band, e.g. coexistence with n34 TDD. | Phase 1
7 | TN with NTN | TN UL | NTN DL | Applicable for satellite operating in S band, e.g. coexistence with n41 TDD. | Phase 2
8 | TN with NTN | NTN DL | TN UL | Applicable for satellite operating in S band, e.g. coexistence with n41 TDD. | Phase 1
9 | NTN with NTN | NTN DL | NTN DL | LEO-LEO | Phase 2
 |  |  |  | GEO-GEO | Phase 2
 |  |  |  | GEO-LEO@600 or HAPS-HAPS | Phase 2
 |  | NTN UL | NTN UL | LEO-LEO | Phase 2
 |  |  |  | GEO-GEO | Phase 2
 |  |  |  | GEO-LEO@600 or HAPS-HAPS | Phase 2

## Slide 5: Way Forward - Interference Table
Open issues:
Further clarify NTN with NTN scenarios with the agreed bands included in this WID.
Whether to capture the Figure 1, 2 &3 as informative Annex.
Details are all captured in R4-2108645.
Remaining open issue are with [] and will be further discussed.

## Slide 6: Way Forward - NW layout models
Coordinate system:
Option 1: RAN4 to consider the used assumptions in TR 38.811 for 3D global coordinate system as well the curvature of earth formula to calculate the slant distance between the UE and satellite. (Option 1 of R4-2106105)
Option 2: There is no need to consider the curvature of earth for layout, assuming one satellite beam for the simulation. The distances for LEO-600, LEO-1200 and GEO can be assumed as 600km, 1200km and 35786km separately for any point under the 3dB satellite beam. (Option 2 of R4-2106105)
Agreement: Adopt Option 1 for calibration and co-existence study.

## Slide 7: Way Forward - NW layout models
Method to generate TN sites for NTN-TN co-existence studies:
Agreements:
It should not be assumed that all TN networks are transmitting simultaneously in simulation.
Low elevation angle cases should be further considered based on the table below.
Open issues: 4 options are captured in R4-2108645 with [] and will be further discussed.

## Slide 8: Way Forward - NW layout models
Co-existence between NTN and NTN
Recommended WF:
NTN-NTN layouts in R4-2106105 has been agreed as a starting point and square brackets have been removed.
Other new options are not precluded.
Details are all captured in R4-2108645.
Remaining open issue are with [] and will be further discussed.

## Slide 9: Way Forward - Simulation Assumptions
Detailed assumptions have been captured in R4-2108645.
Consensus have been achieved on following items
Item | Agreements
NTN FRF | Follow RAN4#98bis-e agreement as following, 2 phases will be considered for FRF: FRF=1 in phase 1 for simplification; FRF=3 in phase 2 or it is found FRF=1 is too stringent.
Satellite max TX power | Update Set-1 Satellite parameter table with max TX power in dBm. Update TX power for 20MHz BW if it is agreed.
TN BS AAS Antenna | Refer to TR 38.921 pattern.
TN BS non-AAS Antenna | Only Non-AAS antenna can be used for NB-IoT. For non-AAS antennas, refer to the ITU LS reply in R4-2008924 but its vertical coverage should be ~10deg. (and not 30) and the gain should be around 17-18 dBi (not 12). Antenna pattern information need to be explicitly provided.
Number of active NTN UE | 3 in UL and 1 in DL (same with TN)
NTN Performance metric | The average throughput loss and 5%-ile throughput loss should be less than 5%.
Propagation model in TR 38.811 | Companies who contributed to TR 38.811 section 6.6.2 are invited and strongly encouraged to provide information w.r.t. this matter.

## Slide 10: Way Forward - Simulation Assumptions
Satellite max TX power: Agreements as following
The satellite max Tx power can be calculated by the equation as below:
Configuration FR1 S-band | NRB (5MHz BW) | NRB (10MHz BW) | NRB (15MHz BW) | NRB (20MHz BW)
SCS 15 kHz | 25 | 52 | 79 | TBA
SCS 30 kHz | 11 | 24 | 38 | TBA
Satellite orbit |  | GEO |  |  |  | LEO-1200 |  |  |  | LEO-600 |  |  | 
Payload characteristics for DL transmissions |  |  |  |  |  |  |  |  |  |  |  |  | 
Satellite max TX power in dBm | BW | 5MHz | 10MHz | 15MHz | 20MHz | 5MHz | 10MHz | 15MHz | 20MHz | 5MHz | 10MHz | 15MHz | 20MHz
 | SCS 15kHz | 44.53 | 47.71 | 49.53 | TBA | 46.53 | 49.71 | 51.53 | TBA | 40.53 | 43.71 | 45.53 | TBA
 | SCS 30kHz | 43.98 | 47.37 | 49.36 | TBA | 45.98 | 49.37 | 51.36 | TBA | 39.98 | 43.37 | 45.36 | TBA
Following information is to be updated in Set-1 satellite parameters table.
NRB configuration per BandWidth size and SCS:

## Slide 11: Way Forward - Simulation Assumptions
Satellite channel bandwidth (BW): FFS
Option 1: 20MHz (associated with FRF=1)
NTN system noise figure in dB: Further discuss values in the table below.
Satellite | GEO | LEO 600 | LEO 1200
G/T (dB K-1) | 19 | 1.1 | 1.1
G_Rx (dBi) | 51 | 30 | 30
NF (dB) | 7.4 | 4.3 | 4.3
TN Parameters: FFS as attached.

## Slide 12: Way Forward - Simulation Assumptions
TN BS AAS Antenna:
  Option 1: For AAS antennas, refer to the ITU LS reply in R4-2008924.
  Option 2: Adopt the extended BS AAS antenna model for TN in the scope of NTN simulations.
   Agreements: For AAS antennas, refer to TR 38.921 pattern.
Description | Equation
Peak normalized element radiation pattern | 
Peak gain normalized element radiation pattern | 
Sub-array excitation | 
Sub-array radiation pattern | , where
Array excitation | 
Composite array radiation pattern | , where
Description | Equation
Peak normalized element radiation pattern | 
Peak gain normalized element radiation pattern | 
Sub-array excitation | 
Sub-array radiation pattern | 
Array excitation | 
Composite array radiation pattern | 
Option 2

## Slide 13: Way Forward - Simulation Assumptions
TN BS non-AAS Antenna:
  Option 1: For non-AAS antennas, refer to the ITU LS reply in R4-2008924 but its vertical coverage should be ~10deg. (and not 30) and the gain should be around 17-18 dBi (not 12).
  Option 2: RAN4 to refer to TR 36.942 for the BS non-AAS antenna pattern.
  Option 3: Table 2.4.3-1 of R4-2106105
  Note that Table 2.4.3-1 of R4-2106105 defined the antenna element pattern for non-AAS antennas.RAN4 needs to define the antenna pattern for non-AAS BS for simulation.
   Agreement:
  Only Non-AAS antenna can be used for NB-IoT.
  Option 1 agreed and non-AAS antenna pattern information need to be explicitly provided.

## Slide 14: Way Forward - Simulation Assumptions
Deployment of NTN UE: FFS
  Option 1: NTN UE should be randomly generated within the NTN area. And when co-locate with TN network, co-ex study only consider those NTN UE dropped within the TN network. The simulation should follow similar Monte-Carlo approach as for TN simulation assumptions. And further discuss following factors
  Depending on who is the aggressor, and who is the victim, the simulation approach may be different. For generating interference, RAN4 simulations may consider multiple sources, but for measuring interference, RAN4 simulation may use one single destination in different locations.
  The simulation assumptions should consider UEs connecting with higher priority to the network providing higher QoS.
  The simulation assumptions could be further simplified with NTN UEs at the edge of TN network or outside TN network.
  Option 2: Distribute the NTN UEs within the TN network boundaries or centers randomly corresponding to simulation cases.

## Slide 15: Way Forward - Simulation Assumptions
Principles to consider UE numbers: FFS
  RAN4 should consider the number of TN UEs or their respective densities as a function of interference type.
  RAN4 should consider the number of NTN UEs or their respective densities as a function of interference type.
  If TN simulation assumptions are using one single TN UE scheduled approach, NTN simulation assumptions should also use one single NTN UE scheduled approach.
  If TN simulation assumptions are using a density of TN UEs, NTN simulation assumptions should also use a density of NTN UEs.
Number of active NTN UE:
 Agreement: 3 in UL and 1 in DL (same with TN)

## Slide 16: Way Forward - Simulation Assumptions
Indoor/outdoor TN UE: FFS
  Option 1: Assume 80% of TN UEs are outdoor and 20% indoor for TN macro urban and suburban.
  Option 2: 100% Outdoor
   Recommended WF: Adopt Option 2
NTN UL TPC: FFS
  Option 1: Whether to use NTN UL power control or set 23 dBm may depend on the relation between CLx-ile, Path loss and Satellite Rx max Gain.
  Option 2: The CLx-ile value should be adapted for rural, dense urban and indoor scenarios.
  Option 3: RAN4 to reuse the same TN TPC for NTN with SNR target 15dB.
  Recommended WF: Adopt Option 3 for calibration

## Slide 17: Way Forward - Simulation Assumptions
Throughput ~ SNR mapping: FFS
  Option 1: the parameters in tale 5-1 can be reused for the following parameters  , SNIRMIN, and SNIRMAX, but other options are not precluded.
   Recommended WF: Option 1 can be a starting point.
Parameter | DL | UL | Notes
α, attenuation | 0.6 | 0.4 | Represents implementation losses
SNIRMIN, dB | -10 | -10 | Based on QPSK, 1/8 rate (DL) & 1/5 rate (UL)
SNIRMAX, dB | 30 | 22 | Based on 256QAM 0.93(DL) & 64QAM 0.93 (UL)
It’s infeasible to achieve 30dB/22dB DL/UL maximum SNIR for NR NTN, so the following parameters need to be further studied and RAN4 need to check them with RAN1.
 Attenuation factor, representing implementation losses SNIRMIN Minimum SNIR of the code set, dB SNIRMAX Maximum SNIR of the code set, dB

## Slide 18: Way Forward - Simulation Assumptions
Interference impact analysis when TN UL is victim: FFS
  Option 1: Only consider the TN cells hosting NTN UEs (i.e. impact should be checked only for TN UEs inside those TN cells).
  Option 2: Consider all TN cells.
  Option 3 (new): Consider the impact to the whole TN network (19-Cell, 57 Sectors), if NTN UE is dropped within this TN network (19-cell, 57 sectors), we consider the impact.
Details are all captured in R4-2108645.
Remaining open issue are with [] and will be further discussed.

## Slide 19: Way Forward - HAPS
Agreed on HAPS UE NF=9dB.
HAPS UE UL TPC: FFS
  Use the following parameters to set the UE’s UL transmit power in the agreed UL power control model:
    Transmission bandwidth will be further revised to align with the conclusion on uplink scheduled bandwidth and uplink UE number in next page.
UL power control parameter | TN | HAPS
Pmax (dBm) | 23 | 23
Rmin (dB) | -54 | -54
γ | 1 | 1
X, transmission bandwidth (MHz) | [2.88] | [0.36]
Y, BS noise figure (dB) | 5 | 5
Layout between HAPS and TN: FFS

## Slide 20: Way Forward - HAPS
Antenna parameters: FFS
Element gain | 5.5 dBi
Loss | 2.0 dB
Element HPBW horizontal/vertical | for both H/V
Tx power per antenna panel | 43 dBm
HAPS Platform e.i.r.p./cell | 
HAPS Platform e.i.r.p. Spectral Density/cell | 
Element gain | 5.5 dBi
Loss | 2.0 dB
Element HPBW horizontal/vertical | 
Tx power per antenna panel | 43 dBm
HAPS Platform e.i.r.p./cell | 
HAPS Platform e.i.r.p. Spectral Density/cell | 
Option 1
Option 2
Number of cells | 7
Antenna array configuration (row x column) | 2 x 2 for 1st layer cell 4 x 2 for 2nd layer cell
Antenna polarization | Linear ±45°
Element gain | [7.8 dBi]
Element HPBW horizontal/vertical | 65° for both H/V
Element front-to-back ratio horizontal/vertical | 30 dB for both H/V
Element spacing horizontal/vertical | 0.7 wavelength for both H/V
Antenna panel tilt (from the horizon) | 90° for 1st layer cell 23° for 2nd layer cell
EIPR/cell | 56.8 dBm (1st layer cell), 59.8 dBm (2nd layer cell)
EIRP spectral density/cell | 43.8 dBm/MHz (1st layer cell), 46.8 dBm/MHz (2nd layer cell)
Tx power per antenna panel | 43 dBm
Noise figure | 5 dB
Indoor UE percentage | 0%
Coverage area (7 cells combined) | A 100 Km radius circular area centered by the serving HAPS
UE distribution | Uniformly distributed in the coverage area

## Slide 21: Way Forward - HAPS
Details are all captured in R4-2108646.
Remaining open issue are with [] and will be further discussed.
Uplink scheduled bandwidth: FFS
  Option 1:
  For the HAPS network, UL scheduled bandwidth is 2 RBs per UE and 10 UEs are scheduled per cell. Scheduled UE resources are randomly distributed across the bandwidth.
  For the TN network, UL scheduled bandwidth is 16 RBs per UE and 6 UEs are scheduled per cell. Scheduled UE resources are randomly distributed across the bandwidth.
  Option 2:
  For the HAPS network, 3 or 10
  For the TN network, 3UEs are usually assumed for simultaneous transmission

## Slide 22: Way Forward - Calibration
Agreement:
Develop tables (R4-2108721) to calibrate following values for TN, NTN and HAPS respectively.
TN: DL SINR cdf , the UE Tx cdf and the UL SINR cdf
NTN: DL SINR cdf , the UE Tx cdf and the UL SINR cdf
HAPS: DL SINR cdf , the UE Tx cdf and the UL SINR cdf
Conduct the calibration during and after this meeting.
Finalize the calibration by RAN4#100e.

## Slide 23: Way Forward - Work plan
Micro work plan for calibration and co-existence has been agreed.
~ August, 2021: conduct offline discussion and finalize calibration before the RAN4 meeting in August.
2021 Q3：collect results for phase 1 scenarios, and draw conclusion for phase 1 scenarios with ACIR as output.
2021 Q4: collect results for phase 2 scenarios, draw conclusion for NTN co-existence study with ACIR as output.

## Slide 24: Appendix

## Slide 25: Reference
[1] R4-2108700, “Email discussion summary for [99-e][313] NTN_Solutions_Part2”, Samsung
[2] R4-2108645, “Simulation assumptions for NTN co-existence study ”, Samsung, CATT
[3] R4-2108646, “Simulation assumptions for HAPS co-existence study ”, Nokia
[4] R4-2108721 , “Template for NTN co-existence calibration results collection ”, Samsung

## Slide 26: Contribution list in RAN4 #99s-e
TDoc Number | Title | Company
R4-2109118 | Updated simulation assumptions for NTN co-existence | CATT
R4-2109119 | Comparison of co-existence performance w/w.o. consideration on earthe curvature | CATT
R4-2109544 | Proposed simulation assumptions for NTN co-existence study | Samsung
R4-2109645 | On simplification of TN UL --> NTN UL simulation | CATT
R4-2110119 | NTN Simulations assumptions | Ericsson
R4-2110121 | NTN - simulation results for alignment | Ericsson
R4-2110193 | Preminary simulation result for coexistence study on NR to support non-terrestrial networks | Xiaomi
R4-2110412 | Further discussion on NTN simulation assumptions | Huawei, HiSilicon
R4-2110689 | HAPS simulation assumptions for coexistence study | Nokia, Nokia Shanghai Bell
R4-2110690 | HAPS adjacent channel coexistence simulation results | Nokia, Nokia Shanghai Bell
R4-2110799 | Simulation scenarios and assumptions for NTN co-existence | Qualcomm Incorporated
R4-2110800 | HAPS coexistence simulation assumptions | Qualcomm Incorporated
R4-2111423 | Reference Deployment Scenario for NTN MSS S-Band | THALES
R4-2111462 | On the S-band NTN Scenarios and Parameters for Coexistence Study | THALES
R4-2108463* | Preliminary simulation result for discussion and calibration | Samsung
*Late document, not treated