## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e R4-2108647 Electronic Meeting, May. 19 – 27, 2021
CATT…
WF on NTN RF aspects

## Slide 2: Frequency error
RAN4#98-bis-e agreement: The mean value of basic measurements of UE modulated carrier frequency shall be accurate to within ±0.1 ppm observed over a period of 1ms of cumulated measurement intervals compared to the carrier frequency received from the gNB.
Note: The gNB refers to RAN3 NTN architecture.
The additional frequency error introduced by NTN payload, feeder link Doppler compensation error and NTN-Gateway is negligible.

## Slide 3: Network side
Take the RF requirement in 38.104 as the starting point for NTN network side.
Companies are invited to contribute on the following points in RAN4#100e meeting
  The following figure might be used as starting point for further discussion.
  Which [NTN BS] types is the baseline for R17 specification.
    Candidates include, BS type 1-C, BS type 1-H, BS type 1-O. Additional prefix for [NTN BS] type is FFS.
  How to define [NTN BS] classes?
    Further discuss whether to differentiate into different [NTN BS] classes and the criteria. e.g. the type of NTN (HEO, GEO, LEO etc.) and corresponding altitude.
  Whether and how to consider EVM distortion for NTN intra-gNB (refer to RAN3 architecture): FFS

## Slide 4
[1] R4-2108701, Email discussion summary for [99-e][314] NTN_Solutions_Part3, Moderator (CATT)