## Slide 1: Way forward on RRM test configurations
Ericsson
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1808802

## Slide 2: Way forward on RMC sets
RAN4 specifies 4 RMC configurations:
  SCS=15kHz with 10MHz for FDD (below 3GHz in FR1) and 4 SS/PBCH blocks within SS burst,
  SCS=15kHz with 10MHz for TDD (below 3GHz in FR1) and 4 SS/PBCH blocks within SS burst,
  SCS=30kHz with 20MHz for TDD (above 3GHz in FR1) and 4 SS/PBCH blocks within SS burst, and
  SCS=120kHz with 100MHz for TDD (FR2) and 16 SS/PBCH blocks within SS burst.
RAN4 configures PDCCH/PDSCH scheduling for RMC as follows:
  Use the same subcarrier spacing as SS/PBCH block,
  Allocate 24PRB for PDSCH as same as LTE, and
  Set PDSCH MCS to 1/3 QPSK.
Set DDSUU for TDD UL/DL configuration every 5ms for SCS=15kHz. For higher SCS, scale the number of DL/UL slots accordingly. DL/UL ratio in the flexible slot ‘S’ is FFS.

## Slide 3: Way forward on the assumption of SS/PBCH block and RMSI CORESET configurations used for RMC
Schedule SS/BPCH blocks every 20ms for the baseline RMC configuration.
SS/PBCH blocks are transmitted within the active bandwidth part.
SS/PBCH blocks and PDCCH/PDSCH do not overlap in frequency domain.
PDCCH/PDSCH is not scheduled during the SMTC window.
PRB#0 of SS/PBCH is set to nPRB=0 in the active bandwidth part.
All the common search spaces (paging, SI, RAR, etc.) are configured with the RMSI CORESET.
Apply SS/PBCH and RMSI CORESET multiplexing pattern 1 for both FR1 and FR2.
RMSI CORESET starts at the same PRB as SS/PBCH, i.e., RB offset 0 in pdcch-ConfigSIB1.

## Slide 4: Way forward for DL power allocation
RAN4 will specify the DL power allocation as follow:
  EPRE of PBCH DMRS, PDCCH DMRS, PDSCH DMRS, OCNG DMRS, PSS, and NZP-CSI-RS are set relative to SSS EPRE
  EPRE of physical channels (PBCH, PDCCH, PDSCH, OCNG) are set relative to the EPRE of associated DMRS (e.g., PDSCH to PDSCH DMRS)
RAN4 is define the OCNG relative power level of the i-th virtual UE is defined as:
  γi = (EPRE ratio of PDSCHi to PDSCHi DMRS) / (EPRE ratio of OCNG to OCNG DMRS)

## Slide 5: Example of DL power allocation (for information)
Parameter | Unit | Value (Baseline) | Values for RLM out-of-synch
SSS transmit power | W | Test specific | Test specific
EPRE ratio of PSS to SSS | dB | 0 | 0
EPRE ratio of PBCH DMRS to SSS | dB | 0 | 0
EPRE ratio of PBCH to PBCH DMRS | dB | 0 | 0
EPRE ratio of PDCCH DMRS to SSS | dB | 0 | 4
EPRE ratio of PDCCH to PDCCH DMRS | dB | 0 | 0
EPRE ratio of PDSCH DMRS to SSS | dB | 0 | 0
EPRE ratio of PDSCH to PDSCH DMRS | dB | Test specific | Test specific
EPRE ratio of CSI-RS to SSS | dB | 0 | 0
EPRE ratio of OCNG DMRS to SSS | dB | 0 | 0
EPRE ratio of OCNG to OCNG DMRS (Note 1) | dB | 0 | 0
Note 1: Number of DMRS CDM groups without data for PDSCH DMRS configuration for OCNG is set to 1. |  |  |