## Slide 1: Discussion on PDCCH channel realization and testing time
Agenda Item: 5.4.1.4
Source: Ericsson
Document for: Discussion
3GPP TSG-RAN WG4 Meeting #AH1807
Montreal, Canada, 2nd – 6th Jul, 2018
R4-1809130

## Slide 2: Background
PDCCH configured for each individual UE could only occupy partial channel bandwidth.
    During LTE time all PDCCH tests are allocated with full bandwidth for one single UE, which allows the channel getting stable during the testing time
    For NR the condition changes in the following aspects.
      The propogation channel is different for NR compared to LTE, which uses TDL-A/C for FR1 and TBD for FR2.
      The channel bandwidths for both FR1 and FR2 can be much larger than LTE, We may not always configure the full channel bandwidth for all PDCCH tests
    For NR PDCCH tests we need to check if the channel realization works in the same way, in order to ensure a stable testing environment.

## Slide 3: Initial numbers for PDCCH spread - BLER
PDCCH split in 400 parts, comprising 400 subframes (and PDCCH realizations), a total of 160k PDCCH. The PDCCHs are localized and has AL2.
Overall mean BLER, as well as the 50% (median), 75% and 95% percentiles

## Slide 4: Initial numbers for PDCCH spread – linear mean BLER
Same condition as previous figure
Overall mean BLER in linear, as well as the 50% (median), 75% and 95% percentiles

## Slide 5: Proposals for PDCCH tests
Interested companies run PDCCH with the following test scenarios to study the PDCCH spread, over different number of simulation slots.
    Channel bandwidth
      20MHz
      40MHz
      100MHz
    Channel allocation
      Full bandwidth
      Partial bandwidth
    AL
      2
      4
      8
    Propagation channel
      TDL-A
      TDL-C
    Targeted BLER
      1% mean BLER
      1% Mean 50% BLER
      1% 95% BLER
    Simulation slots number
      10000
      20000
      100000
      200000

## Slide 6
ftp://ftp.3gpp.org/TSG_RAN/WG4_Radio/TSGR4_AHs/TSGR4_AH-1807/Docs/R4-1809130.zip