## Slide 1: WF on UE RF UL RMC
Qualcomm Inc., …
R4-1809334
3GPP TSG-RAN WG4 Meeting #AH1807
Montreal, Canada, 2-6 July 2018
Agenda Item: 5.5

## Slide 2: Background
R5-183950 recommends possible modulations, waveforms and RB allocation for UE RF tests for defining UL RMC at RAN4
This document summarizes the parameters for defining UL RMC for different UE RF tests.

## Slide 3: MCS and Target Code Rate
Use following MCS and code rate for different modulations:
  DFT-s-OFDM Pi/2 BPSK: MCS 0, Target Code Rate = 1/4
  DFT-s/CP OFDM QPSK: MCS 2, Target Code Rate = 1/6
  DFT-s/CP OFDM 16QAM: MCS 10, Target Code Rate = 1/3
  DFT-s OFDM 64QAM: MCS 18, Target Code Rate = 1/2
  CP OFDM 64QAM: MCS 19, Target Code Rate = 1/2
  DFT-s/CP OFDM 256QAM: MCS 20, Target Code Rate = 2/3

## Slide 4: RMC Tables
Define single RMC table for Full RB and Partial RB allocation.
Define separate tables for each combination of modulation and SCS.
In next slides, we list out all UL RMCs to be defined for UE RF tests in this meeting.

## Slide 5: Parameters for REFSENS FR1
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
5 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 75 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 20 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 100 | 2 | QPSK | 1/6
25 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
30 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
40 | 15 | DFT-S-OFDM | 216 | 2 | QPSK | 1/6
50 | 15 | DFT-S-OFDM | 270 | 2 | QPSK | 1/6
60 | 30 | DFT-S-OFDM | 162 | 2 | QPSK | 1/6
100 | 30 | DFT-S-OFDM | 270 | 2 | QPSK | 1/6

## Slide 6: Parameters for REFSENS FR2
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 132 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 264 | 2 | QPSK | 1/6

## Slide 7: Parameters for FR1 MOP: QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modul2ation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5, 10, 15, 20, 25, 30, 40, 50 | 15 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
5 | 15 | DFT-S-OFDM | 12 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
25 | 15 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
30 | 15 | DFT-S-OFDM | 80 | 2 | QPSK | 1/6
40 | 15 | DFT-S-OFDM | 108 | 2 | QPSK | 1/6
50 | 15 | DFT-S-OFDM | 135 | 2 | QPSK | 1/6
5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 30 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
5 | 30 | DFT-S-OFDM | 5 | 2 | QPSK | 1/6
10 | 30 | DFT-S-OFDM | 12 | 2 | QPSK | 1/6
15 | 30 | DFT-S-OFDM | 18 | 2 | QPSK | 1/6
20 | 30 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
25 | 30 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
30 | 30 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
40 | 30 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
50 | 30 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
60 | 30 | DFT-S-OFDM | 81 | 2 | QPSK | 1/6
80 | 30 | DFT-S-OFDM | 108 | 2 | QPSK | 1/6
90 | 30 | DFT-S-OFDM | 120 | 2 | QPSK | 1/6
100 | 30 | DFT-S-OFDM | 135 | 2 | QPSK | 1/6
10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 60 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
10 | 60 | DFT-S-OFDM | 5 | 2 | QPSK | 1/6
15 | 60 | DFT-S-OFDM | 9 | 2 | QPSK | 1/6
20 | 60 | DFT-S-OFDM | 12 | 2 | QPSK | 1/6
25 | 60 | DFT-S-OFDM | 15 | 2 | QPSK | 1/6
30 | 60 | DFT-S-OFDM | 18 | 2 | QPSK | 1/6
40 | 60 | DFT-S-OFDM | 25 |  | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
60 | 60 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
80 | 60 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
90 | 60 | DFT-S-OFDM | 60 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6

## Slide 8: Parameters for FR2 MOP: DFT-s-OFDM QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
200 | 60 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
200 | 60 | DFT-S-OFDM | 256 | 2 | QPSK | 1/6
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
50 | 120 | DFT-S-OFDM | 16 | 2 | QPSK | 1/6
50 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 256 | 2 | QPSK | 1/6

## Slide 9: Parameters for FR1 MPR: Pi/2 BPSK (Full RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
10 | 15 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
15 | 15 | DFT-S-OFDM | 75 | 0 | PI/2 BPSK | 1/4
20 | 15 | DFT-S-OFDM | 100 | 0 | PI/2 BPSK | 1/4
25 | 15 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
30 | 15 | DFT-S-OFDM | 160 | 0 | PI/2 BPSK | 1/4
40 | 15 | DFT-S-OFDM | 216 | 0 | PI/2 BPSK | 1/4
50 | 15 | DFT-S-OFDM | 270 | 0 | PI/2 BPSK | 1/4
5 | 30 | DFT-S-OFDM | 10 | 0 | PI/2 BPSK | 1/4
10 | 30 | DFT-S-OFDM | 24 | 0 | PI/2 BPSK | 1/4
15 | 30 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
20 | 30 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
25 | 30 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
30 | 30 | DFT-S-OFDM | 75 | 0 | PI/2 BPSK | 1/4
40 | 30 | DFT-S-OFDM | 100 | 0 | PI/2 BPSK | 1/4
50 | 30 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
60 | 30 | DFT-S-OFDM | 162 | 0 | PI/2 BPSK | 1/4
80 | 30 | DFT-S-OFDM | 216 | 0 | PI/2 BPSK | 1/4
90 | 30 | DFT-S-OFDM | 243 | 0 | PI/2 BPSK | 1/4
100 | 30 | DFT-S-OFDM | 270 | 0 | PI/2 BPSK | 1/4
10 | 60 | DFT-S-OFDM | 10 | 0 | PI/2 BPSK | 1/4
15 | 60 | DFT-S-OFDM | 18 | 0 | PI/2 BPSK | 1/4
20 | 60 | DFT-S-OFDM | 24 | 0 | PI/2 BPSK | 1/4
25 | 60 | DFT-S-OFDM | 30 | 0 | PI/2 BPSK | 1/4
30 | 60 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
40 | 60 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
60 | 60 | DFT-S-OFDM | 75 | 0 | PI/2 BPSK | 1/4
80 | 60 | DFT-S-OFDM | 100 | 0 | PI/2 BPSK | 1/4
90 | 60 | DFT-S-OFDM | 120 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 135 | 0 | PI/2 BPSK | 1/4

## Slide 10: Parameters for FR1 MPR: Pi/2 BPSK (Partial RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5, 10, 15, 20, 25, 30, 40, 50 | 15 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
5 | 15 | DFT-S-OFDM | 12 | 0 | PI/2 BPSK | 1/4
10 | 15 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
15 | 15 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
20 | 15 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
25 | 15 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
30 | 15 | DFT-S-OFDM | 80 | 0 | PI/2 BPSK | 1/4
40 | 15 | DFT-S-OFDM | 108 | 0 | PI/2 BPSK | 1/4
50 | 15 | DFT-S-OFDM | 135 | 0 | PI/2 BPSK | 1/4
5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 30 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
5 | 30 | DFT-S-OFDM | 5 | 0 | PI/2 BPSK | 1/4
10 | 30 | DFT-S-OFDM | 12 | 0 | PI/2 BPSK | 1/4
15 | 30 | DFT-S-OFDM | 18 | 0 | PI/2 BPSK | 1/4
20 | 30 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
25 | 30 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
30 | 30 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
40 | 30 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
50 | 30 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
60 | 30 | DFT-S-OFDM | 81 | 0 | PI/2 BPSK | 1/4
80 | 30 | DFT-S-OFDM | 108 | 0 | PI/2 BPSK | 1/4
90 | 30 | DFT-S-OFDM | 120 | 0 | PI/2 BPSK | 1/4
100 | 30 | DFT-S-OFDM | 135 | 0 | PI/2 BPSK | 1/4
10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 | 60 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
10 | 60 | DFT-S-OFDM | 5 | 0 | PI/2 BPSK | 1/4
15 | 60 | DFT-S-OFDM | 9 | 0 | PI/2 BPSK | 1/4
20 | 60 | DFT-S-OFDM | 12 | 0 | PI/2 BPSK | 1/4
25 | 60 | DFT-S-OFDM | 15 | 0 | PI/2 BPSK | 1/4
30 | 60 | DFT-S-OFDM | 18 | 0 | PI/2 BPSK | 1/4
40 | 60 | DFT-S-OFDM | 25 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
60 | 60 | DFT-S-OFDM | 36 | 0 | PI/2 BPSK | 1/4
80 | 60 | DFT-S-OFDM | 50 | 0 | PI/2 BPSK | 1/4
90 | 60 | DFT-S-OFDM | 60 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4

## Slide 11: Parameters for FR1 MPR: DFT-s-OFDM QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 25 | 2 | QPSK | 1/6
10 | 15 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
15 | 15 | DFT-S-OFDM | 75 | 2 | QPSK | 1/6
20 | 15 | DFT-S-OFDM | 100 | 2 | QPSK | 1/6
25 | 15 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
30 | 15 | DFT-S-OFDM | 160 | 2 | QPSK | 1/6
40 | 15 | DFT-S-OFDM | 216 | 2 | QPSK | 1/6
50 | 15 | DFT-S-OFDM | 270 | 2 | QPSK | 1/6
5 | 30 | DFT-S-OFDM | 10 | 2 | QPSK | 1/6
10 | 30 | DFT-S-OFDM | 24 | 2 | QPSK | 1/6
15 | 30 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
20 | 30 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
25 | 30 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
30 | 30 | DFT-S-OFDM | 75 | 2 | QPSK | 1/6
40 | 30 | DFT-S-OFDM | 100 | 2 | QPSK | 1/6
50 | 30 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
60 | 30 | DFT-S-OFDM | 162 | 2 | QPSK | 1/6
80 | 30 | DFT-S-OFDM | 216 | 2 | QPSK | 1/6
90 | 30 | DFT-S-OFDM | 243 | 2 | QPSK | 1/6
100 | 30 | DFT-S-OFDM | 270 | 2 | QPSK | 1/6
10 | 60 | DFT-S-OFDM | 10 | 2 | QPSK | 1/6
15 | 60 | DFT-S-OFDM | 18 | 2 | QPSK | 1/6
20 | 60 | DFT-S-OFDM | 24 | 2 | QPSK | 1/6
25 | 60 | DFT-S-OFDM | 30 | 2 | QPSK | 1/6
30 | 60 | DFT-S-OFDM | 36 | 2 | QPSK | 1/6
40 | 60 | DFT-S-OFDM | 50 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
60 | 60 | DFT-S-OFDM | 75 | 2 | QPSK | 1/6
80 | 60 | DFT-S-OFDM | 100 | 2 | QPSK | 1/6
90 | 60 | DFT-S-OFDM | 120 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 135 | 2 | QPSK | 1/6

## Slide 12: Parameters for FR1 MPR: DFT-s-OFDM 16QAM (Full RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 25 | 10 | 16QAM | 1/3
10 | 15 | DFT-S-OFDM | 50 | 10 | 16QAM | 1/3
15 | 15 | DFT-S-OFDM | 75 | 10 | 16QAM | 1/3
20 | 15 | DFT-S-OFDM | 100 | 10 | 16QAM | 1/3
25 | 15 | DFT-S-OFDM | 128 | 10 | 16QAM | 1/3
30 | 15 | DFT-S-OFDM | 160 | 10 | 16QAM | 1/3
40 | 15 | DFT-S-OFDM | 216 | 10 | 16QAM | 1/3
50 | 15 | DFT-S-OFDM | 270 | 10 | 16QAM | 1/3
5 | 30 | DFT-S-OFDM | 10 | 10 | 16QAM | 1/3
10 | 30 | DFT-S-OFDM | 24 | 10 | 16QAM | 1/3
15 | 30 | DFT-S-OFDM | 36 | 10 | 16QAM | 1/3
20 | 30 | DFT-S-OFDM | 50 | 10 | 16QAM | 1/3
25 | 30 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
30 | 30 | DFT-S-OFDM | 75 | 10 | 16QAM | 1/3
40 | 30 | DFT-S-OFDM | 100 | 10 | 16QAM | 1/3
50 | 30 | DFT-S-OFDM | 128 | 10 | 16QAM | 1/3
60 | 30 | DFT-S-OFDM | 162 | 10 | 16QAM | 1/3
80 | 30 | DFT-S-OFDM | 216 | 10 | 16QAM | 1/3
90 | 30 | DFT-S-OFDM | 243 | 10 | 16QAM | 1/3
100 | 30 | DFT-S-OFDM | 270 | 10 | 16QAM | 1/3
10 | 60 | DFT-S-OFDM | 10 | 10 | 16QAM | 1/3
15 | 60 | DFT-S-OFDM | 18 | 10 | 16QAM | 1/3
20 | 60 | DFT-S-OFDM | 24 | 10 | 16QAM | 1/3
25 | 60 | DFT-S-OFDM | 30 | 10 | 16QAM | 1/3
30 | 60 | DFT-S-OFDM | 36 | 10 | 16QAM | 1/3
40 | 60 | DFT-S-OFDM | 50 | 10 | 16QAM | 1/3
50 | 60 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
60 | 60 | DFT-S-OFDM | 75 | 10 | 16QAM | 1/3
80 | 60 | DFT-S-OFDM | 100 | 10 | 16QAM | 1/3
90 | 60 | DFT-S-OFDM | 120 | 10 | 16QAM | 1/3
100 | 60 | DFT-S-OFDM | 135 | 10 | 16QAM | 1/3

## Slide 13: Parameters for FR1 MPR: DFT-s-OFDM 16QAM (Partial RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 12 | 10 | 16QAM | 1/3
10 | 15 | DFT-S-OFDM | 25 | 10 | 16QAM | 1/3
15 | 15 | DFT-S-OFDM | 36 | 10 | 16QAM | 1/3
20 | 15 | DFT-S-OFDM | 50 | 10 | 16QAM | 1/3
25 | 15 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
30 | 15 | DFT-S-OFDM | 80 | 10 | 16QAM | 1/3
40 | 15 | DFT-S-OFDM | 108 | 10 | 16QAM | 1/3
50 | 15 | DFT-S-OFDM | 135 | 10 | 16QAM | 1/3
5 | 30 | DFT-S-OFDM | 5 | 10 | 16QAM | 1/3
10 | 30 | DFT-S-OFDM | 12 | 10 | 16QAM | 1/3
15 | 30 | DFT-S-OFDM | 18 | 10 | 16QAM | 1/3
20 | 30 | DFT-S-OFDM | 25 | 10 | 16QAM | 1/3
25 | 30 | DFT-S-OFDM | 32 | 10 | 16QAM | 1/3
30 | 30 | DFT-S-OFDM | 36 | 10 | 16QAM | 1/3
40 | 30 | DFT-S-OFDM | 50 | 10 | 16QAM | 1/3
50 | 30 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
60 | 30 | DFT-S-OFDM | 81 | 10 | 16QAM | 1/3
80 | 30 | DFT-S-OFDM | 108 | 10 | 16QAM | 1/3
90 | 30 | DFT-S-OFDM | 120 | 10 | 16QAM | 1/3
100 | 30 | DFT-S-OFDM | 135 | 10 | 16QAM | 1/3
10 | 60 | DFT-S-OFDM | 5 | 10 | 16QAM | 1/3
15 | 60 | DFT-S-OFDM | 9 | 10 | 16QAM | 1/3
20 | 60 | DFT-S-OFDM | 12 | 10 | 16QAM | 1/3
25 | 60 | DFT-S-OFDM | 15 | 10 | 16QAM | 1/3
30 | 60 | DFT-S-OFDM | 18 | 10 | 16QAM | 1/3
40 | 60 | DFT-S-OFDM | 25 | 10 | 16QAM | 1/3
50 | 60 | DFT-S-OFDM | 32 | 10 | 16QAM | 1/3
60 | 60 | DFT-S-OFDM | 36 | 10 | 16QAM | 1/3
80 | 60 | DFT-S-OFDM | 50 | 10 | 16QAM | 1/3
90 | 60 | DFT-S-OFDM | 60 | 10 | 16QAM | 1/3
100 | 60 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3

## Slide 14: Parameters for FR1 MPR: DFT-s-OFDM 64QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 25 | 18 | 64QAM | 1/2
10 | 15 | DFT-S-OFDM | 50 | 18 | 64QAM | 1/2
15 | 15 | DFT-S-OFDM | 75 | 18 | 64QAM | 1/2
20 | 15 | DFT-S-OFDM | 100 | 18 | 64QAM | 1/2
25 | 15 | DFT-S-OFDM | 128 | 18 | 64QAM | 1/2
30 | 15 | DFT-S-OFDM | 160 | 18 | 64QAM | 1/2
40 | 15 | DFT-S-OFDM | 216 | 18 | 64QAM | 1/2
50 | 15 | DFT-S-OFDM | 270 | 18 | 64QAM | 1/2
5 | 30 | DFT-S-OFDM | 10 | 18 | 64QAM | 1/2
10 | 30 | DFT-S-OFDM | 24 | 18 | 64QAM | 1/2
15 | 30 | DFT-S-OFDM | 36 | 18 | 64QAM | 1/2
20 | 30 | DFT-S-OFDM | 50 | 18 | 64QAM | 1/2
25 | 30 | DFT-S-OFDM | 64 | 18 | 64QAM | 1/2
30 | 30 | DFT-S-OFDM | 75 | 18 | 64QAM | 1/2
40 | 30 | DFT-S-OFDM | 100 | 18 | 64QAM | 1/2
50 | 30 | DFT-S-OFDM | 128 | 18 | 64QAM | 1/2
60 | 30 | DFT-S-OFDM | 162 | 18 | 64QAM | 1/2
80 | 30 | DFT-S-OFDM | 216 | 18 | 64QAM | 1/2
90 | 30 | DFT-S-OFDM | 243 | 18 | 64QAM | 1/2
100 | 30 | DFT-S-OFDM | 270 | 18 | 64QAM | 1/2
10 | 60 | DFT-S-OFDM | 10 | 18 | 64QAM | 1/2
15 | 60 | DFT-S-OFDM | 18 | 18 | 64QAM | 1/2
20 | 60 | DFT-S-OFDM | 24 | 18 | 64QAM | 1/2
25 | 60 | DFT-S-OFDM | 30 | 18 | 64QAM | 1/2
30 | 60 | DFT-S-OFDM | 36 | 18 | 64QAM | 1/2
40 | 60 | DFT-S-OFDM | 50 | 18 | 64QAM | 1/2
50 | 60 | DFT-S-OFDM | 64 | 18 | 64QAM | 1/2
60 | 60 | DFT-S-OFDM | 75 | 18 | 64QAM | 1/2
80 | 60 | DFT-S-OFDM | 100 | 18 | 64QAM | 1/2
90 | 60 | DFT-S-OFDM | 120 | 18 | 64QAM | 1/2
100 | 60 | DFT-S-OFDM | 135 | 18 | 64QAM | 1/2

## Slide 15: Parameters for FR1 MPR: DFT-s-OFDM 256QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | DFT-S-OFDM | 25 | 20 | 256QAM | 2/3
10 | 15 | DFT-S-OFDM | 50 | 20 | 256QAM | 2/3
15 | 15 | DFT-S-OFDM | 75 | 20 | 256QAM | 2/3
20 | 15 | DFT-S-OFDM | 100 | 20 | 256QAM | 2/3
25 | 15 | DFT-S-OFDM | 128 | 20 | 256QAM | 2/3
30 | 15 | DFT-S-OFDM | 160 | 20 | 256QAM | 2/3
40 | 15 | DFT-S-OFDM | 216 | 20 | 256QAM | 2/3
50 | 15 | DFT-S-OFDM | 270 | 20 | 256QAM | 2/3
5 | 30 | DFT-S-OFDM | 10 | 20 | 256QAM | 2/3
10 | 30 | DFT-S-OFDM | 24 | 20 | 256QAM | 2/3
15 | 30 | DFT-S-OFDM | 36 | 20 | 256QAM | 2/3
20 | 30 | DFT-S-OFDM | 50 | 20 | 256QAM | 2/3
25 | 30 | DFT-S-OFDM | 64 | 20 | 256QAM | 2/3
30 | 30 | DFT-S-OFDM | 75 | 20 | 256QAM | 2/3
40 | 30 | DFT-S-OFDM | 100 | 20 | 256QAM | 2/3
50 | 30 | DFT-S-OFDM | 128 | 20 | 256QAM | 2/3
60 | 30 | DFT-S-OFDM | 162 | 20 | 256QAM | 2/3
80 | 30 | DFT-S-OFDM | 216 | 20 | 256QAM | 2/3
90 | 30 | DFT-S-OFDM | 243 | 20 | 256QAM | 2/3
100 | 30 | DFT-S-OFDM | 270 | 20 | 256QAM | 2/3
10 | 60 | DFT-S-OFDM | 10 | 20 | 256QAM | 2/3
15 | 60 | DFT-S-OFDM | 18 | 20 | 256QAM | 2/3
20 | 60 | DFT-S-OFDM | 24 | 20 | 256QAM | 2/3
25 | 60 | DFT-S-OFDM | 30 | 20 | 256QAM | 2/3
30 | 60 | DFT-S-OFDM | 36 | 20 | 256QAM | 2/3
40 | 60 | DFT-S-OFDM | 50 | 20 | 256QAM | 2/3
50 | 60 | DFT-S-OFDM | 64 | 20 | 256QAM | 2/3
60 | 60 | DFT-S-OFDM | 75 | 20 | 256QAM | 2/3
80 | 60 | DFT-S-OFDM | 100 | 20 | 256QAM | 2/3
90 | 60 | DFT-S-OFDM | 120 | 20 | 256QAM | 2/3
100 | 60 | DFT-S-OFDM | 135 | 20 | 256QAM | 2/3

## Slide 16: Parameters for FR1 MPR: CP-OFDM QPSK (Full RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | CP-OFDM | 25 | 2 | QPSK | 1/6
10 | 15 | CP-OFDM | 52 | 2 | QPSK | 1/6
15 | 15 | CP-OFDM | 79 | 2 | QPSK | 1/6
20 | 15 | CP-OFDM | 106 | 2 | QPSK | 1/6
25 | 15 | CP-OFDM | 133 | 2 | QPSK | 1/6
30 | 15 | CP-OFDM | 160 | 2 | QPSK | 1/6
40 | 15 | CP-OFDM | 216 | 2 | QPSK | 1/6
50 | 15 | CP-OFDM | 270 | 2 | QPSK | 1/6
5 | 30 | CP-OFDM | 11 | 2 | QPSK | 1/6
10 | 30 | CP-OFDM | 24 | 2 | QPSK | 1/6
15 | 30 | CP-OFDM | 38 | 2 | QPSK | 1/6
20 | 30 | CP-OFDM | 51 | 2 | QPSK | 1/6
25 | 30 | CP-OFDM | 65 | 2 | QPSK | 1/6
30 | 30 | CP-OFDM | 78 | 2 | QPSK | 1/6
40 | 30 | CP-OFDM | 106 | 2 | QPSK | 1/6
50 | 30 | CP-OFDM | 133 | 2 | QPSK | 1/6
60 | 30 | CP-OFDM | 162 | 2 | QPSK | 1/6
80 | 30 | CP-OFDM | 217 | 2 | QPSK | 1/6
90 | 30 | CP-OFDM | 245 | 2 | QPSK | 1/6
100 | 30 | CP-OFDM | 273 | 2 | QPSK | 1/6
10 | 60 | CP-OFDM | 11 | 2 | QPSK | 1/6
15 | 60 | CP-OFDM | 18 | 2 | QPSK | 1/6
20 | 60 | CP-OFDM | 24 | 2 | QPSK | 1/6
25 | 60 | CP-OFDM | 31 | 2 | QPSK | 1/6
30 | 60 | CP-OFDM | 38 | 2 | QPSK | 1/6
40 | 60 | CP-OFDM | 51 | 2 | QPSK | 1/6
50 | 60 | CP-OFDM | 65 | 2 | QPSK | 1/6
60 | 60 | CP-OFDM | 79 | 2 | QPSK | 1/6
80 | 60 | CP-OFDM | 107 | 2 | QPSK | 1/6
90 | 60 | CP-OFDM | 121 | 2 | QPSK | 1/6
100 | 60 | CP-OFDM | 135 | 2 | QPSK | 1/6

## Slide 17: Parameters for FR1 MPR: CP-OFDM QPSK (Partial RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | CP-OFDM | 13 | 2 | QPSK | 1/6
10 | 15 | CP-OFDM | 26 | 2 | QPSK | 1/6
15 | 15 | CP-OFDM | 40 | 2 | QPSK | 1/6
20 | 15 | CP-OFDM | 53 | 2 | QPSK | 1/6
25 | 15 | CP-OFDM | 67 | 2 | QPSK | 1/6
30 | 15 | CP-OFDM | 80 | 2 | QPSK | 1/6
40 | 15 | CP-OFDM | 108 | 2 | QPSK | 1/6
50 | 15 | CP-OFDM | 135 | 2 | QPSK | 1/6
5 | 30 | CP-OFDM | 6 | 2 | QPSK | 1/6
10 | 30 | CP-OFDM | 12 | 2 | QPSK | 1/6
15 | 30 | CP-OFDM | 19 | 2 | QPSK | 1/6
20 | 30 | CP-OFDM | 26 | 2 | QPSK | 1/6
25 | 30 | CP-OFDM | 33 | 2 | QPSK | 1/6
30 | 30 | CP-OFDM | 39 | 2 | QPSK | 1/6
40 | 30 | CP-OFDM | 53 | 2 | QPSK | 1/6
50 | 30 | CP-OFDM | 67 | 2 | QPSK | 1/6
60 | 30 | CP-OFDM | 81 | 2 | QPSK | 1/6
80 | 30 | CP-OFDM | 109 | 2 | QPSK | 1/6
90 | 30 | CP-OFDM | 123 | 2 | QPSK | 1/6
100 | 30 | CP-OFDM | 137 | 2 | QPSK | 1/6
10 | 60 | CP-OFDM | 6 | 2 | QPSK | 1/6
15 | 60 | CP-OFDM | 9 | 2 | QPSK | 1/6
20 | 60 | CP-OFDM | 12 | 2 | QPSK | 1/6
25 | 60 | CP-OFDM | 16 | 2 | QPSK | 1/6
30 | 60 | CP-OFDM | 19 | 2 | QPSK | 1/6
40 | 60 | CP-OFDM | 26 | 2 | QPSK | 1/6
50 | 60 | CP-OFDM | 33 | 2 | QPSK | 1/6
60 | 60 | CP-OFDM | 40 | 2 | QPSK | 1/6
80 | 60 | CP-OFDM | 54 | 2 | QPSK | 1/6
90 | 60 | CP-OFDM | 61 | 2 | QPSK | 1/6
100 | 60 | CP-OFDM | 68 | 2 | QPSK | 1/6

## Slide 18: Parameters for FR1 MPR: CP-OFDM 16QAM (Full RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | CP-OFDM | 25 | 10 | 16QAM | 1/3
10 | 15 | CP-OFDM | 52 | 10 | 16QAM | 1/3
15 | 15 | CP-OFDM | 79 | 10 | 16QAM | 1/3
20 | 15 | CP-OFDM | 106 | 10 | 16QAM | 1/3
25 | 15 | CP-OFDM | 133 | 10 | 16QAM | 1/3
30 | 15 | CP-OFDM | 160 | 10 | 16QAM | 1/3
40 | 15 | CP-OFDM | 216 | 10 | 16QAM | 1/3
50 | 15 | CP-OFDM | 270 | 10 | 16QAM | 1/3
5 | 30 | CP-OFDM | 11 | 10 | 16QAM | 1/3
10 | 30 | CP-OFDM | 24 | 10 | 16QAM | 1/3
15 | 30 | CP-OFDM | 38 | 10 | 16QAM | 1/3
20 | 30 | CP-OFDM | 51 | 10 | 16QAM | 1/3
25 | 30 | CP-OFDM | 65 | 10 | 16QAM | 1/3
30 | 30 | CP-OFDM | 78 | 10 | 16QAM | 1/3
40 | 30 | CP-OFDM | 106 | 10 | 16QAM | 1/3
50 | 30 | CP-OFDM | 133 | 10 | 16QAM | 1/3
60 | 30 | CP-OFDM | 162 | 10 | 16QAM | 1/3
80 | 30 | CP-OFDM | 217 | 10 | 16QAM | 1/3
90 | 30 | CP-OFDM | 245 | 10 | 16QAM | 1/3
100 | 30 | CP-OFDM | 273 | 10 | 16QAM | 1/3
10 | 60 | CP-OFDM | 11 | 10 | 16QAM | 1/3
15 | 60 | CP-OFDM | 18 | 10 | 16QAM | 1/3
20 | 60 | CP-OFDM | 24 | 10 | 16QAM | 1/3
25 | 60 | CP-OFDM | 31 | 10 | 16QAM | 1/3
30 | 60 | CP-OFDM | 38 | 10 | 16QAM | 1/3
40 | 60 | CP-OFDM | 51 | 10 | 16QAM | 1/3
50 | 60 | CP-OFDM | 65 | 10 | 16QAM | 1/3
60 | 60 | CP-OFDM | 79 | 10 | 16QAM | 1/3
80 | 60 | CP-OFDM | 107 | 10 | 16QAM | 1/3
90 | 60 | CP-OFDM | 121 | 10 | 16QAM | 1/3
100 | 60 | CP-OFDM | 135 | 10 | 16QAM | 1/3

## Slide 19: Parameters for FR1 MPR: CP-OFDM 16QAM (Partial RB)
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | CP-OFDM | 13 | 10 | 16QAM | 1/3
10 | 15 | CP-OFDM | 26 | 10 | 16QAM | 1/3
15 | 15 | CP-OFDM | 40 | 10 | 16QAM | 1/3
20 | 15 | CP-OFDM | 53 | 10 | 16QAM | 1/3
25 | 15 | CP-OFDM | 67 | 10 | 16QAM | 1/3
30 | 15 | CP-OFDM | 80 | 10 | 16QAM | 1/3
40 | 15 | CP-OFDM | 108 | 10 | 16QAM | 1/3
50 | 15 | CP-OFDM | 135 | 10 | 16QAM | 1/3
5 | 30 | CP-OFDM | 6 | 10 | 16QAM | 1/3
10 | 30 | CP-OFDM | 12 | 10 | 16QAM | 1/3
15 | 30 | CP-OFDM | 19 | 10 | 16QAM | 1/3
20 | 30 | CP-OFDM | 26 | 10 | 16QAM | 1/3
25 | 30 | CP-OFDM | 33 | 10 | 16QAM | 1/3
30 | 30 | CP-OFDM | 39 | 10 | 16QAM | 1/3
40 | 30 | CP-OFDM | 53 | 10 | 16QAM | 1/3
50 | 30 | CP-OFDM | 67 | 10 | 16QAM | 1/3
60 | 30 | CP-OFDM | 81 | 10 | 16QAM | 1/3
80 | 30 | CP-OFDM | 109 | 10 | 16QAM | 1/3
90 | 30 | CP-OFDM | 123 | 10 | 16QAM | 1/3
100 | 30 | CP-OFDM | 137 | 10 | 16QAM | 1/3
10 | 60 | CP-OFDM | 6 | 10 | 16QAM | 1/3
15 | 60 | CP-OFDM | 9 | 10 | 16QAM | 1/3
20 | 60 | CP-OFDM | 12 | 10 | 16QAM | 1/3
25 | 60 | CP-OFDM | 16 | 10 | 16QAM | 1/3
30 | 60 | CP-OFDM | 19 | 10 | 16QAM | 1/3
40 | 60 | CP-OFDM | 26 | 10 | 16QAM | 1/3
50 | 60 | CP-OFDM | 33 | 10 | 16QAM | 1/3
60 | 60 | CP-OFDM | 40 | 10 | 16QAM | 1/3
80 | 60 | CP-OFDM | 54 | 10 | 16QAM | 1/3
90 | 60 | CP-OFDM | 61 | 10 | 16QAM | 1/3
100 | 60 | CP-OFDM | 68 | 10 | 16QAM | 1/3

## Slide 20: Parameters for FR1 MPR: CP-OFDM 64QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | CP-OFDM | 25 | 19 | 64QAM | 1/2
10 | 15 | CP-OFDM | 52 | 19 | 64QAM | 1/2
15 | 15 | CP-OFDM | 79 | 19 | 64QAM | 1/2
20 | 15 | CP-OFDM | 106 | 19 | 64QAM | 1/2
25 | 15 | CP-OFDM | 133 | 19 | 64QAM | 1/2
30 | 15 | CP-OFDM | 160 | 19 | 64QAM | 1/2
40 | 15 | CP-OFDM | 216 | 19 | 64QAM | 1/2
50 | 15 | CP-OFDM | 270 | 19 | 64QAM | 1/2
5 | 30 | CP-OFDM | 11 | 19 | 64QAM | 1/2
10 | 30 | CP-OFDM | 24 | 19 | 64QAM | 1/2
15 | 30 | CP-OFDM | 38 | 19 | 64QAM | 1/2
20 | 30 | CP-OFDM | 51 | 19 | 64QAM | 1/2
25 | 30 | CP-OFDM | 65 | 19 | 64QAM | 1/2
30 | 30 | CP-OFDM | 78 | 19 | 64QAM | 1/2
40 | 30 | CP-OFDM | 106 | 19 | 64QAM | 1/2
50 | 30 | CP-OFDM | 133 | 19 | 64QAM | 1/2
60 | 30 | CP-OFDM | 162 | 19 | 64QAM | 1/2
80 | 30 | CP-OFDM | 217 | 19 | 64QAM | 1/2
90 | 30 | CP-OFDM | 245 | 19 | 64QAM | 1/2
100 | 30 | CP-OFDM | 273 | 19 | 64QAM | 1/2
10 | 60 | CP-OFDM | 11 | 19 | 64QAM | 1/2
15 | 60 | CP-OFDM | 18 | 19 | 64QAM | 1/2
20 | 60 | CP-OFDM | 24 | 19 | 64QAM | 1/2
25 | 60 | CP-OFDM | 31 | 19 | 64QAM | 1/2
30 | 60 | CP-OFDM | 38 | 19 | 64QAM | 1/2
40 | 60 | CP-OFDM | 51 | 19 | 64QAM | 1/2
50 | 60 | CP-OFDM | 65 | 19 | 64QAM | 1/2
60 | 60 | CP-OFDM | 79 | 19 | 64QAM | 1/2
80 | 60 | CP-OFDM | 107 | 19 | 64QAM | 1/2
90 | 60 | CP-OFDM | 121 | 19 | 64QAM | 1/2
100 | 60 | CP-OFDM | 135 | 19 | 64QAM | 1/2

## Slide 21: Parameters for FR1 MPR: CP-OFDM QPSK 256QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
5 | 15 | CP-OFDM | 25 | 20 | 256QAM | 2/3
10 | 15 | CP-OFDM | 52 | 20 | 256QAM | 2/3
15 | 15 | CP-OFDM | 79 | 20 | 256QAM | 2/3
20 | 15 | CP-OFDM | 106 | 20 | 256QAM | 2/3
25 | 15 | CP-OFDM | 133 | 20 | 256QAM | 2/3
30 | 15 | CP-OFDM | 160 | 20 | 256QAM | 2/3
40 | 15 | CP-OFDM | 216 | 20 | 256QAM | 2/3
50 | 15 | CP-OFDM | 270 | 20 | 256QAM | 2/3
5 | 30 | CP-OFDM | 11 | 20 | 256QAM | 2/3
10 | 30 | CP-OFDM | 24 | 20 | 256QAM | 2/3
15 | 30 | CP-OFDM | 38 | 20 | 256QAM | 2/3
20 | 30 | CP-OFDM | 51 | 20 | 256QAM | 2/3
25 | 30 | CP-OFDM | 65 | 20 | 256QAM | 2/3
30 | 30 | CP-OFDM | 78 | 20 | 256QAM | 2/3
40 | 30 | CP-OFDM | 106 | 20 | 256QAM | 2/3
50 | 30 | CP-OFDM | 133 | 20 | 256QAM | 2/3
60 | 30 | CP-OFDM | 162 | 20 | 256QAM | 2/3
80 | 30 | CP-OFDM | 217 | 20 | 256QAM | 2/3
90 | 30 | CP-OFDM | 245 | 20 | 256QAM | 2/3
100 | 30 | CP-OFDM | 273 | 20 | 256QAM | 2/3
10 | 60 | CP-OFDM | 11 | 20 | 256QAM | 2/3
15 | 60 | CP-OFDM | 18 | 20 | 256QAM | 2/3
20 | 60 | CP-OFDM | 24 | 20 | 256QAM | 2/3
25 | 60 | CP-OFDM | 31 | 20 | 256QAM | 2/3
30 | 60 | CP-OFDM | 38 | 20 | 256QAM | 2/3
40 | 60 | CP-OFDM | 51 | 20 | 256QAM | 2/3
50 | 60 | CP-OFDM | 65 | 20 | 256QAM | 2/3
60 | 60 | CP-OFDM | 79 | 20 | 256QAM | 2/3
80 | 60 | CP-OFDM | 107 | 20 | 256QAM | 2/3
90 | 60 | CP-OFDM | 121 | 20 | 256QAM | 2/3
100 | 60 | CP-OFDM | 135 | 20 | 256QAM | 2/3

## Slide 22: Parameters for FR2 MPR: Pi/2 BPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
50 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
100 | 60 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
200 | 60 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
200 | 60 | DFT-S-OFDM | 256 | 0 | PI/2 BPSK | 1/4
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 0 | PI/2 BPSK | 1/4
50 | 120 | DFT-S-OFDM | 16 | 0 | PI/2 BPSK | 1/4
50 | 120 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
100 | 120 | DFT-S-OFDM | 32 | 0 | PI/2 BPSK | 1/4
100 | 120 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
200 | 120 | DFT-S-OFDM | 64 | 0 | PI/2 BPSK | 1/4
200 | 120 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
400 | 120 | DFT-S-OFDM | 128 | 0 | PI/2 BPSK | 1/4
400 | 120 | DFT-S-OFDM | 256 | 0 | PI/2 BPSK | 1/4

## Slide 23: Parameters for FR2 MPR: DFT-s-OFDM QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
50 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
100 | 60 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
200 | 60 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
200 | 60 | DFT-S-OFDM | 256 | 2 | QPSK | 1/6
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 2 | QPSK | 1/6
50 | 120 | DFT-S-OFDM | 16 | 2 | QPSK | 1/6
50 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 64 | 2 | QPSK | 1/6
200 | 120 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 128 | 2 | QPSK | 1/6
400 | 120 | DFT-S-OFDM | 256 | 2 | QPSK | 1/6

## Slide 24: Parameters for FR2 MPR: DFT-s-OFDM 16QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 10 | 16QAM | 1/3
50 | 60 | DFT-S-OFDM | 32 | 10 | 16QAM | 1/3
50 | 60 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
100 | 60 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
100 | 60 | DFT-S-OFDM | 128 | 10 | 16QAM | 1/3
200 | 60 | DFT-S-OFDM | 128 | 10 | 16QAM | 1/3
200 | 60 | DFT-S-OFDM | 256 | 10 | 16QAM | 1/3
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 10 | 16QAM | 1/3
50 | 120 | DFT-S-OFDM | 16 | 10 | 16QAM | 1/3
50 | 120 | DFT-S-OFDM | 32 | 10 | 16QAM | 1/3
100 | 120 | DFT-S-OFDM | 32 | 10 | 16QAM | 1/3
100 | 120 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
200 | 120 | DFT-S-OFDM | 64 | 10 | 16QAM | 1/3
200 | 120 | DFT-S-OFDM | 128 | 10 | 16QAM | 1/3
400 | 120 | DFT-S-OFDM | 128 | 10 | 16QAM | 1/3
400 | 120 | DFT-S-OFDM | 256 | 10 | 16QAM | 1/3

## Slide 25: Parameters for FR2 MPR: DFT-s-OFDM 64QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | DFT-S-OFDM | 1 | 18 | 64QAM | 1/2
50 | 60 | DFT-S-OFDM | 32 | 18 | 64QAM | 1/2
50 | 60 | DFT-S-OFDM | 64 | 18 | 64QAM | 1/2
100 | 60 | DFT-S-OFDM | 64 | 18 | 64QAM | 1/2
100 | 60 | DFT-S-OFDM | 128 | 18 | 64QAM | 1/2
200 | 60 | DFT-S-OFDM | 128 | 18 | 64QAM | 1/2
200 | 60 | DFT-S-OFDM | 256 | 18 | 64QAM | 1/2
50,100,200,400 | 120 | DFT-S-OFDM | 1 | 18 | 64QAM | 1/2
50 | 120 | DFT-S-OFDM | 16 | 18 | 64QAM | 1/2
50 | 120 | DFT-S-OFDM | 32 | 18 | 64QAM | 1/2
100 | 120 | DFT-S-OFDM | 32 | 18 | 64QAM | 1/2
100 | 120 | DFT-S-OFDM | 64 | 18 | 64QAM | 1/2
200 | 120 | DFT-S-OFDM | 64 | 18 | 64QAM | 1/2
200 | 120 | DFT-S-OFDM | 128 | 18 | 64QAM | 1/2
400 | 120 | DFT-S-OFDM | 128 | 18 | 64QAM | 1/2
400 | 120 | DFT-S-OFDM | 256 | 18 | 64QAM | 1/2

## Slide 26: Parameters for FR2 MPR: CP-OFDM QPSK
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | CP-OFDM | 1 | 2 | QPSK | 1/6
50 | 60 | CP-OFDM | 33 | 2 | QPSK | 1/6
50 | 60 | CP-OFDM | 66 | 2 | QPSK | 1/6
100 | 60 | CP-OFDM | 66 | 2 | QPSK | 1/6
100 | 60 | CP-OFDM | 132 | 2 | QPSK | 1/6
200 | 60 | CP-OFDM | 264 | 2 | QPSK | 1/6
200 | 60 | CP-OFDM | 264 | 2 | QPSK | 1/6
50,100,200,400 | 120 | CP-OFDM | 1 | 2 | QPSK | 1/6
50 | 120 | CP-OFDM | 16 | 2 | QPSK | 1/6
50 | 120 | CP-OFDM | 32 | 2 | QPSK | 1/6
100 | 120 | CP-OFDM | 33 | 2 | QPSK | 1/6
100 | 120 | CP-OFDM | 66 | 2 | QPSK | 1/6
200 | 120 | CP-OFDM | 66 | 2 | QPSK | 1/6
200 | 120 | CP-OFDM | 132 | 2 | QPSK | 1/6
400 | 120 | CP-OFDM | 132 | 2 | QPSK | 1/6
400 | 120 | CP-OFDM | 264 | 2 | QPSK | 1/6

## Slide 27: Parameters for FR2 MPR: CP-OFDM 16QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | CP-OFDM | 1 | 10 | 16QAM | 1/3
50 | 60 | CP-OFDM | 33 | 10 | 16QAM | 1/3
50 | 60 | CP-OFDM | 66 | 10 | 16QAM | 1/3
100 | 60 | CP-OFDM | 66 | 10 | 16QAM | 1/3
100 | 60 | CP-OFDM | 132 | 10 | 16QAM | 1/3
200 | 60 | CP-OFDM | 264 | 10 | 16QAM | 1/3
200 | 60 | CP-OFDM | 264 | 10 | 16QAM | 1/3
50,100,200,400 | 120 | CP-OFDM | 1 | 10 | 16QAM | 1/3
50 | 120 | CP-OFDM | 16 | 10 | 16QAM | 1/3
50 | 120 | CP-OFDM | 32 | 10 | 16QAM | 1/3
100 | 120 | CP-OFDM | 33 | 10 | 16QAM | 1/3
100 | 120 | CP-OFDM | 66 | 10 | 16QAM | 1/3
200 | 120 | CP-OFDM | 66 | 10 | 16QAM | 1/3
200 | 120 | CP-OFDM | 132 | 10 | 16QAM | 1/3
400 | 120 | CP-OFDM | 132 | 10 | 16QAM | 1/3
400 | 120 | CP-OFDM | 264 | 10 | 16QAM | 1/3

## Slide 28: Parameters for FR2 MPR: CP-OFDM 64QAM
Channel bandwidth | Subcarrier Spacing | Waveform | Number of resource blocks | MCS Index | Modulation | Target Coding Rate
MHz | KHz |  |  |  |  | 
50, 100, 200 | 60 | CP-OFDM | 1 | 19 | 64QAM | 1/2
50 | 60 | CP-OFDM | 33 | 19 | 64QAM | 1/2
50 | 60 | CP-OFDM | 66 | 19 | 64QAM | 1/2
100 | 60 | CP-OFDM | 66 | 19 | 64QAM | 1/2
100 | 60 | CP-OFDM | 132 | 19 | 64QAM | 1/2
200 | 60 | CP-OFDM | 264 | 19 | 64QAM | 1/2
200 | 60 | CP-OFDM | 264 | 19 | 64QAM | 1/2
50,100,200,400 | 120 | CP-OFDM | 1 | 19 | 64QAM | 1/2
50 | 120 | CP-OFDM | 16 | 19 | 64QAM | 1/2
50 | 120 | CP-OFDM | 32 | 19 | 64QAM | 1/2
100 | 120 | CP-OFDM | 33 | 19 | 64QAM | 1/2
100 | 120 | CP-OFDM | 66 | 19 | 64QAM | 1/2
200 | 120 | CP-OFDM | 66 | 19 | 64QAM | 1/2
200 | 120 | CP-OFDM | 132 | 19 | 64QAM | 1/2
400 | 120 | CP-OFDM | 132 | 19 | 64QAM | 1/2
400 | 120 | CP-OFDM | 264 | 19 | 64QAM | 1/2