## Slide 1: Way forward on OCNG pattern for RF and demodulation requirements
Rohde & Schwarz
3GPP TSG-RAN WG4 Meeting AH-1807 R4-1809343
Montreal, Canada, 02nd – 06th July 2018

## Slide 2: Background and Rational
At R4-AH-1807 meeting, R4-1808852 and R4-1808849 propose OCNG pattern for NR RF Rx testing for respectively for FR1 and FR2.
The pattern description follow the LTE format, where different OCNG patterns were defined for different RBs allocated with OCNG.
However the scope and result is always the same:
  all unallocated resources are filled with pseudo randomly QPSK modulated data with the same power
In addition:
  the many virtual UEs are not necessary since these would be transparent for DUT, which is assumed to demodulate only the assigned PDSCH.
  since there is no DL Tx diversity for NR, in case multiple antenna ports transmission is used, the same transmission scheme as for the DUT can be used for OCNG.
  allocation of control region with OCNG can be part of the OCNG pattern
As such the definition of OCNG for NR can be more generic, which will decrease the maintenance work and the specification readability.

## Slide 3: Proposals
1) Describe OCNG pattern in a more compact and simplified manner using following table format.
2) Don‘t differentiate OCNG patterns based on different resources allocated with OCNG.
3) Introduction of a power coefficient scaling the OCNG power relative to PDSCH is need based.
4) The proposal is for RF and Demod. Simplification for RRM needs still to be discussed.
OCNG Appliance OCNG Parameters | Control Region (CORESET) | Data Region
Resources allocated | All unused REs (Note 1) | All unused REs
Structure | PDCCH | PDSCH
Content | Padding REs | Uncorrelated pseudo random QPSK modulated data
Transmission scheme for multiple antennas ports transmission | … | Spatial multiplexing using any precoding matrix with dimensions same as for RMC PDSCH
Subcarrier Spacing | Same as for RMC PDCCH | Same as for RMC PDSCH
Power Level | Same as for RMC PDCCH | Same as for RMC PDSCH
Note 1: All unused REs in the active CORESETS appointed by the search spaces in use on a given TTI |  | 
Table A.5…: OP.1 Generic OCNG pattern for full unused-resources allocation