## Slide 1: Way forward on the DL power allocation and SNR definition for UE RF and demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809344

## Slide 2: Background
In LTE, the downlink power allocation setting for the UE demodulation and CSI reporting requirements are set with σA (RA) and σB (RB), which is the ratio of physical channel EPRE to the common reference symbol EPRE. However, NR has no CRS and therefore TS38.101 cannot use RA/RB for power allocation setting.

## Slide 3: Way forward on DL power allocation
RAN4 will specify the DL power allocation as follow:
  The downlink SSS transmit power is defined as the linear average over the power contributions (in [W]) of all resource elements that carry the SSS within the operating system bandwidth (cf. TS38.214 4.1).
  EPRE of PBCH_DMRS, PDCCH_DMRS, PDSCH_DMRS, PSS, and NZP-CSI-RS are set relative to SSS EPRE
  EPRE of physical channels (PBCH, PDCCH, PDSCH) are set relative to the EPRE of associated DMRS (e.g., PDSCH to PDSCH_DMRS)
  EPRE of PT-RS is set relative to the associated PDSCH
  FFS for OCNG
EPRE: Energy per Resource Element

## Slide 4: Example of DL power allocation (For information)
Parameter | Unit | Value
SSS transmit power | W | Test specific
EPRE ratio of PSS to SSS | dB | 0
EPRE ratio of PBCH_DMRS to SSS | dB | 0
EPRE ratio of PBCH to PBCH_DMRS | dB | 0
EPRE ratio of PDCCH_DMRS to SSS | dB | 0
EPRE ratio of PDCCH to PDCCH_DMRS | dB | 0
EPRE ratio of PDSCH_DMRS to SSS | dB | 0
EPRE ratio of PDSCH to PDSCH_DMRS | dB | Test specific
EPRE ratio of CSI-RS to SSS | dB | 0
EPRE ratio of PT-RS to PDSCH | dB | Test specific
Note 1: Number of DMRS CDM groups without data for PDSCH_DMRS configuration for OCNG is set to 1. |  | 

## Slide 5: Way forward on SNR definition
UE demodulation and CSI requirements specified in TS 38.101-4 define the SNR definition for physical channels or signals as follows:
    demotes the number of receiver reference points, and the super script receiver reference point j.
    The SNR<signal> definition assumes that the resource elements are not precoded.
    The SNR<signal> definition does not account for any gain which can be associated to the precoding operation.
    denotes the averaged received energy per resource element (EPRE) of the wanted signal <signal>.
      Example of <signal>: PDSCH, PDSCH_DMRS, PDCCH, etc.
    denotes the power spectral density of a white noise source (average power per RE normalized to the subcarrier spacing.

## Slide 6: Examples of SNR definition
PDSCH
PDSCH DMRS
SSS