## Slide 1: WF on NR PUSCH demodulation requirements
Nokia, Nokia Shanghai Bell, […]
3GPP TSG-RAN WG4 RAN#86bis
Montreal, Canada, July 2nd – 6th 2018
Agenda: 5.4.2.2
R4-1809336
Document for: Approval

## Slide 2: Test setup
Transmission scheme.
  Define the requirements of PUSCH with 1Tx and 2Tx
  Define the requirements for 2 layer transmission for 2Tx
    FFS: pre-coding used in the test cases
DMRS configuration
  DMRS symbol length: UL-DMRS-max-len = 1
  No data and DM-RS multiplexing in the same OFDM symbol
  DMRS type
    Requirements are defined for DMRS type 1
    FFS if requirements are defined for DMRS type 2
  DMRS number
    FR1: 1 (one front-loaded) and 1+1 (one front-loaded and one additional)
    FR2: 1 (one front-loaded)
PTRS configuration
  PTRS are configured in FR2 test cases, the configuration is:
    KPTRS : [2 (PTRS every 2 RBs)]
    LPTRS : [1 (all symbols with PTRS)]

## Slide 3: Test setup
Time domain resource
  FR1
    Slot-based transmission with resource mapping type A
    FFS:
      resource mapping type B
      non-slot based transmission
  FR2
    Non-slot-based transmission with resource mapping type B and X UL symbols
      X is FFS.
    FFS:
      slot-based transmission
      Resource mapping type A
Frequency domain resource
  Only full RB allocation of the applicable test BW is used

## Slide 4: Test setup
MCS to be used for test
  CP-OFDM
    QPSK: MCS2 (LDPC base graph #2)
    16QAM: MCS16 (LDPC base graph #1)
    64QAM: MCS20 (LDPC base graph #1) for 1Tx
  DFT-s-OFDM
    Only use QPSK for DFT-s-OFDM
    FFS: Define the performance requirement for pi/2-BPSK in Q4 2018 in Rel-15
Code block group based PUSCH: Disabled
Frequency hopping: Disabled
Limited buffer rate matching: FFS enabled or disabled
Testing metric
  Only use SNR @ 70% maximum throughput of the FRC

## Slide 5: Simulation assumptions for simulation alignment
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1 | 1
Number of Rx | 2 | 2
Transmission scheme | n.a. | n.a.
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1
symbols length | 14 | X
Time domain resource allocation type | type A | type B
MCS index | 2, 16, 20 | 2, 16, 20
Carrier frequency (GHz) | 4 | 30
Propagation channel | TDL-A 30ns 10Hz | AWGN
SCS and BW | 15kHz: 10 30kHz: 40 | 60kHz: 100 120kHz: 100
Timing offset | 0 | 0
Frequency offset | 0 | 0
PTRS | Not configured | Configured with KPTRS =2, LPTRS =1