## Slide 1: Way forward on PBCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting AH1807
Montreal, Canada, 2 – 6 July, 2018
R4-1809391

## Slide 2: Agreements
RAN4 introduces the PBCH demodulation requirements in Rel-15.
  Note the PBCH demodulation requirements do not need to be tested in RAN5 as same as LTE PBCH demodulation requirements.
Test metric:
  SNR_PBCH@1% Pm-bch. Pm-bch is defined as 1-A/B, where A is the number of correctly decoded MIB PDUs and B is the number of transmitted MIB PDUs.
  UE combines the PBCH symbols of the same SSB index within the MIB TTI (80ms).
Interested companies are encouraged to provide the simulation results in RAN4#88.
  Companies may prioritize other physical channel (PDSCH and PDCCH), and CSI reporting.

## Slide 3: Simulation assumption (Common setup)
Parameters | Unit | Values
Cell ID |  | 0
CP length |  | Normal
Number of SS/PBCH blocks within an SS burst set periodicity |  | 1
SS/PBCH block index |  | 0
SS burst periodicity | ms | 20
MIB size | bits | 24
PBCH payload size (including CRC=24bits and 8 bits of SS/PBCH location information) | bits | 56

## Slide 4: Simulation assumption (For initial alignment purpose)
Parameters | Test 1 | Test 2 | Test 3 | Test 4
Frequency range | FR1 | FR1 | FR2 | FR2
Channel BW | 10MHz | 40MHz | 100MHz | 100MHz
SS/PBCH SCS | 15kHz | 30kHz | 120kHz | 240kHz
SS Block pattern (Note 2) | Case A | Case B Case C | Case D | Case E
Antenna configuration | 1x2 | 1x2 | 1x2 | 1x2
Propagation channel (Note 1) | TDL-C RMS DS=300ns Doppler=100Hz | TDL-A RMS DS=30ns, Doppler=10Hz | FFS | FFS
Note 1: Use PDP specified in TS38.901
Note 2: Depending on the operating band. Refers to TS38.101-1 Table 5.4.3.3-1 for which band uses which pattern