## Slide 1: Way forward on channel model for NR UE demodulation and CSI requirements for FR2
Qualcomm Inc., Keysight Technologies,…
R4-1809399
3GPP TSG-RAN WG4 Meeting #AH1807
Montreal, Canada, 2-6 July 2018
Agenda Item: 5.4.1

## Slide 2: Background
From Testability SI, two channel model options are considered to be feasible from TE implementation perspective.
These channel models will be emulated and then transmitted into test chamber using single probe dual-polarized antenna.
Methodologies for generating these models are captured in TR38.810.
This paper summarizes the two channel model options.

## Slide 3: Channel Model Option 1
Modelling methodology is based on TR 38.901
TDL PDPs can be generated from CDL taking into account Tx/Rx beamforming or existing PDPs in TE 38.901 could be reused
Each tap is modelled based on the Jakes Doppler fading model
R4-1808758 (Intel) provides more details on this option.

## Slide 4: Channel Model Option 2
This option considers channel model methodology with non-Jakes spectrum. Multi-path fading propagation conditions between the gNB emulator and test chamber probe is modelled as Clustered Delay Line (CDL).
Detailed model description is provided in TR 38.810 and TR 38.901
The model results in Non-Jakes Doppler spectrum
R4-1808797(Qualcomm) and R4-1809236 (Keysight) provide more details on the values of parameters. These values are summarized in the Annex A.

## Slide 5: Down-selection
Based on offline discussion, below are the preferences of different companies:
Channel Model Option 1:
  Intel, Huawei
Channel Model Option 2:
  Qualcomm, Verizon, Ericsson, AT&T

## Slide 6: Annex A: Channel model 2 parameters proposal
Target delay spread and angle spreads:
Model | Scenario | [ns] | [deg] |  |  |  | Kf [dB]
 |  |  | ASD | ASA | ZSD | ZSA | 
CDL-A | UMi O2I NLOS | 239.9 | 17.8 | 57.5 | 1.6 | 10.2 | -
CDL-B | UMi NLOS | 65.9 | 15.6 | 49.3 | 1.1 | 7.3 | -
CDL-C | Indoor NLOS | 26.2 | 41.7 | 50.4 | 12.0 | 14.7 | -
CDL-D | Indoor LOS | 19.7 | 33.3 (39.8) | 26.0 (31.9) | 1.4 | 11.5 | 7
CDL-E | UMi LOS | 32.3 | 11.7 (13.7) | 28.0 (41.0) | 1.6 | 3.8 | 9
The target spread values of Table 8.2.1.2-2 are median values from Table 7.5-6 in 38.901. However, the ASD and ASA values marked in Table 8.2.1.2-2 in red font are modified target spreads and the actual median values are given in parenthesis. The modification is done, because the median values are not achievable with the Ricean K-factor values of 7 and 9 dB.

## Slide 7: Annex A: Channel model 2 parameters proposal
K-factor:
  K-factor is as in the table:
Model | Scenario | Kf [dB]
CDL-A | UMi O2I NLOS | -
CDL-B | UMi NLOS | -
CDL-C | Indoor NLOS | -
CDL-D | Indoor LOS | 7
CDL-E | UMi LOS | 9

## Slide 8: Annex A: Channel model 2 parameters proposal
Initial phases for each ray m of each cluster n for NLOS paths and distance d3D (explained in 38.901, Figure 7.4.1-1 to model LOS path loss) for LOS path:
  Use the random number generator defined in TS 38.211 Section 5.2.1 with fixed cinit to generate the initial phases for generating the channel model using option2.
Coupling of ray angles of arrival and departure:
  Fixed pairing between angles of arrival and angles of departure as described by the table:

## Slide 9: Annex A: Channel model 2 parameters proposal
gNB antenna characteristics (gNB antenna field pattern, gNB antenna orientation and polarization):
Antenna elements are ±45 deg polarized.
The antenna orientation at the gNB is set such that the main-lobe of the antenna radiation pattern (broad side of the array) aligns to the strongest cluster direction, which is the LOS direction in LOS scenarios.

## Slide 10: Annex A: Channel model 2 parameters proposal
UE antenna characteristics (UE antenna field pattern, UE antenna orientation and polarization):
Antenna elements are V/H polarized.
The antenna orientation at the UE is set such that the main-lobe of the antenna radiation pattern (broad side of the array) aligns to the strongest cluster direction, which is the LOS direction in LOS scenarios..

## Slide 11: Annex A: Channel model 2 parameters proposal
UE speed and direction:
  UE velocity direction is chosen to be exactly opposite to the direction of arrival (DoA) of the strongest cluster of the chosen CDL table. The strongest cluster is chosen based on the cluster power. For the LOS CDL channel models, the UE velocity direction is chosen based on the LOS DoA. This ensures the maximum Doppler shift for the strongest cluster.
Model | Scenario | Speed km/h
CDL-A | UMi O2I NLOS | 3
CDL-B | UMi NLOS | 30
CDL-C | Indoor NLOS | 3
CDL-D | Indoor LOS | 3
CDL-E | UMi LOS | 30

## Slide 12: Annex A: Channel model 2 parameters proposal
Tx/Rx beam selection procedure between emulated gNB and emulated UE antenna:
  Beam is always pointed to the strongest directions. This is the antenna array broad side direction at both Tx and Rx, because the arrays are oriented to the the strongest cluster direction.
Carrier Frequency: 28 GHz

## Slide 13: Annex A: Channel model 2 parameters proposal
MIMO correlation:
  Option 1 (Based on initial phases and XPR)
    Use the ratio of the first highest eigen value to the next highest eigen value of the channel correlation matrix of the cluster with the strongest power as the metric to define low, medium and high MIMO correlations for generating the channel model using option2.
    Define different MIMO correlations as below for generating the channel model using option2:
    Initial phases and XPR for different correlations can be found in R4-1808797.
  Option 2: Based K Ricean factors
    Ricean K-factor can be specified also for the NLOS scenarios, for purposes of modifying the MIMO correlation.