## Slide 1: Discussion on handling of PRD21 v120
CMCC, Ericsson, Huawei, Hisilicon, Keysight
3GPP TSG-RAN5 Meeting #96-e R5-225269
Electronic Meeting, Aug 15 – 26, 2022

## Slide 2: More Rel-17 WIs need to be introduced into PRD21 v120
Observation 1: There were 8 5G NR WIs impacting 5G NR bands or CADC configs have been introduced at RAN5#95e.
 | UIC | 3GPP Work Item Name
5G NR feature specific WIs | 960071 | UE Conformance - 4Rx support for NR band n8
 | 960073 | UE Conformance - Introduction of DL 1024QAM for NR frequency range 1 (FR1)
 | 960080 | NR support for high speed train scenario in frequency range 2 (FR2)Remark:n257, n258, n261
 | 960083 | UE Conformance - NR Sidelink Relay
 | 960084 | UE Conformance - NR Sidelink enhancement
 | 960088 | UE Conformance - Introduction of UE TRP (Total Radiated Power) and TRS (Total Radiated Sensitivity) requirements and test methodologies for FR1 (NR SA and EN-DC) Remark: n41, n28, n78, and n79
 | 960090 | RF requirements enhancement for NR frequency range 1 (FR1)
5G NR High Power band WI | 960070 | UE Conformance - High power UE (power class 2) for one NR FDD bandRemark: n1 and n3
Proposal 1: In PRD21 v120, to add the 5G NR feature specific WIs (UIC=960071, 960073, 960080, 960083, 960084, 960088, 960090) into the table of Section 4.3, and to add the 5G NR High Power band WI (UIC=960070) into the table of Section 4.4.
Notes: any configuration specific change requests to Chapter 5 ONLY shall NOT be accepted by RAN5

## Slide 3: How to handle the SUL/SDL bands in PRD21
Observation 2: From technical point of view, in RAN5 spec, the test cases for SUL/SDL band can not be defined alone and have to be defined by using the corresponding SUL/SDL configs.
Proposal 2: For the SUL/SDL bands, the test cases need to be defined and implemented by using the corresponding SUL/SDL band configurations. Once the SUL/SDL band configurations to be assigned with “Interested Operator”, the corresponding SUL/SDL bands shall be assigned with the same “Interested Operator” and shall be set as “Ongoing” in the PRD21 5G NR CADC list.
Notes: any configuration specific change requests to Chapter 5 ONLY shall NOT be accepted by RAN5

## Slide 4: How to handle non-optional maximum CBW extension in PRD21
Observation 3: In PRD21 v110, 90 and 100MHz CBW are pending for n40. However, in 38.508-1, by default, the highest test channel BW required for n40 is 100MHz.
Proposal 3: Considering almost all the CBWs are/will be mandatory for single NR bands, all the CBWs of the “Ongoing” NR bands are encouraged to be defined in RAN5 specifications.
For the newly introduced CBW extension of the “Ongoing” NR bands, its status shall be set as “Ongoing (CBW)” in the PRD21 5G NR CADC list even if without “Interested Operator”.

## Slide 5: How to handle V2X bands/configs. in PRD21
Observation 4: How to handle V2X bands and configs is not addressed in PRD 21 v110 [1]. Sometimes the V2X operation works under pure PC5 mode, which means no interoperation with the network. So operators might not be interested in these scenarios. If the same “Ongoing configuration” definition to be kept, some V2X bands/configurations might be kept ”Pending” since no operator interest is shown in RAN5.
Proposal 4: Considering V2X industry might be also driven by terminal vendors, it is proposed to update “Ongoing configuration” definition to having at least one ‘Interested company’ for both V2X bands and V2X configurations. And to introduce Section 5.5 “5G NR V2X bands worksheet” and Section 5.6 “5G NR V2X Configurations worksheet” into PRD21 v120.
Notes: any configuration specific change requests to Chapter 5 ONLY shall NOT be accepted by RAN5

## Slide 6: Reference
[1] PRD21 NR bands and 5G NR CADC configuration handling in RAN5 (Release 15 and later releases) v1.1.0 (2022-6).
Notes: (2022-3)

## Slide 7: Thank you!