## Slide 1: RAN5#97 TTCN sidebar Wednesday 16th November 2022
Olivier Genoud
Task Force 160 Leader, 3GPP MCC

## Slide 2
MCX:
  Corrections to MCVideo Transmission Control Messages.
Rel-16 5G V2X: Test Model and ASP updates:
  Layer2 Test Models,
  Timing ASP updates,
  New MMI.
Rel-17 baseline upgrade follow-up:
  Corrections to 5GC NAS type definitions,
  R5s221246(R&S): Symbol related issue.
Rel-17 RedCap:
  Handling of RedCap dedicated LCIDs for UL CCCH/CCCH1.
Misc.:
  R5s221287(R&S): AT/MMI command issue.
  iwd-22wk43 and new test case verification.
Agenda

## Slide 3
Corrections to MCVideo Transmission Control Messages:
  R5w220XXX_MCX_RAN5#97_TTCN_Sidebar.docx
MCX

## Slide 4
Layer2 Test Models:
  R5-226039r1 + ‘38.523-3 V2X diff AnnexD r1.docx’
Timing ASP updates:
  R5-226039r1 + ‘38.523-3 V2X diff AnnexD r1.docx’ + ‘36.523-3 V2X diff AnnexD r1.docx’
New MMI:
  R5-226039r1
Rel-16 5G V2X:
Test Model and ASP updates

## Slide 5: Corrections to NG NAS Type Definitions
(blue text is deleted, red text is added)
type record ExtdRejectedNSSAI : The IE should consist of a list of either Type 0 or 1 elements, not a single list of either type 0 or 1 elements. Both of these type 0 or type 1 elements also contain a list of XtdRejectedS_NSSAI
From | To
type union PartialXtdRejectedNSSAI { PartialXtdRejectedNSSAIType0List type0List, PartialXtdRejectedNSSAIType1List type1List }; type record of PartialXtdRejectedNSSAIType0 PartialXtdRejectedNSSAIType0List; type record of PartialXtdRejectedNSSAIType1 PartialXtdRejectedNSSAIType1List; type record PartialXtdRejectedNSSAIType0 { B1_Type spare, B3_Type typeOfList ('000’B), B4_Type numOfElements, XtdRejectedS_NSSAI rejectS_NSSAI }; type record PartialXtdRejectedNSSAIType1 { B1_Type spare, B3_Type typeOfList ('001’B), B4_Type numOfElements, O1_Type backOffTimerValue, XtdRejectedS_NSSAI rejectS_NSSAI }; type record ExtdRejectedNSSAI { IEI8_Type iei optional, Type4Length_Type iel, PartialXtdRejectedNSSAI partialXtd }; | type union PartialXtdRejectedNSSAI { PartialXtdRejectedNSSAIType0 type0, PartialXtdRejectedNSSAIType1 type1 }; type record of PartialXtdRejectedNSSAI PartialXtdRejectedNSSAIList; type record PartialXtdRejectedNSSAIType0 { B1_Type spare, B3_Type typeOfList ('000’B), B4_Type numOfElements, record of XtdRejectedS_NSSAI rejectS_NSSAI }; type record PartialXtdRejectedNSSAIType1 { B1_Type spare, B3_Type typeOfList ('001’B), B4_Type numOfElements, O1_Type backOffTimerValue, record of XtdRejectedS_NSSAI rejectS_NSSAI }; type record ExtdRejectedNSSAI { IEI8_Type iei optional, Type4Length_Type iel, PartialXtdRejectedNSSAI_List partialXtdList };
Notes: CRs adding IE: C1-192789 (Rel-15), C1-192790 (Rel-16)
CR correcting this: C1-210740

## Slide 6: Updates to NG_NAS_TypeDefs
type record PEIPS_AssistIE :
type record MBSSessionInfo :
type record MBSSessionInfo { /* 24.501 cl 9.11.4.30 */
B4_Type spareBits,
B2_Type operation,
B2_Type typeOfSessionId,
octetstring sessionId
};
type record NG_UE_SM_Cap :
type record NG_UE_SM_Cap { // 24.501 cl. 9.11.4.1
IEI8_Type iei optional, /* present in case of TLV; omit in case of LV */
Type4Length_Type iel optional, /* present in case of LV or TLV; omit in case of V */
B1_Type tpmic, /* Sep20 @sic R5s201387 Baseline Moving sic@ */
B4_Type atsssST, /* Sep20 @sic R5s201387 Baseline Moving sic@ */
B1_Type ept_S1, /* Sep20 @sic R5s201387 Baseline Moving sic@ */
B1_Type mh6_PDU,
B1_Type rQoS,
B7_Type spareBits optional,
B1_Type apmqf optional, /* Sep22 @sic R5s221179 Baseline Moving sic@ */
octetstring spare length (1..11) optional // @sic R5w190307 sic@
};
From | To
type record PEIPS_AssistIE { B3_Type typeOfInfo, B4_Type peipsValue // equals paging subgroup id if typeOfInfo = 0 // equals UE paging probability info if typeOfInfo = 1 }; | type record PEIPS_AssistIE { B3_Type typeOfInfo, B5_Type peipsValue // equals paging subgroup id if typeOfInfo = 0 // equals UE paging probability info if typeOfInfo = 1 };

## Slide 7
Handling of RedCap dedicated LCIDs for UL CCCH/CCCH1:
  R5w220XXX_RedCap_RAN5#97_TTCN_Sidebar.docx.
Rel-17 RedCap