## Slide 1: Discussion on simplification for inter-band 2UL co-existence test
ZTE Corporation
3GPP TSG-RAN5 Meeting #99 R5-233205 Incheon, South Korea, May 22– 26, 2023

## Slide 2: Simplification on 2UL inter-band CA co-existence requirements
Background:
For the efforts on improving the efficiency to specify band combinations and enhancing the quality of technical specifications, 3GPP has initiated a Rel-18 SI to study on the simplification of band combination specifications for NR and LTE [1].
In RAN4#104-e meeting, a proposal in [2] initiated the discussion on how to simplify the FR1 2UL inter-band CA coexistence requirements.
The FR1 uplink inter-band CA (two bands) spurious emission for UE coexistence requirements in Table 6.5A.3.2.3-1 in TS 38.101-1 has been derived based on the requirements for single carrier operation from each constituent UL band as specified in Table 6.5.3.2-1 in TS 38.101-1.
The protected bands and frequency ranges for a band combination in principle should be specified based on the intersection set from each constituent band coexistence requirements.
  For example, if Band A needs to protect bands A, B, C, D, E, F, G and Band B needs to protect A, B, E, F, G, H, I, then CA_A-B only needs to protect bands A, B, E, F, G.
The requirements for inter-band CA UE coexistence requirements can be specified with a normative text as “For inter-band carrier aggregation with uplink assigned to two NR bands, the requirements are the intersection set from each constituent band coexistence requirements as specified in Table 6.5.3.2-1.” without an explicit coexistence table.
  How to handle the intersection band/ranges with different requirements from each constituent band?
  If there are exceptions not applicable to the principle of the intersection set and how to handle them in either a generic or a combination specific approach?
    Investigate whether the non-3GPP RATs protection can follow the intersection set rule or should be considered as exceptions for FR1 2UL inter-band CA coexistence requirements.
    Identify the cases where the protected bands do not follow the intersection set rule for FR1 2UL inter-band CA coexistence requirements in the current specifications and determine whether they are exceptions or errors.
References
[1] RP-222216 “Revised SID: Study on simplification of band combination specification for NR and LTE”, ZTE, RAN#97-e, September 12th – 16th, 2022
[2] R4-2212357 On FR1 2UL inter-band CA coexistence requirements , Apple, RAN4#104-e, August 15th – 26th, 2022

## Slide 3: Simplification on 2UL inter-band CA co-existence requirements
Agreements in RAN4:
In RAN4#105 meeting, the following agreements have been achieved:
Extend the scope of these simplifications to include all specifications that have 2-band uplink CA/DC coexistence requirements
  To include FR1 CA/DC cases in TS 38.101-1.
  To include FR1 EN-DC / NE-DC cases in TS 38.101-3.
  To include LTE CA cases in TS 36.101.
About non-3GPP RATs protection.
  It is confirmed that non-3GPP RAT does not follow the intersection set rule.

## Slide 4: Simplification on 2UL inter-band CA co-existence requirements
Current status for LTE in RAN4:
In RAN4#106 meeting, based on the agreements on LTE cases, companies believe that single carrier testing mostly guarantees the performance in band combination due to intersection rule. 3 CRs starting from Rel-16 for LTE were agreed for simplify the inter-band CA co-existence table.
  Requirements which are expressed as frequency range are kept with an exception that if such requirement is due to close proximity of two bands, those can also be removed as single band case is more stringent.
  For example, for CA_1-5, the frequency range 859-869 MHz is kept, and other requirements are removed.
References
[1] R4-2300398 LTE interband 2UL CA co-ex simplication R16 Nokia
[2] R4-2300399 LTE interband 2UL CA co-ex simplication R17 Nokia
[3] R4-2300400 LTE interband 2UL CA co-ex simplication R18 Nokia

## Slide 5: Simplification on 2UL inter-band CA co-existence requirements
Current status for NR in RAN4:
In RAN4#106bis-e meeting, a tentative agreement was achieved as below. The CRs for NR are postponed to RAN4#107 meeting.

## Slide 6: Simplification on 2UL inter-band CA co-existence requirements
Proposed actions in RAN5:
Proposal 1 It is proposed to take the above RAN4 progress on inter-band co-existence simplification into consideration and start the simplification work on 2UL inter-band co-existence test in RAN5.
Question 1 NR test vs. LTE test?
  Only apply to NR configurations? Or
  Apply to both NR and LTE configurations?
Question 2 New test cases vs. all test cases?
  Only apply to newly introduced test cases? Or
  Apply to all test cases including the completed test cases?

## Slide 7: Thank you!