## Slide 1: Simplification on test frequencies for inter-band EN-DC band combinations with more than three bands
ZTE Corporation
3GPP TSG-RAN5 Meeting #108 R5-254310
Bengaluru, India, August 25 – 29, 2025

## Slide 2: Overview on test frequencies for inter-band EN-DC band combinations
In TS 38.508-1, test frequencies are specified for bands and band combinations. For inter-band EN-DC configurations, the following guidelines apply:
For the E-UTRA band and E-UTRA CA configurations, test frequencies as specified in TS 36.508, clause 4.3.1 are used.
For the NR band and NR CA configurations, test frequencies as specified in clause 4.3.1.1 are used.
For the EN-DC inter-band configuration that includes an EN-DC contiguous configuration, the EN-DC contiguous configuration is listed in the NR configuration column and the test frequencies as specified in clause 4.3.1.4.2 are used.
For the secondary NR band in inter-band signalling test cases, the band selected is based on the subset of NR bands supported within the EN-DC configurations specified in Table 4.3.1.4.1.2-1 for NR FR1.
The following templates are applied to test frequencies for inter-band EN-DC band combinations, take three bands combination as an example:

## Slide 3: Observations on inter-band EN-DC test frequencies
Observation 1 For each inter-band EN-DC configuration, the test frequencies are categorized into different groups, each of which corresponds to an individual uplink EN-DC configuration.
Observation 2 For each inter-band EN-DC configuration, the E-UTRA/NR downlink configurations are duplicated among different test frequency groups.
Observation 3 The denotation for some E-UTRA/NR configurations in the test frequency table is incorrect, such as NR downlink configuration for DC_2A-14A_n77(2A) should be “CA_n77(2A)” instead of “n77(2A)”.
Example 1
Example 2

## Slide 4: Simplification on inter-band EN-DC test frequency table
Proposal 1 It is suggested to simplify the inter-band EN-DC test frequency table as below.
For each inter-band EN-DC configuration, remove the duplicated E-UTRA/NR downlink configurations and keep only one entry for E-UTRA/NR downlink configuration.
For E-UTRA/NR downlink or uplink configuration, if inter-band or intra-band CA is applied, the prefix “CA_” should not be omitted. If single band is applied, “xA” or “nxA” should be denoted, where “x”/”nx” is an E-UTRA/NR band number.
Proposal 2 It is suggested to simplify all the test frequencies for inter-band EN-DC configurations with more than three bands in TS 38.508-1 by using guidelines in Proposal 1.
Proposal 3 The above test frequency simplification guidelines also apply to NE-DC configurations with more than three bands.
Example 1
Example 2

## Slide 5: Thank you!