## Slide 1: NR FR2 WF on MB relaxation
Apple, Inc.
3GPP TSG-RAN WG5 Meeting #83 R5-194122r1
Reno, USA, 13th May 2019 - 17th May 2019
Agenda Item : 5.3.5.17
Document for : Discussion and Endorsement

## Slide 2: Agreements / Assumptions
Based on RAN4 LS (R5-192901), RAN5 applies MB relaxation into conformance test with following assumptions except for verdict for certification / validation.
  MB relaxation value for each FR2 band are based on “UE declaration”.
  “Verdict per band”, which is same approach as legacy LTE.
Time plan
  Pre meeting discussions : 1) Proposed approach to remaining issues, 2) Raise additional issues
  [RAN5#83] (May-2019): CR implementation to reflect agreements in this WF, Completion target of MB relaxation except for MU, TT
Process of UE declaration (Definition of verdict is TBD.)
  UE manufacturers declare each MB relaxation value to satisfy core requirement.
  Test houses, labs implement declared value into TE by manual since there is no capability for this relaxation.
  TE concludes verdict considering implemented declared value.

## Slide 3: Remaining issues [1/3]
UE declaration
  1-1 How to declare MB relaxation value
    Agreement: TS 38.522
    1-2 Whether declared value can be updated
    Agreement: UE declared value shall not be updated.
  Definition of Verdict
    Whether testing all FR2 bands at the same time with same TE is required?
    Agreement: Not required to use same TE. UE needs to report the same MB Relaxation values for all supported bands. UE declared value shall not be updated. Recommend certified bodies to cross check with other certification body organizations. Final decision can be up to certification body.
MU, TT, SNR estimation
  3-1 Whether MUMB = MUSB for each TC. Agreement: MUMB = MUSB
  3-2 Whether TTMB = TTSB for each TC. Agreement: TTMB = TTSB
  3-3 Whether SNR estimation is required for MB TCs (or estimation of SB can be resued to MB TCs) Agreement: No

## Slide 4: Remaining issues [2/3]
Spec structure
4-1 Test applicability for each TC (TC without MB relaxation and TC with MB relaxation)
Agreement: Single Test Case
4-2 Test procedure for MB should be updated. Whether following points to be captured in the procedure.
1) Process of UE declaration
2) Process of implementing declared value into TE
3) Other
Agreement: Add the note to declare MB value per band in MB relaxation table 6.2.1.2.5-3.
Note 1: MR is the multiband relaxation value declared by the UE for the tested band in table TBD of TS 38.522. This declaration shall fulfill the requirements in clause 6.2.1.1.3.3
Note 2: For a multi-band UE, the final verdict of this test cannot be assigned until all the declared bands have been tested unless ΔMB = 0 for all bands
Note 3: For a single band UE, ΔMB is zero.
4-3 Description of test requirement
How to apply MB relaxation into test requirement. (e.g. 22.4 – TT – MB)?
Agreement: 22.4 - TT - ΔMB
4-4 Whether additional TCs for MB relaxation are required except for TCs captured in the latest WP - MOP (EIRP, TRP, SC), MPR, A-MPR, configured output power, [ACLR?]…
Agreement: Any Test Cases that require power measurement of Min Peak EIRP and Spherical Coverage

## Slide 5: Remaining issues [3/3]
TE Implementation
5-1 Whether should discuss this topic in RAN5 (or this topic should be TE implementation matter.)
Agreement: Not Applicable. MB values should be recorded by certified body.
5-2 Necessity to capture supporting FR2 bands and declared relaxation value for all FR2 bands.
[E.g.] UE supports 3 FR2 bands (n257, n260, n261), and conduct n257 testing.
TC : MOP (Spherical Coverage, MB FR2 bands)
Verdict : PASS (Band n257)
Declared relaxation value : 0.3 dB (n257), 0.1 dB (n260), 1.0dB (n261)
Agreement: Not Applicable.
Certification/Validation
6-1 After completion of RAN5 work, it is required to send LS to certification bodies (e.g. GCF CAG, PTCRB).
Agreement:
1. For certification, UE declares all supported bands to certification body
2. Option 2.1 For certification, UE needs to report the same MB relaxation values for all supported bands to all certification bodies
Option 2.2 Certification body requires to test all support bands
3. For certification, UE requires to pass all declared supported bands.
4. For certification, verdict shall be per band for all UE declared support bands under two conditions:
- Option 1 All the declared bands shall be tested.
- Option 2 All the bands shall be tested.
- The sum of ΔMBP,n and ΔMBS,n per band satisfy the ∑MBP (dB) and ∑MBS (dB) according to Table 6.2.1.3-4 in 38.521-2.
5. UE declared value shall not be updated.
6. Test platform validation shall be done per band basis