## Slide 1
Discussion of work split for studying of AI traffic characteristic
China Mobile, OPPO, CATT, Huawei, ZTE
© 3GPP 2025

## Slide 2: Background of AI traffic characteristic
In the LS of R1-2508184, RAN 1 has agreed to study traffic model(s) for 6GR AI/ML services, and send LS to SA4 (cc RAN2, SA1, SA2) requesting input if any on traffic characteristics for AI/ML services.
SA4 has already provide the LS reply in S4-252135, that to clarify:
  SA4 recognizes the importance of defining traffic models reflecting realistic traffic characteristics. SA4 will provide input as it further progresses the work for AI/ML Services and immersive communication services.
  And also SA4 provides some of the materials that SA4 has done some of the studies for example defining a traffic model for AI/ML in R20.

## Slide 3: SA1 has already kick off the AI traffic related study
In SA1, some of the agreed PRs are related to AI traffic requirements. These requirements focus on AI inference or training related requirements, not for AI media traffic.
Traffic Type | Burst size | Max Allowed latency for a burst(note) | Service bit rate: user-experienced data rate | Delay(note) | Average packet size
Image based GenAI app | 400 KB | 50 ms | 64 Mbps | 20 ms | > 800B
Video based GenAI app | 20 MB | 400 ms | 400 Mbps | 20 ms | > 800B
chatbot | 0.5 KB | 20 ms | 200 Kbps | 30 ms | < 800B
Note: meanings of some KPIs: max allowed latency for a burst: max latency for sending out the whole packets within a burst delay: transmission latency of a packet |  |  |  |  | 
[PR 6.26.6-1] 6G system shall provide efficient QoS assurance mechanisms for different types of application traffic, with the KPI summarized below:
Table 6.26.6-1: Required KPIs for GenAI applications
[PR 6.26.6-2] Subject to operator’s policy, agreement with authorized 3rd party and user consent, 6G network shall be able to be aware of the burst characteristics (e.g. Burst Data Rate) in traffic and provide mechanisms to optimize resource efficiency and assure user experience when handling such traffic.
[PR 6.52.6-3] Subject to operator’s policy, the 6G network shall be able to support dynamic QoS needed for a group of UEs (e.g. multiple robots or third party AI Agents) when traffic characteristics change is predicted to occur or has occurred (e.g. change between AI/ML model transfer and AI/ML inference result transfer).
Some of the agreed PRs are dedicated related to AI media traffic requirements, such as image or video, see below.
Observation 1: SA1 has already start AI traffic characteristic study, including both general AI traffic characteristic and AI media traffic requirements.

## Slide 4: Experience in 5G
In 5G, there are some cooperation examples.
R18 XRM:
  SA2 coordinates with SA4 to standardize PDU set related mechanism in R18, and during SA2 study, SA2 firstly study the end of data burst feature, and cooperation with SA4 to define the IE of end of data burst.
R18 AIML:
  In SA1, there is requirements of split AI/ML operation between AI/ML endpoints and some of KPI table of AIML traffic are provided. And also in SA2, the new Standardized 5QI to QoS characteristics mapping of AIML traffic is determined by SA2.
Observation 2: In 5G, the different WGs are cooperated through LSs. And SA2 can study the AIML traffic related features based on SA1 requirement. SA2 and SA4 are cooperated through LSs, e.g., XRM traffic.

## Slide 5: Way forward and Proposal
  Observation 1: SA1 has already start AI traffic characteristic study, including both general AI traffic characteristic and AI media traffic requirements.
  Observation 2: In 5G, the different WGs are cooperated through LSs. And SA2 can study the AIML traffic related features based on SA1 requirement. SA2 and SA4 are cooperated through LSs, e.g., XRM traffic.
  Proposal: SA2 can start some work based on SA1 requirement. And during the 3GPP work, SA2 is responsible for the architecture and functionality design for AI traffic, and SA4 is responsible for AI media traffic feature related study.