## Slide 1: NFV impacts on 3GPP Agenda Item 5.2
Alcatel-lucent 5th MARCH 2014
3GPP TSG SA meeting#63, March 5-7 2014, Fukuoka, Japan SP-140123

## Slide 2: What is Network Function Virtualization
Evolution of network functions implementation to leverage IT virtualization techniques
  Today’s approach to network function delivery is monolithic
    Closed, proprietary with a tightly-integrated vertical stack
Network functions are implemented as software running on industry-standard IT infrastructure
  Using a shared common and programmable computing, switching and storage infrastructure
  Functions can be moved to, or instantiated in, various locations in the network as required, without the need to physically move or install new hardware equipment
  Function layer and platform layer can scale and evolve more independently
The new Virtualized-functions –based Network scenario

## Slide 3
Static, fixed systems
Dedicated HW platforms per service
Siloed, large, operational teams
OPEX-heavy
More Complex capacity planning/scaling
Slower time-to-market
Dynamic, elastic, software-like
Single platform for compute focused services
Unified, lighter operations teams
OPEX-light
Simpler planning and scaling
Agile, faster time-to-market
Operational resource
RAN
CDN
OSS BSS
Enterprise services
Mobile core
CDN
IMS
RAN
CDN
IMS
Mobile core
OSS BSS
Enterprise services
NFV Platform
Simple general purpose programmable networking
Operational resource
Physical Network
VIRTUAL Network
Functions run as applications
Virtual Networking Moving towards Cloud-based Operations Model

## Slide 4: Is NFV just cloud computing?
NFV can be considered as an application of cloud computing
In essence, NFV is running the network functions in a private cloud
For a communications service provider, NFV has a different focus than cloud computing
Cloud computing is about providing IT services
    Carrier cloud combines network connectivity services with IaaS, PaaS and SaaS
  NFV is about new ways of delivering network services
    Reducing costs
    Increasing agility
    Fostering innovation
NFV adds specific constraints driven by network functions:
  Reliability, guaranteeing the right level of availability (e.g., 5 9’s)
  Performance
  Networking, guaranteeing the specific constraints of the network function in terms of bandwidth, latency, and QoS
  Openness and ease of integration to support multi-vendor applications within a single environment

## Slide 5
  CLOUD NETWORK VISION Three Pillars of the Future Network
  Flexible Virtualized Network Functions running on an IT infrastructure (augmented by high performance dedicated functions as appropriate)
  End to end automated cloud management, maximizing flexibility and efficiency of applications
  SDN, to enable dynamic consumption and programmability of the underlying DC network and transport infrastructure
MASSIVE PARADIGM SHIFT FROM CLOSED, STATIC CONFIGURATION TO OPEN, DYNAMIC ADAPTATION
  Open, distributed cloud infrastructure
  Cloud services & capabilities
  Cloud intelligence & control
SDN
Cloud Orchestration & Automation
Network Virtualization & Automation
  Customers
IT and Application Services
Virtualized Network Functions
Network Controlling Applications
  MAN/WAN
  Enterprise DC
  Network DC
1
2
3
3GPP TSG SA meeting#63, March 5-7 2014, Fukuoka, Japan SP-140123

## Slide 6: 3GPP And NFV : combining functional entities?
3GPP functions normally are mapped to dedicated physical network nodes.
  There is no requirement however in 3GPP specifications to do so. Potential combination of functions have been present in the market for many years.
Exploring combination of current 3GPP function in NFV environment
  This should driven by market requirements and related cost benefit analysis
  “ Functions combination” profiles driven by NFV implementation assumptions should be subject to study in 3GPP so full interoperability, resiliency, scalability and functionality is kept

## Slide 7: 3GPP And NFV : Splitting functional entities?
  Splitting baseband processing and RF processing of base stations
  already happening by using existing industry standards.
    This is largely seen as in implementation effort.
  Splitting other entities into separately purchasable software modules has been considered in NFV
  This activity does not apply to 3GPP if this is not resulting in the definition of open interfaces that are abstract from specific implementation choices (in principle they may result in non virtualized implementations too!)
  Any such split decision should be subject to study in 3GPP

## Slide 8: 3GPP And NFV : Protocol aspects
  Depending on load balancing implementations, cardinality of functions at the two sides of an open interface may change with NFV introduction
  Impacts on protocols to e.g. improve load balancing of virtual functions could be considered as part of activities in stage 3 groups
    relying on internal load balancing proprietary methods is an alternative but this may require additional costs in terms of state maintenance

## Slide 9: NFV and SA5 Work
The MANO group in ETSI-NFV is looking into use cases and requirements particularly related to management of NFV.
3GPP SA5 has been defining the interface and data model over the Itf-N for management of 3GPP-based networks (see next slide).
    Between the Element Manager (EM) and the Network Manager (NM) of a single 3GPP network
    Between the Network Managers (NMs) of a single 3GPP network
  The changes needed to management and orchestration functionality to support the NFV in 3GPP need to be studied.

## Slide 10: 3GPP Management Reference Model (TS 32.101)
1: Between the Network Elements (NEs) and the Element Manager (EM) of a single broadband wireless network
2: Between the Element Manager (EM) and the Network Manager (NM) of a single broadband wireless network
3: Between the Network Managers and the Enterprise Systems of a single broadband wireless network
4: Between the Network Managers (NMs) of a single broadband wireless network
4a: Between the Domain Managers (DMs) of a single broadband wireless network
5: Between Enterprise Systems & Network Managers of different broadband wireless networks
5a: Between the Domain Managers (DMs) of different broadband wireless networks
6: Between Network Elements (NEs)
3GPP Management Standards Focus

## Slide 11: NFV and SA5 Work: proposed focus of study
Detailed use case study is necessary to understand the impact of supporting management of NFV while supporting legacy (non NFV) systems.
  Operators require a smooth transition from existing style of management into managing Virtualized functions.
The study should focus on the following
    Identify use cases for management of virtualized network functions in 3GPP
    Study operational impacts as a result of virtualizing 3GPP network functions and changes in operational models.
    Study the impact on existing 3GPP specifications and identify enhancement needed (if any)
    Identify use cases that impact call trace, MDT, SON, performance collection as a result of 3GPP network functions virtualization
    Determine if there are additional enhancements to areas like MDT, Call Trace, Performance Measurements needed to accommodate 3GPP network functions virtualization
    Provide recommendations for the standardization of management of virtualized 3GPP network functions.
We strongly suggests that SA5 member companies take into account all the use cases and requirements provided by ETSI-NFV and study those in the context of the scope and mandate of SA5.
We would also like to see close co-operation with the ETSI-NFV MANO group.

## Slide 12: Wrap up
Virtualization of 3GPP Network functions is an important market requirement and this is being met.
3GPP can start with the study of the OAM impacts of introduction of NFV in 3GPP networks
It may be necessary to identify any protocol impacts
There seems to be no short-medium term need to change the current 3GPP architecture or functions allocations to logical entities.
  Any longer term evolution of the architecture may be part of experience gathered by NFV field deployments