## Slide 1
Allot Communications, China Mobile, China Unicom, KDDI, China Telecom, Rogers Communications, Orange, Softbank Mobile, IAESI, Comverse, Sandvine Incorporated, Oracle Corporation, Openet Telecom, Broadcom Corporation, CATR, Intel, ZTE, CATT
SA WG2 Prioritization
of FMSS
3GPP TSG SA Meeting #66 SP-140660
Maui, US; 10th – 12th December 2014

## Slide 2: Background
Companies are asked to contribute on outlining their top priority items for Release 13.

## Slide 3: FMSS (Flexible Mobile Service Steering) WID Details
SA1 WID completion: September 2014
  Resulted in the new section 30 of the TS 22.101 on Flexible Mobile Service Steering (FMSS)
    The 3GPP Core Network shall be able to define and modify traffic steering policies that are used to steer traffic in (S)Gi-LAN e.g. to improve e.g. the user’s QoE, apply the bandwidth limitation and provide valued added services.
    The 3GPP Core Network shall be able to define different traffic steering policies for a user’s traffic on a per session basis (e.g. for applying parental control, anti-malware, DDoS protection, video optimization).
    The 3GPP Core Network defines traffic steering policies based on one or more pieces of information such as network operator’s policies, application characteristics, and user’s subscription

## Slide 4: FMSS (Flexible Mobile Service Steering) WID Details
SA2 WID
  The objective in Stage 2 is to meet the service requirements defined in Stage 1, i.e., specify how the 3GPP core network provides policies for mobile service steering in the (S)Gi-LAN.
    Service enablers supported within the (S)Gi-LAN and the routing of traffic between those service enablers are out of this work item scope. The work item scope is restricted to providing policies through interfaces defined by 3GPP.
  Status of SA2 work:
    Skeleton and scope have been agreed
    Architecture assumptions on policy generation by PCRF have been agreed
    2 key issues on interface for providing a policies and semantics of such an interface have been agreed

## Slide 5: SA2 Milestones to achieve
Complete architecture assumptions and key issues
Define solutions
Perform evaluation and conclusions
Standardize according to conclusions

## Slide 6: Things to consider
There is a very big number of WID supporting companies
There is ongoing work on service steering (chaining) currently in IETF, BBF, ETSI NFV
The results of this work in 3GPP may have significant impact on the corresponding work in other fora, thus it is beneficial to complete it as soon as possible
LS from CCSA (SP-140450) was received at SA#65 asking us to standardize this feature in R-13 as highly demanded
Though FMSS is handled under SA2 “Other Track”, this track is also slightly overloaded and require prioritization of topics

## Slide 7: Summary
The cosigning companies believe FMSS Work Item should be given high priority in SA2 group

## Slide 8
Thanks.
For questions please contact:
  Alla Goldner, agoldner@allot.com, +972542493985
  Allot Communications