## Slide 1
ETSI STANDARDS FOR ENERGY EFFICIENCY and considerations on current EE work in TSG SA
3GPP TSG SA Meeting #73 TD SP-160684
New Orleans, Louisiana, USA, 21-23 September 2016
Agenda Item: 16P.1
WI: FS_ENEFF

## Slide 2: Outline
Overview of ETSI standards for energy efficiency of mobile networks
Considerations on current 21.866
Conclusions and possible way forward

## Slide 3: ETSI standard ES 202 706 “Measurement method for power consumption and energy efficiency of wireless access network equipment” (1/2)
V.1.4.1 published on December 2014
It defines methods for power consumption and energy efficiency of base stations in static and dynamic modes.
It includes:
  Reference configurations and measurement conditions
  Static power consumption measurement (under low, medium, busy hour load)
    Calculation of average static power consumption for integrated base stations
    Calculation of average static power consumption for distributed base stations (i.e. with RRH)
    Measurement method for static base station power consumption
  Dynamic base station energy efficiency measurement (dynamic traffic sourced from a certain coverage area)
    Test setup for dynamic energy efficiency measurment
    Capacity test procedure
    Coverage efficiency test procedure

## Slide 4: ETSI standard ES 202 706 “Measurement method for power consumption and energy efficiency of wireless access network equipment” (2/2)
New version of this standard will be in two parts:
  ES 202 706-1 “Metrics and Measurement Method for Energy Efficiency of Wireless Access Network Equipment Part 1: Power Consumption - Static Measurement Method”
    This revision includes clarifications
  ES 202 706-2 “Metrics and Measurement Method for Energy Efficiency of Wireless Access Network Equipment Part 2: Energy Efficiency - Dynamic measurement method”
    This version will provide improvements in the dynamic measurement method in terms of new traffic model, channel model, using User Equipment emulator in the test setup and remove the complexity of the current method.
    Updates of the document will also support the ongoing harmonization process with ATIS standard

## Slide 5: ETSI standard ES 203 228 “Assessment of mobile network energy efficiency” (1/3)
V.1.1.2 published on January 2016
It defines:
  Energy consumption metrics (all equipment in the network)
  Performance metrics (traffic volume with a defined quality of service)
  Energy efficiency metric (ratio of performance and energy consumption)
  Measurement method
  Assessment report content
The standard deals with both a homogeneous and heterogeneous networks (GSM, UMTS, LTE-LTE/A) considering networks whose size and scale could be defined by
  topology (a possible example a control node, its supported access nodes as well as the related network elements)
  geography (city-wide, national or continental networks)
  demographics (urban or rural networks)

## Slide 6: ETSI standard ES 203 228 “Assessment of mobile network energy efficiency” (2/3)

## Slide 7: ETSI standard ES 203 228 “Assessment of mobile network energy efficiency” (3/3)
Example without any reference to actual networks
Hypothesis of 2 weeks measurement in a network with a hypothetical demography distribution as in column 2; weighted measurement of the “available” sub-networks

## Slide 8: ETSI TC-EE Work Item DEN/EE-EEPS25 “Energy Efficiency measurement methodology and KPI/metrics for RAN equipment”
New Work Item just started
This is under the frame of EU mandate M/462 on “Standardisation mandate addressed to CEN, CENELEC and ETSI in the field of ICT to enable efficient energy use in fixed and mobile information and communication networks”
This work item will define Energy Efficiency KPIs for RAN Equipment for different technologies and relevant processes to perform measurement and manage the KPI calculation.
The document will be based on the related specifications in ETSI TC-EE (e.g. ES 202 706-x).
The work will be done in liaison with other SDOs e.g. 3GPP.

## Slide 9: ETSI standard ES 201 554 “Measurement method for Energy efficiency of Mobile Core network and Radio Access Control equipment”
V.1.2.1 published on July 2014
It defines metrics and measurement methods for systems and nodes defined in TS 123 002:
  Mobile core functions (GGSN, HLR, MGW, MME, MSC, SGSN and PGW/SGW).
  Radio Access Controller (RNC).
It includes:
  Definition of Power consumption and metrics for Core networks
  Measurement conditions and procedures

## Slide 10: ETSI standard ES 202 336-12 “Monitoring and control interface for infrastructure equipment; Part 12: ICT equipment power, energy and environmental parameters monitoring information model”
V.1.1.1 published on June 2015
It defines measurement and monitoring of power, energy and environmental parameters for ICT equipment in telecommunications or datacenter or customer premises.
It includes:
  ICT power, energy and environmental parameters monitoring system
  Power/Energy metering data analysis services
  Monitoring / supervision information and functions

## Slide 11: TR 21.866 draft V0.1.0 (2016-06)
This TR defines:
  3GPP System Energy Efficiency Requirements and Principles (High Level Requirements, Architectural Requirements, Functional Requirements, Energy Efficiency Control Principles))
  Energy efficiency KPIs
  Potential solutions for energy efficiency improvement ( 1)Energy efficiency in SON, 2) Extended range of normal operating conditions)
The references of this TR are:
  ETSI ES 202 706 "Environmental Engineering (EE); Measurement method for power consumption and energy efficiency of wireless access network equipment”
  ETSI ES 203 228 "Environmental Engineering (EE); Assessment of mobile network energy efficiency".
  ETSI ES 201 554 "Measurement method for Energy efficiency of Mobile Core network and Radio Access Control equipment”
KPIs in this TR are derived from the above ETSI standards

## Slide 12: Considerations on TR 21.866
It would be useful if the TR focused on a Gap analysis with what is available today
If 3GPP needs to define other KPIs for enegy efficiency that are not in the ETSI standards, it would be appropriate that 3GPP will send a liaison to ETSI TC-EE
About the solutions for energy efficiency improvement:
  Solution with SON functionality: ETSI TC-EE has not defined this aspect, but SA5 seems the right forum for this
  Solution with extended range of normal operatin conditions: the increase of the range of air temperature/humidity in base stations and core network nodes can have a negative impact on the product reliability aspect. Products are designed to operate within the limits defined in the climatogram of the reference environmental standards (e.g. EN 300 019 series) but this means that products conforming to a specific environmental class shall function at all values within the boundary of the climatogram but the operating consitions within the climatogram will have different probabilities of occurrence. Reliability calculation is normally determined at the temperature/humidity conditions with higher probability of occurrence and therefore if a product will work all time at the highest temperature limits, a higher failure rate can be expected in respect to the theoretical calculation at the center of the climatogram. On this aspect, 3GPP should liaise with TC-EE that is also in charge for the environmental standards.
    We do not see it necessary to change the RAN4 spec TS 36.141 on conformance testing of base stations.

## Slide 13: What is in RAN4 spec 36.141 1/2
Normal test environment
Changing this would change test execution ranges of an uncontrolled environment of a lab, so really it will not lead to testing operation at the extremes of the ranges necessarily
  In practical terms this does not change the conformance testing in most labs we know of.
Condition | Minimum | Maximum
Barometric pressure | 86 kPa | 106 kPa
Temperature | 15C | 30C
Relative Humidity | 20 % | 85 %
Power supply | Nominal, as declared by the manufacturer | 
Vibration | Negligible | 
When a normal test environment is specified for a test, the test should be performed within the minimum and maximum limits of the conditions stated in Table D.1.
Table D.1: Limits of conditions for Normal Test Environment
The ranges of barometric pressure, temperature and humidity represent the maximum variation expected in the uncontrolled environment of a test laboratory. If it is not possible to maintain these parameters within the specified limits, the actual values shall be recorded in the test report.
NOTE: This may, for instance, be the case for measurements of radiated emissions performed on an open field test site.

## Slide 14: What is in RAN4 spec 36.141 2/2
Extreme test environment
Clearly we ought to liaise with the International Electro technical Commission if we want to do something here
  But is it really wise to do so at SA level? What would this yield other than some flurry of LSs and consultations involving potentially many industries - also we should have this driven by RAN4 (not SA plenary which does not own this spec).
D.3 Extreme test environment
The manufacturer shall declare one of the following:
  1) the equipment class for the equipment under test, as defined in the IEC 60 721-3-3 [6];
  2) the equipment class for the equipment under test, as defined in the IEC 60 721-3-4 [7];
  3) the equipment that does not comply to the mentioned classes, the relevant classes from IEC 60 721 documentation for Temperature, Humidity and Vibration shall be declared.
NOTE: Reduced functionality for conditions that fall outside of the standard operational conditions is not tested in the present document. These may be stated and tested separately.
D.3.1 Extreme temperature
When an extreme temperature test environment is specified for a test, the test shall be performed at the standard minimum and maximum operating temperatures defined by the manufacturer's declaration for the equipment under test.
Minimum temperature:
The test shall be performed with the environment test equipment and methods including the required environmental phenomena into the equipment, conforming to the test procedure of IEC 60 068-2-1 [8].
Maximum temperature:
The test shall be performed with the environmental test equipment and methods including the required environmental phenomena into the equipment, conforming to the test procedure of IEC 60 068-2-2 [9].
NOTE: It is recommended that the equipment is made fully operational prior to the equipment being taken to its lower operating temperature.

## Slide 15: Conclusions and way forward
To avoid duplication of work, take actions in 3GPP to liaise with ETSI TC-EE about KPIs for energy efficiency of mobile networks as ETSI has already done several studies in this area
  Identify gaps if any as we do so
3GPP should also consult ETSI TC-EE about the potential solution to improve the energy efficiency of mobile networks by increasing the temperature/humidity conditions as TC-EE has already published a technical report on the thermal management (see TR 102 489, clause 5.5)
  We see no need to affect RAN4 specs from SA standpoint
    Any action in this area seems to be not in our decision power in TSG SA as we have working groups experts in this area.
For the SON approach we ought to liaise with SA5
The requirements and principles documented in the TR could be considered by WGs in their design of current and future features, where applicable, effective and feasible.