## Slide 1: 3GPP TSG-SA meeting #84 SP-190516 Newport Beach, US, June 5th – 7th, 2019 Agenda Item: 3.3 Source: Ericsson Title: Nudr Sensitive Data Protection Document for: Discussion, Decision

## Slide 2: Credential Storage in 3GPP UDC Background
HLR/HSS defined as subscription Data Base for legacy NW accesses and IMS
    This includes the functionality of the Authentication Center (AuC) for the storage of the subscription credentials and generation of AKA Authentication Vectors.
However, when deploying HLR/HSS using a layered architecture, the UDR is responsible for the actual storage of subscription profiles.
    Including authentication profile as defined in UDC 3GPP TS 23.335 (Rel-9, 2010).
UDR
HLR
HSS
AuC
3GPP HSS
Ud
IMSI, Ki, SQN
SA3 reviewed security requirements for UDC and confirmed it was possible to store credentials at UDR.
HLR/HSS/UDR following the UDC concept are currently deployed in multiple markets supporting millions of subscriptions.

## Slide 3: Credential Storage in 3GPP 5GC Background
SA2 defined UDM as the Subscription Data Base for 5GC.
    Similar role and functionality to 3GPP HSS.
SA3 defined ARPF as the entity responsible for the storage of subscription credentials and generation of AVs.
    ARPF is a function similar to AuC offered by UDM.
Following UDC approach, TS 23.501 (since v15.0.0, Dec 2017) defines that.
ARPF
UDM
Nudr
SUPI, Ki, SQN
CT4 Nudr TS 29.505 (since, v15.0.0, June 2018) defined accordingly including credentials in UDR
SA3 does however not refer to UDR for any aspect of the security architecture.
  SA3 only argued against this approach while answering CT4 LS on protection of sensitive data over Nudr.
SA3 instructs CT4 and SA2 to change specifications so subscription credentials in 5GC can ONLY be stored at the ARPF.
  If applied in Rel-15, this will have several implications wrt 3GPP, deployment and operational aspects.
UDR

## Slide 4: Credential Storage in 5GC
  Rel-15 stage 2 and Nudr API frozen for 18/12 months already
    Such a significant architectural change shall not be allowed.
    Non backwards compatible changes should not be possible either unless FASMO.
3GPP Specifications missing are at least:
    AV requests for 5G enabled UEs connecting from EPC/IMS, needs to be served by ARPF.
      HSS-UDM IWK could be based on UDICOM Rel-16 but should be implementation dependent in Rel-15.
      ARPF role needs to be extended in 33.501 to also generate AVs for EPS/IMS and even 2G/3G AKA.
Possible Way Forward:
    Keep currently defined approach to allow storage of subscription credentials at UDR (Rel-15 onwards).
      Consider measures to improve security of this approach if needed.
    Allowing storage of credentials at ARPF as a new additional architectural choice to be studied and standardized.
      Consider decoupling of ARPF from UDM and definition of corresponding interface.
      Consider IWK aspects for AV retrieval from ARPF for EPC/IMS (maybe also 2G/3G) AKA.