## Slide 1: SA1 Work Items related to R17 RAN work areas
SP-190870

## Slide 2: Introduction
These slides aims to map the work done in SA1 with the RAN working areas that are currently being discussed in the context of Rel17.
Rel 17 Stage 1 freeze will be done in Dec 2019. Therefore, we also point to TR of on going studies in Rel17. Be aware requirements from TRs can still change in the normative stage.
Release 17 WI codes
NCIS - Network Controlled Interactive Service Requirements
EAV - enhancement for UAVs
MONASTERYEND - Complete Gap Analysis for Railways Mobile Communication System
eCAV - enhancements for cyber-physical control applications in vertical domains
AVPROD - Audio-Visual Service Production
ATRAC - Asset Tracking Use Cases
MUSIM - Support for Multi-USIM Devices
MINT - Support for Minimization of service Interruption
CMED - Communication Services for Critical Medical Applications
REFEC - enhanced Relays for Energy eFficiency and Extensive Coverage

## Slide 3
TS 22.261
TS 22.104
TS 22.125
AVProd
NCIS
CMED
EAV
REFEC
ATRAC
eCAV
MUSIM
MINT
MONAST…
5MBS_eMC
NR Light
Small data transfer opt
Sidelink enhancements
Multi SIM operation
NR multicast broadcast
Coverage enhancements
NR for Non Terrestrial Networks
NB-IoT and eMTC enhancements
Power saving enhancements
Positioning enhancements
Integrated Access and Backhaul enh.
Drones
XR&5G
IIoT and URLLC enh.
Slicing
MIMO enhancements
TEI & Others
TS 22.186

## Slide 4: SA1’s 5G specifications

## Slide 5: 5G SA1 Technical Specifications
TS 22.261 Service requirements for next generation new services and markets
  Possible RAN areas affected: Small data transfer optimization, SideLink enhancements, NR multicast/broadcast, Coverage enhancements, NR for Non Terrestial Networks, Positioning enhancements, Integrated Access and Backhaul enhancements, IIoT and URLLC enhancements, Slicing, XR&5G, NB-IoT and eMTC enhancements
TS 22.104 Service requirements for cyber-physical control applications in vertical domains
  Possible RAN areas affected: IIoT and URLLC enhancements, XR&5G
TS 22.125 Enhancement for Unmanned Aerial Vehicles (UAVs)
  Possible RAN areas affected: Drones
TS 22.186 Enhancement of 3GPP support for V2X scenarios
  Possible RAN areas affected: Sidelink_enhancement

## Slide 6: Release 17 SA1 WIs

## Slide 7: 5MBS_eMC: broadcast / multicast requirements supporting Mission Critical Services in 5G
Objective: | The goal of this Work Item is to add requirements for broadcast/multicast, to the existing requirements enhancing the capabilities for group communication, supporting in particular requirements for mission critical users.
Rapporteur: | Jens Toobe (BDBOS)
WI output | TS 22.261 Service requirements for next generation new services and markets
Possible RAN areas affected | NR multicast broadcast.

## Slide 8: ATRAC: Asset Tracking for 5G
Objective: | The objective includes asset tracking use cases (for example pallets, containers, crates, parcels, luggage) with the emphasis on the use cases bringing new potential requirements and new KPIs to be supported by 5G communication services.
Rapporteur: | Thierry Berisot (Novamint)
WI output | TR 22.836 Study on Asset Tracking Use Cases TS 22.261 Service requirements for next generation new services and markets
Possible RAN areas affected | NB-IoT and eMTC enhancements, NR for Non Terrestial Networks.

## Slide 9: AVPROD: Audio-Visual Service Production
Objective: | This work item shall specify requirements for using the 5G system for the production and contribution of audio-visual content and services as presented in TR 22.827. Specifically, this work item shall address: New KPIs for macro network & non-public networks (NPN), New service requirements for NPN, KPIs for Multicast and Broadcast Services, Network Exposure Requirements, Clock synchronisation, AVPROD application Specific Requirements, Mobile & airborne base stations for NPNs and Service continuity.
Rapporteur: | Ian Wagdin (BBC)
WI output | TR 22.827 Study on Audio-Visual Service Production TS 22.263 Service requirements for Video, Imaging and Audio for Professional Applications (VIAPA)
Possible RAN areas affected | IIoT and URLLC enhancements, Integrated Access and Backhaul enhancements, NR multicast broadcast, Coverage enhancements, Sidelink enhancements.

## Slide 10: CMED: Communication Service Requirements for Critical Medical Applications
Objective: | The objective of this work item is to provide normative requirements to enable a 3GPP system to adequately provide the connectivity between medical devices and critical medical applications. This work leverages the potential requirements identified in TR 22.826. Specifically, requirements relating to the following will be documented: 5G system performances (KPIs) required to enable use cases involving high quality and augmented imaging systems in hybrid ORs, 5G system performances (KPIs) required to enable use cases with tele-diagnosis, 5G system performances (KPIs) required to enable use cases with tele or robotic-aided operations, Security management in 5G systems for the sharing of medical data between care providers or with patients while still fulfilling national regulatory requirements
Rapporteur: | Mathieu Lagrange (b<>com)
WI output: | TR22.826 Study on Communication Services for Critical Medical Applications (FS_CMED) TS22.263 Service requirements for Video, Imaging and Audio for Professional Applications (VIAPA) TS22.261 Service requirements for next generation new services and markets TS22.104 Service requirements for cyber-physical control applications in vertical domains
Possible RAN areas affected | NR multicast broadcast, Coverage enhancements, IIoT and URLLC enhancements, Positioning enhancements, NR Light, XR&5G.

## Slide 11: EAV: 5G Enhancement for UAVs
Objective: | Document new KPIs and requirements to meet the industry applications and UAV communication service needs to a 3GPP subscription. Specifically, requirements relating to the following will be documented: - KPIs based on communication service - KPIs for command and control traffic - On-board radio access node (UxNB) - service restriction for UAV - Network exposure for UAV
Rapporteur: | Qun Wei (China Unicom)
WI output | TR 22.829 Enhancement for Unmanned Aerial Vehicles (UAVs) TS 22.125 Unmanned Aerial System support in 3GPP TS 22.261 Service requirements for next generation new services and markets
Possible RAN areas affected | Drones.

## Slide 12: eCAV: enhancements for CAV
Objective: | The objective of this work item is to identify further Stage 1 5G service requirements for cyber-physical control applications in vertical domains. Relative to the Rel-16 baseline, there are more specific requirements or additional requirements for closely-related additional functionality in order to improve the applicability of 5G systems to vertical domains. This work item shall specify further cyberCAV Stage 1 service requirements. Specifically, this work item shall address: - Industrial Ethernet integration, which includes time synchronization, different time domains, integration scenarios, and support for time-sensitive networking (TSN); - High-level requirements for network operation and maintenance in 5G non-public networks for cyber-physical control applications in vertical domains; - Positioning with focus on vertical directions / dimension for Industrial IoT;
Rapporteur: | Michael Bahr (Siemens)
WI output | TR 22.832 Study on enhancements for cyber-physical control applications in vertical domains TS 22.104 Service requirements for cyber-physical control applications in vertical domains TS 22.261 Service requirements for next generation new services and markets
Possible RAN areas affected | IIoT and URLLC enhancements, NR Light, NB IoT and EMTC enhancements, Sidelink enhancements, Positioning enhancements.

## Slide 13: MINT: Support for Minimization of service Interruption
Objective: | The aim of this work is to specify normative service requirements coming out of the study on Support for Minimization of service Interruption. Requirements related to the following will be specified: - Ensuring that the behaviour of all UEs impacted by a disaster condition takes into consideration the existence of the disaster condition; - Ensuring all UEs impacted by a disaster condition access to relevant network based on the start or end of the disaster condition; - Enabling a network to prevent congestion due to incoming huge number of roaming UEs as a result of impact of the disaster; - Handling of restrictions (e.g. forbidden PLMNs) during an applicable disaster condition
Rapporteur: | SungDuck Chun (LG Electronics)
WI output | TR 22.831 Study on Support for Minimization of service Interruption TS 22.261 Service requirements for next generation new services and markets TS 22.011 Service accessibility
Possible RAN areas affected | TEI & Others.

## Slide 14: MONASTERYEND: Complete Gap Analysis for Railways Mobile Communication System
Objective: | The railway community is considering a successor to GSM-R, as the forecast obsolescence of the 2G-based GSM-R technology is envisaged around 2030, with first FRMCS trial implementations expected to start around 2022/2023. The Future Railway Mobile Communication System (FRMCS) functional working group (FWG) of the International Union of Railways (UIC) have investigated and summarized their requirements for the next generation railway communication system in the Future Railway Mobile Communication User Requirements Specification. This work complete the gap analysis.
Rapporteur: | Guillaume Gach (UIC)
WI output | TR22.889 Study on Future Railway Mobile Communication System TS22.280 Mission Critical Services Common Requirements TS22.281 Mission Critical (MC) video TS22.282 Mission Critical (MC) data TS22.179 Mission Critical Push to Talk (MCPTT) TS22.289 Mobile communication system for railways
Possible RAN areas affected | Sidelink enhancements (direct communication with LOS up to 3km), NR multicast broadcast, MIMO enhancements (to support high speed trains up to 500 km/h) + bandwidths less than 5MHz (no related RAN work area but requirement as stated in TR 22.889 [R-12.23-001]), Positioning enhancements (positioning accuracy).

## Slide 15: MUSIM: Support for Multi-USIM Devices
Objective: | Based on the conclusion made in the study of FS_MUSIM (SP-190241), the aim of this work item (SP-190309) is to address the following aspects and provide consolidate service requirements in TS 22.278, TS 22.261, and TS 22.101 for enabling multi-USIM devices supports in EPS and 5G system: Enabling the support for terminal with multiple USIMs, Supporting Mobile-Terminated Service by providing service categories for the network to specify the service that triggers paging in the paging procedure, and handling of service prioritization and specifying the UE behaviour upon reception of paging information based on USIM configuration or user preferences or both, and Handling of emergency calls and sessions.
Rapporteur: | Ellen C Liao (Intel)
WI output | TR 22.834 Study on Support for Multi-USIM Devices TS 22.261 Service requirements for next generation new services and markets TS 22.278 Service requirements for the Evolved Packet System (EPS) TS 22.101 Service aspects; Service principles
Possible RAN areas affected | Multi SIM operation.

## Slide 16: NCIS: Network Controlled Interactive Service
Objective: | Objective: The aim of this work is to specify the interactive service requirements in additions to existing requirements e.g. KPI requirements defined in SMARTER and ProSe requirements in TS 22.278. Specifically, aspects to be specified are: KPIs for interactive service (including data rate, latency, reliability, user number, etc.) required for either ProSe Communication path or 5GC path; Group support and management for interactive service required for either ProSe Communication or 5GC path; Requirements related to suitable Hosted Service discovery. Normative requirements documented in this work item apply to 5GS with NR.
Rapporteur: | Ning Yang (OPPO)
WI output | TR 22.842 Study on Network Controlled Interactive Service in 5GS (FS_NCIS) TS 22.261 Service requirements for next generation new services and markets
Possible RAN areas affected | Sidelink enhancements, XR&5G.

## Slide 17: REFEC: enhanced Relays for Energy eFficiency and Extensive Coverage
Objective: | The objective of this work item is to develop Stage 1 normative service requirements for multi-hop relay by enhancing the work done for 'Indirect 3GPP Communication' in TS 22.278. This work will consider the potential requirements and KPIs in different domains (e.g. inHome, SmartCities, SmartFarming, SmartFactories, Smart Energy, Public Safety, Logistics) identified and concluded in TR 22.866 and use them as the basis for developing stage 1 normative requirements. This work item aims to update TS 22.261 to include multi-hop support for UE-to-Network Relay UEs regarding the following aspects: - General aspects. - Permissions and authorization. - Relay selection. - Relays for IoT. - Service continuity. - Functionality Exposure to 3rd parties. - Traffic scenarios
Rapporteur: | Toon Norp (KPN)
WI output | TR 22.866 Study on enhanced Relays for Energy eFficiency and Extensive Coverage TS 22.261 Service requirements for next generation new services and markets
Possible RAN areas affected | Sidelink enhancements, NB IoT and EMTC enhancements.