## Slide 1: Service Discovery For IP Applications
Lionel Morand
Orange

## Slide 2: Disclaimer: The content of this document is only for information. It describes possible solutions that have been discussed by CT4 during CT4#98-e. Further analysis is required and none of them has been endorsed by CT4.

## Slide 3: DNS-based Service Discovery (DNS-SD)

## Slide 4: DNS-based Service Discovery (DNS-SD)
Specifies how DNS resource records are named and structured to facilitate service discovery.
This mechanism allows clients to discover a list of named instances of a desired service in a given domain, using standard DNS queries.
No change to the structure of DNS messages, no new operation codes, response codes, resource record types, or any other new DNS protocol values.

## Slide 5: DNS-SD Principles
PTR lookup for the service name in the form of <Service>.<Domain>
  i.e. looking for this service in this domain
DNS-SD's PTR lookup result is combination of DNS records:
  DNS PTR (RFC1035) record(s)
    Providing the list of available instances in a domain as "Service Instance Names"
  DNS SRV (RFC2782) record(s)
    providing the port number and target host name of the Service Instance Names
  DNS A (RFC1035) and/or AAAA (RFC3596) record(s)
    All IP addresses of the target host name listed in the SRV record(s).
  DNS TXT (RFC1035) record(s)
    additional data for the given Service Instance
    single zero octet indicates that there is no additional data for the given Service Instance

## Slide 6: Structured Service Instance Name
Service Instance Name = <Instance>.<Service>.<Domain>
<Instance>
  user-friendly name, consisting of arbitrary Net-Unicode text
  Stored directly in the DNS serving <Domain>
<Service>
  ".<name>_tcp" (for app over TCP) or ".<name>_udp" (for all others).
  <name>: IANA registered name using simple "First Come First Served" policy
<Domain>
  "local." in the absence of any DNS server, meaning "link-local Multicast DNS"
  Otherwise, subdomain of an existing DNS domain name.

## Slide 7: DNS Queries 1/2
When a DNS server is deployed, DNS queries are sent to the Unicast DNS server.
The subdomain selected by the operator may be statically configured learned by some other mechanism, such as:
  the DHCP "Domain" option (option code 15) (RFC2132),
  the DHCP "Domain Search" option (option code 119) (RFC3397)
  IPv6 Router Advertisement Options (RFC6106)

## Slide 8: DNS Queries 2/2
In the absence of any DNS server, the DNS top-level domain ".local." is used
DNS queries are sent either to:
  IPv4/IPv6 multicast address to discover service instances on local link
    An node on the local link supporting the service receiving the mDNS request will respond
  a unicast IPv4/IPv6 address of a specific service instance
    Using the destination port 5353.
    On the local link or outside (if secured/authorized)
    The IP address of the target node is discovered by configuration.

## Slide 9: DNS configuration and update
DNS records are created at the set-up of the nodes
  Listening port selected by the implementation indicated in SRV RR
    Preferably from the User range [1024-49151]
  Via configuration file or DNS Update
  Configuration file can be automatically generated
Frequency of port number updates in DNS records is expected to be fairly low
  Each node using its own listening port, impacts of conflicts with IANA assignment is limited
If any update required:
  mDNS
    DNS records are locally updated into the nodes
  Conventional DNS
    Manually update of the records into the name server's configuration file
    Monitoring tool can generate a standard zone file to be updated into DNS server
    Use of DNS Update

## Slide 10: 3GPP standard action
Document the DSN-SD procedures in TS 29.303
  Generic mechanisms that can be reused for any new application/protocol defined by 3GPP
Reference to IETF standard procedures
Register specific 3GPP service name at IANA:
  under the "First Come First Served" policy
  No need for RFC/expert review
  e.g. for W1 application: "3gpp-w1ap"
To be further analysed

## Slide 11: OAM

## Slide 12: Principles
Static configuration by the operators of the listening port to be used for the 3GPP application/protocol
a port in the Private/Dynamic Port Numbers range [49152 - 65535] for a new 3GPP application
Easiest way: the same port should be used for the same service/interface across the PLMN
To be further analysed

## Slide 13: Fixed port assigned by 3GPP

## Slide 14: Principles
3GPP standardizes the listening port to be used for the application/protocol
From a port in the Private/Dynamic Port Numbers range [49152 - 65535] for a new 3GPP application
All 3GPP compliant implementations will know the listening port to use for a given 3GPP application/protocol.
To be further analysed

## Slide 15: Thank You!