## Slide 1
Network based Sensing in R18
2021-9-8

## Slide 2
Sensing Contents and Scenarios
Category of comm. sensing | Sensing contents | Potential scenarios
Macro information sensing | Information of weather, air quality, etc. | Meteorology, agriculture, life services
 | Target tracking, ranging, speed measurement, shape measurement, etc. | Application scenarios of radar
 | Statistics of the traffic flow at the intersection, personnel flow (including intrusion detection) | Intelligent transportation, business services
 | 3D environment construction (including reflector detecting) | Intelligent driving and navigation (car/UAV), smart city (3D map), network planning and optimization
Short distance refined information sensing | Heartbeat and breathing monitoring | Health care, medical care
 | Imaging, material detection, etc. | Security check, industry, etc.
In wireless communication, electromagnetic waves propagation transmits signals and carries environmental information at the same time
The integration of communication and sensing is one of the most effective means to build a digital twin world

## Slide 3
Network architecture Supporting network based Sensing
Sensing mode
End-to end Arch. supporting sensing
Sensing function: management, control and computing, etc.
Procedure(s):
  Sensing Control procedure
  Sensing Data report procedure
Prioritize sensing based on existing measurements in R18：
UE existing SRS, RAN obtains uplink measurements;
Existing or new measurements between RANs;
Existing or new measurements based on RAN echo;
Existing RRM configuration, UE obtains existing downlink measurements
No. | Transmitter | Receiver
1 | UE | BS
2 | BS A | BS B
3 | BS A | BS A
4 | BS | UE
5 | UE A | UE B
6 | UE A | UE A
BS: Base Station
Notes: 注：可扩展到多UE多基站

## Slide 4
UE involved sensing(BS -> UE & UE -> BS) complements BS echo detecting in R18
 | Transmitter BS A, receiver BS A (echo detecting) | BS -> UE & UE -> BS (UE involved sensing)
Sensing range | BS position is fixed; The number of BS is much smaller than the number of UE; The sensed area/objects is restricted | UE is widely distributed in the cell and the number of UE is larger than the number of BS. The sensed area/objects is greatly extended.
Sensing use cases | Rader-like sensing use cases including range/velocity/angle measurements | More use cases are supported (See Table 2).
Hardware implementation | In order to support echo detecting, BS need to support full duplex/pulse signal | No new hardware requirements.
Measurements |  | DL/UL | Use cases
Existing measurements | RSRP | BS -> UE & UE -> BS | Information of weather; air quality; traffic/personnel flow
 | RSRP, angle | BS -> UE & UE -> BS | 3D environment construction
New measurement | CSI (amplitude and phase of frequency domain channel response) | BS -> UE & UE -> BS | Heartbeat and breathing monitoring
Table 1: Comparison between BS echo detecting and UE involved sensing
Table 2: Example of measurements and use cases for UE involved sensing
Notes: 上报周期
耗电
NRPPa CN下任务给RAN，可能需要UE辅助。
LPP CN下任务给UE

## Slide 5
Trial (sensing for Breathing Monitoring) setup:
gNB
(use only 1Tx out of 4Tx)
UE (4Rx)
Target person for breathing monitoring
System：5G NR, Central frequency 3.63GHz, bandwidth 100MHz
Scenario：vivo Beijing site, indoor
gNB：indoor gNB
UE：prototype developed by vivo
gNB Tx antenna： 1Tx
UE Rx antenna ：4Rx
gNB-UE distance： 2 meters
Person-UE distance： 0.5 meter
CSI-RS periodicity: 20 ms
Raw data for sensing: channel frequency response on 1 PRB estimated by CSI-RS, 20ms periodicity, data of 40 seconds
(total 40/0.02 = 2000 samples)
Sensing trial based on NR: trial setup

## Slide 6
Breathing rate:~0.268Hz (16 breaths per minute)
Sensing trial based on NR: trial results
Target person for breathing monitoring
Amplitude of channel frequency response
Phase of channel frequency response
Step 1: channel estimation on 1 PRB based on CSI-RS
Step 2: channel frequency response of Rx 1 ./ channel frequency response of Rx 2
Step 3: do FFT on the data from Step 2, and get the breathing rate of the target people
Utilizing the channel frequency response of existing reference signal (e.g., CSI-RS for DL and SRS for UL), the receiver can monitor the breathing rate of the target people.

## Slide 7
Potential Architecture enhancement(s) for Supporting Network based Sensing in R18
1) Investigate architecture enhancement for sensing by introducing a new Sensing Function and corresponding procedure(s) for sensing control and sensing data report – 3GPP SA2
2) Investigate how to handle user privacy (SA2+SA3)
3) Sensing based charging (SA2+SA5-Charging)
Fig1a. Architecture for Sensing Control (per UE)
Fig2a. Architecture for Sensing Data Report (per UE)
Fig2b. Architecture for Sensing Data Report (per area)
Fig1b. Architecture for Sensing Control (per area)

## Slide 8
1. The AMF receives the Sensing Service Request from AF (via NEF optionally), which may include the target Area/UE ID, the required QoS.
2. The AMF selects an Sensing Function based on the factors may including the required QoS, Sensing Function capabilities and its load.
3. The AMF sends the Sensing Service Request to the Sensing Function .
4. The Sensing Function selects the RAN-Node and/or UE based on the target Area/UE and decides the sensing method to be used.
5. The Sensing Function performs sensing procedures with RAN-node to collect sensing data to obtain the sensing result.
6. Sensing measurement based on UE existing measurements or RAN existing/new measurements.
7. Sensing measurement report to SF.
8-10.The Sensing Function returns the Sensing Service Response towards the AMF and AMF returns it to the source of request.
Overall procedures(per UE or Per Area)

## Slide 9
Proposal for Introduction of sensing in R18
Potential standard impact(s) in R18
Architecture enhancement for supporting sensing(SA2, leading)
Alignment with RAN3(RAN3, dependent on SA2 discussion outcome)
User Privacy(SA2/SA3)
Charging for sensing(SA5/SA2-Charging)

## Slide 10
THANK
YOU