## Slide 1: Rel-18 Requirements for Access Traffic Steering, Switching & Splitting (ATSSS)
Lenovo, Motorola Mobility, ZTE, Broadcom, Apple, Alibaba, Tencent, China Mobile, Convida Wireless, Deutsche Telekom, Nokia, Nokia Shanghai Bell, Samsung, Interdigital, Matrixx, Cisco Systems, Charter Communications, CableLabs, Comcast, CATT, Intelsat, Vivo, BT, Thales, HPE, Tessares, Telefonica

## Slide 2: ATSSS Overview
The ATSSS feature was introduced in Rel-16 & enhanced in Rel-17
Enables multi-access communication between UE and UPF using one 3GPP access path and one non-3GPP access path
Traffic distributed to the access paths based on policy (multi-access rules) created by PCF
SDF traffic distributed based on a steering mode: Active-Standby, Load Balancing, Priority-based, or Smallest delay
Two steering functionalities: Multi-Path TCP (MP-TCP) and ATSSS-Low Layer (ATSSS-LL)

## Slide 3: What is missing?
Streamlining the ATSSS solution to support a new steering functionality for non-TCP traffic based on well-known IETF protocols, e.g., QUIC and/or DCCP.
ATSSS already supports MP-TCP, but it can only be applied to TCP traffic.
Similar support is needed for non-TCP traffic.
ATSSS-LL can be used for non-TCP traffic, but it is only a scheduler; not a transport protocol.

## Slide 4: What is missing?
This can enable ATSSS towards edge services and towards cloud services
Supporting ATSSS when the user plane contains a Branching Point (BP) or UL Classifier (ULCL)
Presently,
the ATSSS functionality
is assumed to be at the central UPF (PSA)

## Slide 5: What is missing?
Supporting use cases, which require ATSSS to support two 3GPP access paths
A non-3GPP access path may also be needed, resulting in three access paths between the UE and UPF

## Slide 6: What is missing?
Supporting use cases, which require ATSSS to support two Non-3GPP access paths (e.g. NWu & NWt) and, at least, Active-Stanby steering.
A 3GPP access path may not always be present, so it should be possible to tranfer traffic directly between NWu and NWt access paths.
N3
NG-RAN
Nwu
Nwt

## Slide 7: What is missing?
Supporting ATSSS for traffic to Local Area Data Networks (LADNs)
Data traffic to an LADN is only allowed when the UE is located in a specific area called “LADN service area”.
Rel-17 specs do not allow the UE to establish a MA PDU Session towards an LADN because it cannot be guaranteed that, when the UE gets outside the LADN service area, the user-plane traffic will be prohibited.

## Slide 8: What is missing?
Support redundant steering functionality for guaranteeing QoE (e.g. Improved Reliability).
Redundant transmission is critical for ensuring the QoE via guaranteeing latency and packet loss ratio for live video streaming.
The Rel-17 ATSSS study considered the redundant steering mode; see solution 4 in TR 23.700-93. In this solution, the transmitter (UE or UPF) decides to activate or deactivate packet transmission redundancy (i.e. replication of packets on both accesses) based on performance measurements and thresholds.
However, the solution in Rel-17 was not fully specified, e.g., it was not fully specified what types of ATSSS rules are required for redundant operation and how the UE/UPF operate in detail. Also, additional mechanisms for the activation / deactivation of packet transmission redundancy (e.g., triggers from an AF/streaming server) were not considered.
Now, there is a revitalized interest in redundant steering, specifically, for improving the reliability and latency of live video streams.