## Slide 1: 3GPP Inputs to GSMA OPAG API Mapping

## Slide 2
GSMA OPAG API Mapping Feedback – NBI (1/3)
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Application onboarding and image management | ETSI MEC 010-2 | How much can be reused? | 3GPP TS 28.538 | 3GPP TS 28.538 specifies Edge Computing Management. It support lifecycle management (e.g. onboarding) of Edge applications.
Application Instance Management (Resource Life-Cycle Management) | ETSI MEC 010-2 | How much can be reused? | 3GPP TS 28.538 | 3GPP TS 28.538 specifies Edge Computing Management. It support lifecycle management of Edge applications.
Telemetry | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF), 3GPP 28.552, 3GPP 28.554 (depending on data source) | Not all requirements collected in the PRD might be covered in 3GPP definition. | 3GPP TS 28.532 ¦ 3GPP TS 28.550 ¦ 3GPP TS 28.422 | It is unclear on the use of SCEF/NEF for this API. All telemetry requirements refers to management plane, and specified in 3GPP TS 28.552/28.554. 3GPP TS 28.532/28.550 defined mechanism to collect measurements (Telemetry). TS 28.422 specifies trace and MDT data collection mechanism. NOTE: 3GPP TS 28.538 will specify requirements and impacts to 28.552/554 for Edge-related telemetry functions.
Notifications | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) | Not all requirements collected in the PRD might be covered in 3GPP definition. | 3GPP TS 23.558 (Stage 2) ¦ 3GPP TS 29.558 (Stage 3) ¦ 3GPP TS 28.532 | 3GPP TS 23.558 specifies Edge-specific notifications about events related to UE: UE location in clause 8.6.2, Application Client Information in clause 8.6.4, and EES: service continuity management notifications in clause 8.6.3, QoS event notification in clause 8.6.6, service continuity status notifications in clause 8.8.3.6 TS 28.532 captures the management related notification.
Network Events | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) |  | 3GPP TS 23.558 (Stage 2) ¦ 3GPP TS 29.558 (Stage 3) 3GPP TS 23.222 (Stage 2) ¦ 3GPP TS 29.222 (Stage 3) | 3GPP TS 23.558 specifies enhanced application-aware exposure of network events via EDGE-3 (leveraging CAPIF as specified in clause 8.7.3) e.g. for continuous reporting to track UE's location
Trouble Ticketing | TMF 621 |  | 3GPP TS 28.532 | 3GPP TS 28.532 provides fault supervision management service which support the trouble ticketing.

## Slide 3
GSMA OPAG API Mapping Feedback – NBI (2/3)
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Application Resource Catalogue | ETSI MEC 011, TMF 639, TMF 634 (Resource inventory), (Resource Catalog)) | ETSI MEC to confirm if ETSI MEC 010-2 or 011? | 3GPP TS 28.538¦ 3GPP TS 28.632 | 3GPP TS 28.538 specifies resource management for Edge applications (e.g. virtual network resource) TS 28.632 provides 3GPP inventory management.
Ordering | TMF 641 |  | NA | NA
Charging | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) |  | Stage 2: 3GPP TS 32.254 ¦ TS 32.257 ¦ TS 32.290 Stage 3: 3GPP TS 32.299 ¦ TS 32.298 ¦ TS 32.291 | 3GPP TS 32.290 defines 5G system, Services, operations and procedures of charging using Service Based Interface 3GPP TS 32.254 defines Exposure function Northbound Application Program Interfaces charging, including the SCEF and NEF charging. 3GPP TS 32.257 defines Edge application-specific billing/charging framework 3GPP TS 32.291 defines 5G system, charging service for NEF charging 3GPP TS 32.298 defines Charging Data Record (CDR) parameter description and ASN.1 for charging 3GPP TS 32.299 defines Diameter charging applications for SCEF charging
Billing | TMF 636 (BSS) |  | 3GPP TS 32.257 | 3GPP TS 32.257 defines Edge application-specific billing/charging framework
QoS Management | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF), ETSI GS MEC 015 (NEF) |  | 3GPP TS 23.558 (Stage 2) ¦ 3GPP TS 29.558 (Stage 3) ¦ 3GPP TS 28.541 | 3GPP TS 23.558 specifies Edge application-aware management (create/update/revoke) of session with specific QoS in clause 8.6.6 TS 28.541 specifies the configuration of 5QI including dynamic5QI and configurable5QI.
Traffic Influence | 3GPP TS 29.522 (NEF), ETSI GS MEC 015 (NEF) |  | 3GPP TS 23.558 (Stage 2) ¦ 3GPP TS 29.558 (Stage 3) | 3GPP TS 23.558 clause 8.6.3 specifies detection of user plane path change for the application traffic and report user plane path change to the Application

## Slide 4
GSMA OPAG API Mapping Feedback – NBI (3/3)
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Managing Service availability in LADN | LADN Concept defined by 3GPP 23.501 | Stage 2 and Stage 3 Status? | 3GPP TS 28.538 ¦ 3GPP TS 23.558 (Stage 2) ¦ 3GPP TS 29.558 (Stage 3) | 3GPP TS 28.538 address EDN with LADN (DN) 3GPP TS 23.558 specifies EDN deployment using LADN in clause 7.3.3.4 and Annex A.2.4.
Application relocation | 3GPP 23.558 ¦ TS 23.548 ¦ ETSI MEC 021 ¦3GPP TS 23.501, TS 23.502 | How much work is already done on 3GPP? | 3GPP TS 29.558 (Stage 3) | 3GPP TS 29.558 specifies Stage 3 aspects of Application relocation APIs
NEW: Confirm User Location | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) |  | 3GPP TS 23.558 (Stage 2)¦ 3GPP TS 29.558 (Stage 3) | 3GPP TS 23.558 in clause 8.6.2 specifies both request-response for one-time query as well as subscribe-notify model for providing UE's location on a continuous basis enabling EAS to track any UE's location changes

## Slide 5
GSMA OPAG API Mapping Feedback – SBI-CR
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Orchestration |  |  | 3GPP TS 28.532 ¦ 3GPP TS 28.531 ¦ 3GPP TS 28.541 | 3GPP TS 28.532, 28.531 and 28,541 together specifies orchestration for 5G VNF. Edge Application when deployed as VNF can be orchestrated using same specifications.
Virtualised Infrastructure Manager |  |  |  | 
Container Infrastructure Manager |  |  |  | 
Telemetry |  |  | 3GPP TS 28.552 ¦ 3GPP TS 28.554 ¦ 3GPP TS 28.532 ¦ 3GPP TS 28.550 | 3GPP TS 28.552 and TS 28.554 defines the performance measurements and KPIs for edge applications respectively. 3GPP TS 28.532/28.550 defined mechanism to collect measurements (Telemetry). NOTE: 3GPP TS 28.538 will specify requirements and impacts to 28.552/554 for Edge-related telemetry functions.
Notifications |  |  | 3GPP TS 28.552 ¦ 3GPP TS 28.532 | 3GPP TS 28.552 defines the virtual resource usage measurements for a slice. Measurements for edge application can also be defined. TS 28.532 captures the management related notification.

## Slide 6
GSMA OPAG API Mapping Feedback - EWBI
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Application onboarding | ETSI MEC 010-2 |  | See NBI | Requirements for EWBI has a strong dependency on NBI requirements, therefore the mapping information provided for NBI also applies for EWBI. Further, please note that 3GPP is addressing EWBI functionality as part of Rel-18 in SA2, SA5 and SA6 working groups. NOTE: EWBI requirements (e.g. application roaming) are being studied in 3GPP TR 23.700-98 (Rel-18)
Application Instance Management (Resource Life-Cycle Management) | ETSI MEC 010-2 |  | See NBI | 
Telemetry | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF), 3GPP 28.552, 3GPP 28.554 (depending on data source) | Not all requirements collected in the PRD might be covered in 3GPP definition. | See NBI | 
Notifications | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) | Not all requirements collected in the PRD might be covered in 3GPP definition. | See NBI | 
Network Events | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) |  | See NBI | 
Trouble Ticketing | TMF 621 |  | See NBI | 
East/West Bound Interface Management | ETSI MEC is leading the EWBI scope, however these functionalities are not yet defined/developed. ETSI MEC 40? Stage 3 Development? | To check how 3gpp and ETSI can collaborate on those capabilities not already defined. | See NBI | 
Availability Zone Information Synchronisation Service |  |  |  | 
LBO Roaming (Monitoring) |  |  |  | 
LBO Roaming (Authentication) |  |  |  | 
Edge Node Sharing (resource onboarding & Management) |  |  |  | 

## Slide 7
GSMA OPAG API Mapping Feedback – SBI-NR
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
User Authentication and Authorisation | 3GPP TS 29.522 |  | 3GPP TR 33.839 ¦ 3GPP TS 33.558 3GPP TS 23.501 ¦ 3GPP TS 23.502¦ 3GPP TS 23.503¦ 3GPP TS 23.548 ¦ 3GPP TR 28.817 | 3GPP TR 33.839 and TS 33.558 is specifying security aspects for Edge computing application architecture. Clause 7 of 3GPP TR 33.839 provides the study conclusions. 3GPP TS 23.501¦TS 23.502¦TS 23.503¦TS 23.548 provides core network procedures related to user authentication/authorization. TR 28.817 provides access control for management services
Mobility Triggers | 3GPP TS 29.122 ¦ 3GPP TS 29.522 |  |  | 
Mobility Control | 3GPP TS 29.522 |  |  | 
Confirm user location | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF) |  |  | 
QoS Management | 3GPP TS 29.122 (SCEF) ¦ TS 29.522 (NEF), ETSI GS MEC 015 (NEF) |  | 3GPP TS 28.541 | TS 28.541 specifies the configuration of 5QI including dynamic5QI and configurable5QI.
Traffic Influence | 3GPP TS 29.522 (NEF), ETSI GS MEC 015 (NEF) |  |  | 
Collecting Network Status | 3GPP TS 29.122 ¦ 3GPP TS 29.522 |  | 3GPP TS 28.545 ¦ 3GPP TS 28.550 ¦ 3GPP TS 28.532 ¦ 3GPP TS 28.552 ¦ 3GPP TS 28.554 ¦ 3GPP TS 28.541 | 3GPP TS 28.545 defined fault (alarm) supervision 3GPP TS 28.552/554 defines performance measurement and KPIs 3GPP TS 28.550/532 defined performance assurance used to collect network data. TS 28.541 provides network management resource models.
Managing Service availability in LADN | LADN Concept defined by 3GPP 23.501 | Stage 2 and Stage 3 Status? | 3GPP TS 23.501 ¦ TS 23.502¦ TS 23.503 | LADN mechanism was defined in Rel-15 and has been implemented in stage 3 specs.
Application relocation | 3GPP 23.558 ¦ TS 23.548 ¦ ETSI MEC 021 ¦3GPP TS 23.501, TS 23.502 |  | 3GPP TS 29.558 (Stage 3) 3GPP TS 29.522 (NEF) (Stage 3) | 3GPP TS 29.558 specifies Stage 3 aspects of Application relocation APIs
NEW: Location Privacy Indicator | 3GPP TS 29.522 |  |  | 

## Slide 8
GSMA OPAG API Mapping Feedback – SBI-CHF
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Charging events | 3GPP TS 32.291 |  | Stage 2: 3GPP TS 32.290 ¦ 3GPP TS 32.255 ¦ 3GPP TS 32.254 ¦ 3GPP TS 32.256 3GPP TS 32.257 Stage 3: 3GPP TS 32.298 | 3GPP TS 32.290 defines 5G system, Services, operations and procedures of charging using Service Based Interface 3GPP TS 32.255 defines 5G data connectivity domain charging 3GPP TS 32.254 defines Exposure function Northbound Application Program Interfaces charging, including the SCEF and NEF charging. 3GPP TS 32.256 defines 5G connection and mobility domain charging (AMF charging) 3GPP TS 32.257 defines edge computing charging aspects 3GPP TS 32.298 defines Charging Data Record (CDR) parameter description and ASN.1 for charging

## Slide 9
GSMA OPAG API Mapping Feedback – UNI
APIs | Covered by SDOs | Comments on SDOs References | Missing 3GPP references (based 2nd column) | Additional Feedback/Remarks
Registration | 3GPP TS 23.558 |  | 3GPP TS 24.558 (Stage 3) 3GPP TS 23.548 (Stage 2) | 3GPP TS 24.558 specifies Stage 3 aspects for registration 3GPP TS 23.548 specifies Stage 2 core network aspects on authorization, deployment information provisioning and support functions for Application level registration
Discovery | 3GPP TS 23.558 |  | 3GPP TS 24.558 (Stage 3) 3GPP TS 23.548 (Stage 2) | 3GPP TS 24.558 specifies Stage 3 aspects for discovery 3GPP TS 23.548 specifies Stage 2 core network aspects for DNS/EASDF based discovery
Mobility/QoE | 3GPP TS 23.558 |  | 3GPP TS 24.558 (Stage 3) ¦ 3GPP TS 28.404 (Stage 1) ¦ 3GPP TS 28.405(Stage 2) ¦ 3GPP TS 23.548 (Stage 2) | 3GPP TS 24.558 specifies Stage 3 aspects for mobility aspects 3GPP TS 28.404 and TS 28.405 specifies QOE management. 3GPP TS 23.548 specifies Stage 2 core network aspects for mobility

## Slide 10: Thank You!