## Slide 1: TSG SA WG4 (SA4) Status Report at TSG SA#95-e
Frédéric Gabin
SA4 Chair (Dolby Laboratories Inc.)
(Agenda Item 4.4)

## Slide 2: Outline
General
  Leadership and subgroups
  Meetings and statistics
  Progress highlights
Work progress
  CRs to features in Rel-16 and earlier
  CRs to completed features, TEI17 and non-SA4 items in Rel-17
  Rel-17 Work Items
  Rel-18 Work Items
  Study Items
New Study and Work Items
IETF Dependencies
Summary of action items

## Slide 3: SA4 leadership and subgroups
SA4 officials:
  Chair: Frédéric Gabin (Dolby Laboratories Inc. , ETSI)
  Vice Chairs:
    Gilles Teniou (Tencent, CCSA)
    Jaeyeon Song (Samsung Electronics Co., Ltd, TTA)
  Secretary: Ms Jayeeta Saha (MCC Support)
Sub Working Groups and their Chairs – New!
  EVS and SQ SWGs are merged into a single “Audio SWG”
  MTSI SWG is renamed as Real Time Communications (RTC) SWG
Audio SWG | Multicast-Broadcast-Streaming (MBS) SWG | Real Time Communications (RTC) SWG | Video SWG
Imre Varga (Qualcomm CDMA Technologies, ETSI) & Stéphane Ragot (Orange, ETSI) | Frédéric Gabin (Dolby Laboratories Inc. , ETSI) | Nikolai Leung (Qualcomm Incorporated, ATIS) | Gilles Teniou (Tencent, CCSA)

## Slide 4: Meetings held since SA#94-e
SWG conference calls (2 to 3 hours each)
  MBS SWG AH Telcos: 16 December, 13 January (jointly with SA2 and CT3 on EVEX), 3 February, 3 and 10 March;
  Video SWG AH Telcos: 14 December, 11 January, 1 February, and 8 March;
  MTSI SWG AH Telcos: 15 December and 2 February;
  EVS SWG AH Telco: 24 January and 14 March;
SA4 Release 18 Workshop #3 (telco)
  27th January 2022
SA4 plenary meeting
Meetings | Dates | Venue and Host
SA4#117-e | E-meeting: 14-23 February 2022 | Host: MCC, Electronic meeting

## Slide 5: Calendar of future meetings - 1
SWG conference calls
  MBS SWG AH Telcos: 25 March (jointly with SA2 and CT3 on EVEX);
  Video SWG AH Telcos: 22 March;
  RTC SWG AH Telcos: 16 March (on new Rel-18 WIDs);
SA4 plenary meetings (2022)
Meetings in 2022 | Dates | Venue and Host
SA4#118-e | E-meeting: 6-14 April 2022 | Host: MCC, Electronic meeting
SA4#119-e | E-meeting: 11-20 May 2022 | Host: MCC, Electronic meeting
SA4#120/-e | F2F: 22-26 August 2022 OR, E-meeting: 17-26 August 2022 | Host: TBD, Venue: Malaga, ES OR, Host: MCC, Electronic meeting
SA4#121/-e | F2F: 14-18 November 2022 OR, E-meeting: 9-18 November 2022 | Host: TBD, Venue: TBD, US OR, Host: MCC, Electronic meeting

## Slide 6: Calendar of future meetings - 2
SA4 plenary meetings (2023)
Meetings in 2023 | Dates | Venue and Host
SA4#122/-e | F2F: 20-24 February 2023 OR, E-meeting: 20 February-1 March 2023 | Host: TBD, Venue: TBD
SA4#123/-e | F2F: 17-21 April 2023 OR, E-meeting: 12 (or 17)-21 April 2023 | Host: TBD, Venue: TBD Note: preference for an e-meeting
SA4#124/-e | F2F: 22-26 May 2023 OR, E-meeting: 17 (22)-26 May 2023 | Host: TBD, Venue: TBD
SA4#125/-e | F2F: 21-25 August 2023 OR, E-meeting: 16-25 August 2023 | Host: TBD, Venue: TBD
SA4#126/-e | F2F: 13-17 November 2023 OR, E-meeting: 8-17 November 2023 | Host: TBD, Venue: TBD

## Slide 7: Calendar of future meetings - 3
SA4 plenary meetings (2024)
Meetings in 2024 | Dates | Venue and Host
SA4#127/-e | F2F: 29 January - 2 February 2024 OR, E-meeting: 24 January - 2 February 2024 | Host: TBD, Venue: TBD
SA4#127bis/-e | F2F: 8-12 April 2024 OR, E-meeting: 8-12 April 2024 | Host: TBD, Venue: TBD
SA4#128/-e | F2F: 20-24 May 2024 OR, E-meeting: 20-27 May 2024 | Host: TBD, Venue: TBD
SA4#129/-e | [F2F: 22-26 July 2024 OR, E-meeting: 17-26 July 2024] Note: dates TBC due to MPEG | Host: TBD, Venue: TBD
SA4#130/-e | F2F: 18-22 November 2024 OR, E-meeting: 13-22 November 2024 | Host: TBD, Venue: TBD

## Slide 8: SA4 meeting statistics

## Slide 9: SA4 progress highlights
SA4 Rel-18 workshop #3 held 27th January to progress Rel-18 planning. No further Workshop is planned as SID and WIDs are now being processed to implement the plan. At SA4#117-e, priority was given to Rel-17 completion.
The list of SA4 Rel-16 TSs/TRs to be promoted to Rel-17 were agreed and listed in S4-220330.
2024 SA4 meeting dates were agreed
Completed the Rel-17 work on support of Immersive Teleconferencing and Telepresence for Remote Terminals (ITT4RT)
Completed several of the Rel-17 work item objectives on Handsets Featuring Non-Traditional Earpieces (HaNTE) while certain objectives will be moved to a future new Rel-18 WID.
Completed Rel-17 work on 8K Television over 5G (8K_TV_5G)
Completed Rel-17 work on 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA)
Completed Study items on VR Streaming Conformance and Guidelines , 5G Glass-type AR/MR Devices and 5G media streaming extensions
3 Rel-17 Work Item and 3 Study Items Exceptions are requested to allow completion in June 2022
2 new Rel-18 Work items (immersive Real-time Communication for WebRTC, Media Capabilities for Augmented Reality) and 3 Study Items (Artificial Intelligence (AI) and Machine Learning (ML) for Media, enhancements for immersive Real-time Communication for WebRTC, Smartly Tethering AR Glasses, ) are presented for approval

## Slide 10: CRs to features to completed items in Rel-16 and earlier
Rel-16:
  SP-220031 ”CR pack for correction and adding support for VR-QoE metrics [26.512; WID:5GMS3]”: A missing property is added to the M5 client metrics reporting configuration resource structure telling the Media Session Handler which metrics reporting scheme to use when submitting QoE metrics reports. Support for VR QoE metrics was missing. It is now corrected.
  SP-220036 “CR Pack on Missing XML Data Type for Attributes in MBMS USD [26.346; WID:AE_enTV-S4, TEI16]”: It adds indication in the Rel-16 XML schema extension that the data type of the subcarrierSpacing and bandwidth attributes of the Frequency element is xs:decimal.
  SP-220037 “CR pack on Correction 5GMS Client definition and clarification of reference point usage [26.501; WID: 5GMSA]”: Triggered by a discussion in the 5G-MAG Reference Tools group, it is clarified that the 5GMS Client internal structure is up for implementation.

## Slide 11: CRs to completed features, TEI17 and non-SA4 items in Rel-17
Rel-17:
  SP-220033: CR Pack for QoE measurements [26.114 and 26.247; WID: NR_QoE- Core]: in particular, Slice id (DNN+S-NSSAI) is added into the QoE reports for QMC based QoE configuration and reporting.
  SP-220038: CR Pack on Extensions to MBMS-URLs for ROM Services [26.347;WID: TEI17, TRAPI]: CR to 26.347 agreed on Extensions to MBMS-URLs for ROM Services (Rel-17). For Receive-only Mode (ROM) services, an extended URL is specified to find service announcements and services. The following domain name is explicitly reserved for Receive-only Mode services: mbms://rom.3gpp.org

## Slide 12: Overview of work progress Rel-17 Work Items
Note: Progress since last SA is shown with blue colour.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
820003 | Support of Immersive Teleconferencing and Telepresence for Remote Terminals (ITT4RT) | 90% | 100% | 03/22 | Completed !
860012 | Handsets Featuring Non-Traditional Earpieces (HaNTE) | 85% | 100% | 03/22 | Completed !
880012 | Extension for headset interface tests of UE (HInT) | - | 100% | 03/22 | Completed at SA#94-e
920011 | 8K Television over 5G (8K_TV_5G) | 60% | 100% | 03/22 | Completed !
920008 | 5GMS AF Event Exposure (EVEX) | 40% | 60% | 03/22 -> 06/22 | Exception request for approval
920009 | Edge Extensions to the 5G Media Streaming Architecture (5GMS_EDGE) | - | 100% | 12/21 | Completed at SA#94-e
920010 | 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA) | 60% | 100% | 03/22 | Completed !
890009 | Operation Points for 8K VR 360 Video over 5G (8K_VR_5G) | - | 100% | 09/21 | Completed at SA#93
940008 | 5G Multicast-Broadcast Protocols (5MBP3) | 0% | 40% | 03/22 -> 06/22 | Exception request for approval
940009 | Edge Extensions to 5GMS Stage 3 (5GMS_EDGE_3) | 0% | 60% | 03/22 -> 06/22 | Exception request for approval

## Slide 13: Support of Immersive Teleconferencing and Telepresence for Remote Terminals (ITT4RT) – Completed !
Purpose
The objective of this Work Item is to specify VR support in MTSI in TS 26.114 and IMS-based Telepresence in TS 26.223 to enable support of an immersive experience for remote terminals joining teleconferencing and telepresence sessions. WID: SP-180985
Progress in the last quarter
The ITT4RT work item is now 100% completed. The following documents are presented for approval:
SP-220250 TR 26.962: Immersive Teleconferencing and Telepresence for Remote Terminals (ITT4RT) Operation and Usage Guidelines
SP-220251 TR 26.862: Immersive Teleconferencing and Telepresence for Remote Terminals (ITT4RT) Use Cases, Requirements and Potential Solutions
SP-220035 CR Pack on ITT4RT Phase 2 [26.114; WID: ITT4RT]
A WI summary has been endorsed.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
820003 | Support of Immersive Teleconferencing and Telepresence for Remote Terminals (ITT4RT) | 90% | 100% | 03/22 | Completed !

## Slide 14: Handsets Featuring Non-Traditional Earpieces (HaNTE) – Completed !
Purpose
UEs supporting handset mode communication without a traditional earpiece to produce sound are becoming available in the market, and 3GPP specs require updates to allow for their appropriate testing. WID: SP-191212
Progress in the last quarter
A CR to 26.132 on ECRP determination has been agreed: SP-220034 CR Pack on the method for determining ECRP for HaNTE-devices [26.132; WID: HanTE]
Specific WI objectives that were partially addressed have been incorporated in a new Rel-18 WID proposal. Based on this way forward, the HaNTE WI for Rel-17 is 100% completed.
A WI summary has been endorsed.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
860012 | Handsets Featuring Non-Traditional Earpieces (HaNTE) | 85% | 100% | 03/22 | Completed !

## Slide 15: 8K Television over 5G (8K_TV_5G) – Completed !
Purpose
The objective of this Work Item is to specify an HEVC-based 8K TV operation point in TS 26.116 as well as the corresponding media decoding capabilities for 5GMS in TS 26.511 in order to enable support for up to 8K video. WID: SP-210381
Progress in the last quarter
Agreed the definition of the 8K TV operation point to be added to the TV video profiles in TS 26.116
Agreed to reference this 8K operation point in 5GMS by indicating that it “may” be used in the TV profile of TS 26.511.
CR to TS 26.116 also clarifies the differences between 3GPP TV video profiles and MPEG CMAF Media profiles.
The description of the 8K TV scenario for the video codec characterization was agreed.
8K video addition to TR 26.955 will be done through a future TEI18 CR when FS_5GVideo Study Item is completed.
Agreed a CR to TR 26.925 on 8K traffic characteristics
Document to SA plenary is SP-220032 CR Pack on 8K HEVC Operation Point, CMAF Alignment and Traffic Characteristics [26.116 and 26.925 & 26.511; WID: 8K_TV_5G]
The Work item is 100% complete.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
920011 | 8K Television over 5G (8K_TV_5G) | 60% | 100% | 03/22 | Completed !

## Slide 16: 5GMS AF Event Exposure (EVEX)
Purpose
Objectives (summarized): define the media related data and formats for the media session data to be exposed by the 5GMS AF. Enhance the 5GMS AF data collection to support direct and indirect collection of UE data pertaining to media sessions. WID: SP-210374
Progress in the last quarter
CR to 26.512 prepared and postponed providing instantiation of generic data collection and reporting architecture for the 5G Media Streaming feature domain as specified in TS 26.531 and TS 26.532.
Draft CR to TS 26.501 agreed as basis for further work on Data collection and reporting for 5G Media Streaming. It provides instantiation of generic data collection and reporting architecture for the 5G Media Streaming architecture.
New draft TS 26.531 prepared with domain model revisited and data exposure restriction model introduced.
SP-220248: TS 26.532: Data Collection and Reporting; Protocols and Formats, new draft TS 26.532 prepared and agreed to be presented for information at SA. This is a stage 3 specification for UE data collection and reporting functionality, to complement the stage 2 specification in TS 26.531 on generic data collection and reporting architecture.
SP-220244 [EVEX] Proposed Exception Sheet: agreed an exception request to allow completion in June 2022. There are dependencies with CT3.
Next steps
Completion of generic data collection and reporting by the AF in Rel-17 TS 26.531 and TS 26.532.
Specification of Rel-17 5G Media Streaming functionality which incorporate relevant features from TS’s 26.531 and 26.532, in Rel-17 TS 26.501 and TS 26.512.
Completion by CT3 of stage 3 Naf_EventExposure and Nnef_EventExposure service APIs in Rel-17 TS 29.517 and TS 29.522 in support of functionality defined by EVEX and reflected in Rel-17 versions of TSs 26.501, 26.512, 26.531 and 26.532.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
920008 | 5GMS AF Event Exposure (EVEX) | 40% | 60% | 03/22 -> 06/22 | Exception request for approval

## Slide 17: 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA) – Completed !
Purpose
Objectives (summarized): specify the 5MBS User Service architecture. Define relevant call flows and procedures to support 5GMS over 5MBS; 5GMS hybrid unicast/broadcast services; 5MBS usage independent of 5GMS. WID: SP-210376
Progress in the last quarter
SP-220039 CR Pack on 5GMS via eMBMS - Architecture, Broadcast and Reporting [26.501; WID: 5MBUSA]: CR to TS 26.501 agreed on 5GMS Architecture on 5GMS via eMBMS. It defines an architecture for downlink 5G Media Streaming via eMBMS that combines the functions and reference points of the 5GMS System with those of the MBMS System. This arrangement allows 5GMS-based downlink media streaming to be deployed as an MBMS-aware Application on top of eMBMS as defined in TS 23.246, TS 26.346, TS 26.347 and TS 26.348.
SP-220297 3GPP TS 26.502 V1.1.0 5G multicast–broadcast services; User Service architecture, agreed to be sent to SA for approval. TS 26.502 defines the stage 2 User Services architecture for 5G multicast–broadcast services. It builds on the foundations of the recently completed MBS System specification defined by SA2 in TS 23.247.
LS (to 3GPP SA2, CT3, CT4) on 5MBS User Services was approved to inform about the completion of the Stage 2 work and ask questions about Group Communication feature over MBS.
The Work Item is 100% complete
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
920010 | 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA) | 60% | 100% | 03/22 | Completed !

## Slide 18: 5G Multicast-Broadcast Protocols (5MBP3)
Purpose
Specify the stage 3 format and protocol for User Service Announcement (between MBSF and MBS Client), MBS distribution methods (between MBSTF and MBS Client) based on existing MBMS delivery methods i.e. Object distribution method and Packet distribution method, associated delivery procedures, and corresponding extensions to TS 26.512, TS 26.346 and TS 26.347 to support 5G Media Streaming via eMBMS.
WID: SP-211335
Progress in the last quarter
The Work Item progressed to 40% and should complete for June 2022. SP-220243 [5MBP3] Proposed Exception Sheet is presented for approval.
SP-220249 TS 26.517: 5G Multicast–Broadcast User Services; Protocols and Formats. Presented for information to SA. TS 26.517 provides a Release 17 stage 3 specification of the protocols and data formats supporting Multicast–Broadcast User Services in the 5G System.
Next steps
Complete 5G Multicast-Broadcast User Services; Protocols and Formats
Complete Distribution Methods for MBS and Extensions for 5GMS delivery
Complete Client APIs for MBS and Extensions to MBMS-APIs for 5GMS delivery
Complete 5G Media Streaming via eMBMS
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
940008 | 5G Multicast-Broadcast Protocols (5MBP3) | 0% | 40% | 03/22 -> 06/22 | Exception request for approval

## Slide 19: Edge Extensions to 5GMS Stage 3 (5GMS_EDGE_3)
Purpose
Based on 5GMS extended architecture TS 26.501 that now supports Edge media processing, extend the M1 interface and APIs to support the provisioning of edge resources for media services, enhance the M5 interface and APIs to support the configuration, discovery, QoS support, tracking, and relocation of edge processing resources; define the 5GMS AF and 5GMS AS application context and the corresponding transfer procedures; introduce any other related stage 3 enablers for edge media processing
WID: SP-211336
Progress in the last quarter
The work progressed with CRs to TS 26.512 on Edge Provisioning for Media Services and Edge Configuration for 5G Media Services prepared but postponed to the next meeting.
SP-220246 [5GMS_EDGE_3] Proposed Exception Request for approval
Next steps
Minimal M6 APIs to enable the application to request and release edge resources for edge media processing sessions
ACR transfer procedures and event-driven EAS relocation triggering
Implementation of and corrections to the corresponding REST APIs
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
940009 | Edge Extensions to 5GMS Stage 3 (5GMS_EDGE_3) | 0% | 60% | 03/22 -> 06/22 | Exception request for approval

## Slide 20: Overview of work progress Rel-18 Work Items
Note: Progress since last SA is shown with blue colour.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
830005 | Terminal Audio quality performance and Test methods for Immersive Audio Services (ATIAS) | 20% | 20% | 12/22 | 
770024 | EVS Codec Extension for Immersive Voice and Audio Services (IVAS_Codec) | 30% | 30% | 12/23 | 

## Slide 21: Terminal Audio quality performance and Test methods for Immersive Audio Services (ATIAS)
Purpose
The overall objective of this work item is to develop a set of test specifications similar to TS 26.131 and 26.132 for objective characterization of terminals for 3GPP immersive services. This covers both conversational services based on MTSI / telepresence and non-conversational services. The tests will be limited to the use of an acoustic or a digital / analog audio interface. WID: SP-190040
Progress in the last quarter
No progress
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
830005 | Terminal Audio quality performance and Test methods for Immersive Audio Services (ATIAS) | 20% | 20% | 12/22 | 

## Slide 22: EVS Codec Extension for Immersive Voice and Audio Services (IVAS_Codec)
Purpose
The overall objective of this work item is to develop a single general-purpose audio codec for immersive 4G and 5G services and applications including the VR use cases envisioned in 3GPP TR 26.918. WID: SP-170611
Progress in the last quarter
IVAS-6 (Selection Deliverables), IVAS-7a (Processing Plan for Selection), IVAS-8a (Test plan for selection phase) updated based on agreed inputs.
Contribution S4-220161 provided the terms of reference (ToR) of the planned public collaboration; the process of joining is entirely open and it is clearly described in the ToR and was also explained in details.
Contribution S4-220111 provided the draft Funding Agreement for the IVAS standardization process. The proposed text reflects the SA4 working assumption that there will be a single common candidate codec to be submitted for selection. The current document structure was provided by ETSI/3GPP MCC and EVS SWG Chairman and was then vetted by ETSI legal.
Next steps
Interested companies are asked to check the Funding Agreement with the goal to be agreed at the next meeting. The Funding Agreement was included in square brackets in IVAS-6 which was then agreed as the next working draft.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
770024 | EVS Codec Extension for Immersive Voice and Audio Services (IVAS_Codec) | 30% | 30% | 12/23 | 

## Slide 23: Overview of work progress Study Items
Note: Progress since last SA is shown with blue colour.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
850004 | Feasibility Study on VR Streaming Conformance and Guidelines (FS_VR_CoGui) | 90% | 100% | 03/22 | Completed !
870013 | Feasibility Study on Typical Traffic Characteristics for XR Services and other Media (FS_XRTraffic) | 75% | 80% | 03/22 -> 06/22 | Exception request for approval
870013 | Feasibility Study on 5G Video Codec Characteristics (FS_5GVideo) | 85% | 90% | 03/22 -> 06/22 | Exception request for approval
880011 | Feasibility Study on 5G Glass-type AR/MR Devices (FS_5GSTAR) | 90% | 100% | 03/22 | Completed !
900029 | 5G media streaming extensions (FS_5GMS_EXT) | 60% | 100% | 03/22 | Completed !
910001 | Feasibility Study on Media Production over 5G NPN (FS_NPN4AVProd) | 60% | 80% | 03/22 -> 06/22 | Exception request for approval
940010 | Feasibility Study on 5G Media Service Enablers (FS_5G_MSE) | 0% (New) | 20% | 09/22 | Target Release: Rel-18

## Slide 24: Feasibility Study on VR Streaming Conformance and Guidelines (FS_VR_CoGui) - Completed !
Purpose
Objective: provide content generation and usage guidelines for the technologies defined in TS 26.118. WID: SP-190642
Progress in the last quarter
SP-220252 TR 26.999: Virtual Reality (VR) Streaming Interoperability and Characterization presented for approval.
The work is now complete.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
850004 | Feasibility Study on VR Streaming Conformance and Guidelines (FS_VR_CoGui) | 90% | 100% | 03/22 | Completed !

## Slide 25: Feasibility Study on Typical Traffic Characteristics for XR Services and other Media (FS_XRTraffic)
Purpose
Objective: Collect and document traffic characteristics for different services, and additional information, such as codecs and protocols in use. Identify additional relevant XR and other media services and document their traffic characteristics. WID: SP-210043
Progress in the last quarter
Agreed version 1.1.0 of the draft TR 926. The rapporteur continued the integration of some material from the permanent document.
Next steps
Agree CR to TR 26.925 on different Traffic Models
Agree new TR 26.926 in version 2.0.0 after having included all agreed information from the permanent document
Communicate with other 3GPP groups and external organizations
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
870013 | Feasibility Study on Typical Traffic Characteristics for XR Services and other Media (FS_XRTraffic) | 75% | 80% | 03/22 -> 06/22 | 

## Slide 26: Feasibility Study on 5G Video Codec Characteristics (FS_5GVideo)
Purpose
Objective: primarily to identify relevant interoperability requirements, performance characteristics and implementation constraints of video codecs in 5G services, and to characterize existing 3GPP video codecs, in particular H.264/AVC and H.265/HEVC in order to have a benchmark for the addition of potential future video codecs. WID: SP-210378
Progress in the last quarter
Draft TR 26.955 progressed to v1.5.0: Some characterization updates were agreed. Progressed the EVC metrics collections and agreed some verification results related to this codec. VVC reference software updated together with its configuration files. Issue identified and resolved on the HDR conversion for 8 bit sequences by setting a correct parameter (ScaleOnly=1). Agreed a few definitions impacting the low delay encoding configurations of the codecs.
SP-220247 [FS_5GVideo] Proposed Exception Sheet: Proposed extension to June 2022 with an exception request to make sure the TR can be published within Rel-17.
Next steps
4 Ad Hoc Telcos are planned to perform all necessary characterization tasks for HEVC, AVC and new codecs.
Agree on TR 26.955 v2.0.0 to be sent to SA for approval
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
870013 | Feasibility Study on 5G Video Codec Characteristics (FS_5GVideo) | 85% | 90% | 03/22 -> 06/22 | 

## Slide 27: Feasibility Study on 5G Glass-type AR/MR Devices (FS_5GSTAR) – Completed !
Purpose
Objectives (summary): Provide formal definitions for the functional structures of AR glasses, describe key use cases for AR services over 5G, describe the architecture for media flow relevant to the use cases identified and Identify necessary content delivery transport protocols and capability exchange mechanisms, as well as suitable 5G system functionalities (e.g., device, edge, network) and QoS. WID: SP-200399
Progress in the last quarter
SP-220254 TR 26.998: Support of 5G Glass-type Augmented Reality / Mixed Reality (AR/MR) devices for approval: Reviewed contributions relating to call flows for immersive cognitive scenarios and shared AR conversational services. Definitions have been simplified in terms of description of AR sessions. Significant time spent on the conclusions to the technical report inviting for normative work considerations.
The study item is complete.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
880011 | Feasibility Study on 5G Glass-type AR/MR Devices (FS_5GSTAR) | 90% | 100% | 03/22 | Completed !

## Slide 28: 5G media streaming extensions (FS_5GMS_EXT) - Completed !
Purpose
The objective of this study is in the context of the following potential improvements and extensions to 5G Media streaming: Content Preparation, Traffic Identification, Additional / New transport protocols, Uplink media streaming, Background traffic, Content Aware Streaming, Network Event usage, Per-application-authorization, Support for encrypted and high-value content, Scalable distribution of unicast Live Services. WID: SP-200937
Progress in the last quarter
SP-220253 TR 26.804: Study on 5G media streaming extensions, presented for approval. Latest additions are allowed use of HTTP/3, aspects of TV-grade mass distribution of unicast Live Services, Conclusion for the Background Data traffic key issue, Corrections and Conclusions for Traffic Identification key issue, Per App authorization, Additional Potential Issues for Network Slicing Extensions and overall Conclusions.
LS (to 3GPP SA2, CT3) on Traffic Identification within 5G Media Streaming
The Study Item is complete.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
900029 | 5G media streaming extensions (FS_5GMS_EXT) | 60% | 100% | 03/22 | Completed !

## Slide 29: Feasibility Study on Media Production over 5G NPN (FS_NPN4AVProd)
Purpose
The study will identify the relevant media production use cases (professional, semi-professional, production, contribution); develop one or several reference media production architecture(s); identify relevant QoS requirements for media production workflows; identify relevant 5G System features like NPNs, Network Slicing, QoS classes, network event reporting and assistance, etc. that are useful for media production. WID: SP-200241
Progress in the last quarter
TR 26.805 Study on Media Production over 5G NPN Systems (Release 17) progressed to v1.1.0 including aspects of QoS Separation and is presented to SA plenary for information (SP-211341). New aspects are: SMPTE audio metadata, mmWAVE for Media Production, Tunnelling RTP media sessions over QUIC, Definition of Collaboration Scenarios, Introduction to Candidate Solutions and updates to KI#2: Media Protocols on 5G: Traffic segregation and traffic prioritization.
SP-220245 [FS_NPN4AVProd] Proposed Exception Request: enables to complete in June 2022 and retain the TR in Rel-17.
Next steps
Agree on Study conclusions
Agree TR 26.805 v2.0.0 to be sent to SA plenary for approval
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
910001 | Feasibility Study on Media Production over 5G NPN (FS_NPN4AVProd) | 60% | 80% | 03/22 -> 06/22 | 

## Slide 30: New Study Item: Feasibility Study on 5G Media Service Enablers (FS_5G_MSE)
Purpose
In recent studies and specification work, it was identified that 5G Media functions and 5G System functions need to be made attractive for third-party applications that include media delivery. Hence, it is important that these functions are accessible to third-party applications independent of a 3GPP service. The objective of the study item is the definition of 5G Media Service Enablers.
WID: SP-211338
Progress in the last quarter
This Study Item was initiated at this meeting and progressed to 20% completion.
3GPP TR 26.857 V0.1.0 5G Media Service Enablers (Rel-18) – First draft TR with agreed outline.
Initial timeplan prepared and agreed.
Next steps
Initiate and progress specification template for Media Service Enablers
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
940010 | Feasibility Study on 5G Media Service Enablers (FS_5G_MSE) | 0% (New) | 20% | 09/22 | Target Release: Rel-18

## Slide 31: Overview of new Items
Note: Progress since last SA is shown with blue colour.
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
950011 | Feasibility Study on Artificial Intelligence (AI) and Machine Learning (ML) for Media (FS_AI4Media) | New | 0% | 12/23 | Target Release: Rel-18
950012 | Feasibility Study on the enhancements for immersive Real-time Communication for WebRTC (FS_eiRTCW) | New | 0% | 06/23 | Target Release: Rel-18
950013 | Feasibility Study on Smartly Tethering AR Glasses (SmarTAR) | New | 0% | 03/23 | Target Release: Rel-18
950014 | WID on immersive Real-time Communication for WebRTC (iRTCW) | New | 0% | 12/23 | Target Release: Rel-18
950015 | WID on Media Capabilities for Augmented Reality (MeCAR) | New | 0% | 12/23 | Target Release: Rel-18

## Slide 32: Feasibility Study on Artificial Intelligence (AI) and Machine Learning (ML) for Media (FS_AI4Media)
Purpose
The objectives of the study item are primarily to identify relevant interoperability requirements and implementation constraints of AI/ML in 5G media services.
WID: SP-220238
Supporting Individual Members: Samsung Electronics Co., Ltd., Qualcomm Incorporated, Fraunhofer HHI, InterDigital Communications, Dolby Laboratories Inc., AT&T, Orange, Nokia Corporation, Tencent, MediaTek
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
940010 | Feasibility Study on 5G Media Service Enablers (FS_5G_MSE) | New | 0% | 12/22 | Target Release: Rel-18

## Slide 33: Feasibility Study on the enhancements for immersive Real-time Communication for WebRTC (FS_eiRTCW)
Purpose
In addition to the foreseen approach identified in TR 26.998 (Support of 5G glass-type AR/MR devices) and taken in WID on iRTCW (immersive Real-time Communication for WebRTC), which leaves C-plane signalling details open and simply makes use of the northbound APIs for end-to-end QoS), the possibility of another approach (i.e., defining a set of advanced details (including C-plane signalling) for the common and wider use among several WebRTC implementations) will be investigated under this SID
WID: SP-220239
Supporting Individual Members: NTT, Qualcomm Incorporated, Facebook, Tencent, Orange, KPN, Samsung Electronics, Co., LTD, AT&T
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
950012 | Feasibility Study on the enhancements for immersive Real-time Communication for WebRTC (FS_eiRTCW) | New | 0% | 06/23 | Target Release: Rel-18

## Slide 34: Feasibility Study on Smartly Tethering AR Glasses (SmarTAR)
Purpose
Defining different tethering architectures for AR Glasses including 5G sidelink and non-5G access based on existing 5G System functionalities
Study the relationship between AR Glasses tethering and AR glasses considered as PIN (Personal IoT Network) elements according to TR 22.859 and the derived service requirements in TS 22.261.
Identify media handling aspects of different tethering architectures
Identify end-to-end QoS-handling for different tethering architectures and define supporting mechanisms to compensate for the non-5G link between the UE and the AR glasses
Provide recommendations for suitable architectures to meet typical AR requirements such as low power consumption, low latency, high bitrates, security and reliability.
WID: SP-220240
Supporting Individual Members: Qualcomm Incorporated, Facebook, Dolby Laboratories Inc., Xiaomi, Samsung Electronics Co., Ltd, Tencent, Huawei Technologies Co., Ltd., AT&T
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
950013 | Feasibility Study on Smartly Tethering AR Glasses (SmarTAR) | New | 0% | 03/23 | Target Release: Rel-18

## Slide 35: WID on immersive Real-time Communication for WebRTC (iRTCW)
Purpose
Objective 1: Define a non-vertical/modularized protocol stack for iRTC clients to support WebRTC-based real-time transport of media over 5G;
Objective 2: Define functional components of an iRTC client in terminal that (as in Figure 1 of TS 26.110 where video and audio I/Os are connected to 3G-324M protocol architecture).
Objective 3: Define inputs into an iRTC client in terminal and their required / recommended parameters, if any. This includes outputs from cameras / microphones (e.g., N depth streams / M RGB streams & their relationships or direction of microphones, in compact and scalable descriptions) with a focus on practical mobile implementations. (More advanced device configurations, e.g., studio-class cameras and microphone set-ups can be considered when available).
Objective 4: Identify the required architecture for radio access network QoS realization over 5G systems, using WebRTC-based transport.
Objective 5: Identify the minimum information / elements in the C/U-Plane signal to establish media sessions with appropriate QoS for WebRTC-based applications.
Objective 6: Document informative examples of iRTC operations to assist implementers.
WID: SP-220241
Supporting Individual Members: Facebook, Dolby, Qualcomm Incorporated, KPN N.V., MediaTek Inc., NTT, TELUS, Xiaomi, Verizon UK Ltd, Tencent, Nokia Corporation, T-Mobile USA, China Mobile Communications Corporation, China Telecom Corporation Ltd., Motorola Mobility UK Ltd., AT&T, Samsung Electronics Co., Ltd, Orange, Fraunhofer IIS
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
950014 | WID on immersive Real-time Communication for WebRTC (iRTCW) | New | 0% | 12/23 | Target Release: Rel-18

## Slide 36: WID on Media Capabilities for Augmented Reality (MeCAR)
Purpose
Define at least one AR device category that addresses the constraints of an EDGAR-type AR glass
Integrate IVAS into suitable AR device categories, once IVAS is available
Define capability exchange mechanisms based on complexity of AR media and capability of device to support EAS KPIs for provisioning of edge/cloud resources
Identify which QoE metrics from VR QoE metrics can be reused or enhanced for AR media (e.g., resolution per eye, Field of view (FOV), round-trip interaction delay, etc.) and define relevant KPIs that are dedicated to AR/MR
Specify additional relevant KPIs and simple QoE Metrics for AR media
Specify encapsulations into RTP, ISOBMFF and CMAF
Specify the relevant codec-level parameters for session setup and negotiation of the media delivery and provide instantiations for SDP and DASH MPD
Enable AR media in 5G Media Streaming by defining suitable 5GMS profiles based on AR media capabilities
Define typical traffic characteristics for AR media
WID: SP-220242
Supporting Individual Members: Xiaomi, Qualcomm Incorporated, Samsung Electronics Co., Ltd, AT&T, MediaTek, Dolby Laboratories Inc., Tencent, Nokia Corporation, InterDigital Communications, KPN N.V, Facebook, Fraunhofer IIS, VoiceAge Corporation, Orange, Ericsson LM
Unique_ID | Name (acronym) | Previous % | Current % | Target completion | Remark/updates/SR
950015 | WID on Media Capabilities for Augmented Reality (MeCAR) | New | 0% | 12/23 | Target Release: Rel-18

## Slide 37: Dependencies on IETF drafts in SA4
No new dependency introduced
All dependencies removed
IETF dependencies in SA4: new ones with red colour, those removed with green colour, and other updates by blue colour:
IETF draft name | 3GPP spec. number | CR# which introduced the dependency | Responsible person (in SA4) | Feature (Release) | Comments

## Slide 38: Summary of action items
Action Points from SA#94-e to SA4:
  n/a
Action items from SA4 to SA#95-e:
  Approve all SA4 agreed CRs,
  Approve all SA4 agreed TRs and TSs presented for approval
  Approve 2 new WIDs and 3 new SIDs
  Approve all SA4 agreed exception requests
  Approve the list of SA4 Rel-16 TSs/TRs to be promoted to Rel-17 (S4-220330)