## Slide 1: R19 Ambient Power-enabled IoT Services Stage-1 Status & System Impacts Observation towards 5G System
from OPPO’s Perspectives
SP-220930
3GPP TSG-SA Meeting #97
E-meeting, 13 – 19 September 2022

## Slide 2: Ambient Power-enabled IoT Presentation Highlights
Ambient Power-enabled IoT – Motivations
Latest Rel-19 SA1 Stage-1 Status on Ambient Power-Enabled IoT Services Study
Network Architecture Impacts Considerations for supporting Ambient Power-enabled IoT Services over 5G system
Security Impacts Considerations for supporting Ambient Power-enabled IoT Services over 5G system
RAN Impacts Considerations for supporting Ambient Power-enabled IoT Services over 5G system
Final Remarks

## Slide 3: Ambient Power-enabled IoT - Motivations
What is ambient power-enabled IoT?
Ambient power-enabled IoT
  Ambient IoT devices are battery-less or with limited energy storage capability, power source depending on energy harvesting is unstable e.g., solar power at night or cloudy day
Key point
  battery-less IoT devices powered by energy harvesting and equipped with (ultra-) low-power transceiver (e.g., power consumption of less than 1mw)
  Ambient power-enabled IoT device is different than today NR/Redcap/LTE-M/NB-IoT ultra low powered devices
  Amount of Ambient power-enabled IoT devices are relatively more massive. However, volume of data transmission for Ambient power-enabled IoT is much smaller (e.g., only active status).
  The capability and cost of Ambient power-enabled IoT devices will be ultra-low.

## Slide 4: Latest Rel-19 SA1 Stage-1 Status on Ambient Power-Enabled IOT Services Study
20 use cases have been identified during SA1#98 and SA1#99
  e.g., automated warehousing, medical instruments inventory management and positioning, smart grid, non-public network for logistics, Intralogistics in automobile manufacturing, automated supply distribution, base station machine room environmental supervision, personal belongings finding, Indoor positioning, smart laundry, sensors in smart homes, flower auction etc.,
  Use cases are categorized into 3 groups
    Asset management and tracking, i.e., identification, stored information reading.
    Sensor data reporting
    Positioning/Ranging
Functional requirements and performance requirement (i.e., KPI) have been discussed and some have been agreed.
  maximum allowed end-to-end latency, user-experienced data rate, message size, device density, communication range etc. have been agreed for smart grid and the flower auction use cases.
In summary, very good progress on the use cases and KPIs have been made in Rel-19 SA1 study for Ambient power-enabled IoT

## Slide 5: Network Architecture Impacts Considerations for supporting Ambient Power-enabled IoT Services over 5G system
Two kinds of network architecture need to be considered for Ambient Power-enabled IoT.
  Direct mode (ambient IoT device connecting to 5G network/gNB directly) as shown in Figure 1 below
  Indirect mode (ambient IoT device connecting to 5G network/gNB via a UE) as shown in Figure 2 below
Key technical areas that could be impacted are:
  Registration, Connection and Mobility Management, more specifically, Mobility management part including procedures and states can be adjusted to cope with unstable power resource challenge
  Connectivity Management for data transmission
  Policy Enhancement,
  Positioning Support and
  Coexistence with legacy UEs and other IoT devices.
Figure 1 Direct mode for Ambient Power-enabled IoT devices
Figure 2 Indirect mode for Ambient Power-enabled IoT devices
Note: “collecting point” is the anchor point for gathering data for IoT devices.
It is expected existing 5G architecture can be reused as much as possible to support Ambient Power-enabled IoT services.

## Slide 6: Security Impacts Considerations for supporting Ambient Power-enabled IoT Services over 5G system
Unique Challenges against Ambient Power-enabled IoT Services.
  When comparing to the NB-IoT/RedCap/NR UEs, the Ambient power-enabled IoT device has less resource in terms of storage and computation
    How to verify device ID and authorize service access
    How to ensure securing the connections and safeguarding data transmissions
    How much security capability that the Ambient power-enabled IoT devices could support
    What kind of security mechanisms (e.g. light weight) for Ambient Power-enabled IoT Services

## Slide 7: RAN Impacts Considerations for supporting Ambient Power-enabled IoT Services over 5G system
Unprecedented challenges against Ambient Power-enabled IoT Services
  Ultra-low power (e.g. 1mW) communication support
  Unstable and limited power source for most of the considered use cases and scenarios while supporting device identity reading and reporting, sensor data reading and reporting and even positioning
  Not economic to use single gNB to support Ambient power-enabled IoT devices over a very small coverage (e.g., tens of meters to 100 meters), should 5G to leverage UE assistance, to provide small coverage such as smart home, small plant etc. so that gNB based deployment and the UE based deployment can share the same design (e.g., the air interface) as much as possible?
Mode-1: gNB based deployment
Mode-2: UE based assistance deployment
It is recommended to include both gNB-to-device communication and UE-to-device communication deployment modes in the RAN study to ensure efficient 5G coverage for Ambient Power-enabled IOT Services

## Slide 8: Final Remarks
A brief summary is present on the latest progress on the stage-1 study on Ambient power-enabled IoT devices during the past SA1#98 and SA1#99 meeting which demonstrated significant good progress including the use cases and the KPIs.
High-level considerations on the 5G system impacts are identified that need to be addressed by various 3GPP Working Groups.
Ambient power-enabled IoT services over 5G system should be considered as an essential services to be supported by 5G system which could leverage “both” gNB-to-device communication and the UE-to-device communication deployment modes.
OPPO welcomes collaboration with companies who are interested in advancing the progress of Ambient power-enabled IoT service over 5G system in Rel-19.

## Slide 9
Comments, Anyone?