## Slide 1: TSG SA WG4 (SA4) Status Report at TSG SA#92-e
Frédéric Gabin
SA4 Chair (Dolby Laboratories Inc.)
(Agenda Item 4.4)

## Slide 2: Outline
General
  Leadership and subgroups
  Meetings and statistics
  Progress highlights
Work progress
  CRs to features in Rel-16 and earlier
  Rel-17 Work Items
  Rel-18 Work Items
  Study Items
Proposed new WIDs/SIDs
IETF Dependencies
Summary of action items

## Slide 3: SA4 leadership and subgroups
SA4 officials:
  Chair: Frédéric Gabin (Dolby Laboratories Inc. , ETSI) – New! Re-elected at SA4#113-e
  Vice Chairs:
    Gilles Teniou (Tencent, CCSA) – New! Re-elected at SA4#113-e
    Stefan Bruhn (Dolby Laboratories Inc., ETSI)
  Secretary: Ms Jayeeta Saha (MCC Support)
New! Elections planned at SA4#115-e 18-27 august 2021 for one Vice-Chair position.
Sub Working Groups and their Chairs
Enhanced Voice Service (EVS) SWG | Multicast-Broadcast-Streaming (MBS) SWG | Multimedia Telephony Service for IMS (MTSI) SWG | Speech Quality (SQ) SWG | Video SWG
Imre Varga (Qualcomm CDMA Technologies, ETSI) | Frédéric Gabin (Dolby Laboratories Inc. , ETSI) | Nikolai Leung (Qualcomm Incorporated, ATIS) | Stéphane Ragot (Orange, ETSI) | Gilles Teniou (Tencent, CCSA)

## Slide 4: Meetings held since SA#91-e
SWG conference calls (2 to 3 hours each)
  MBS SWG AH Telcos (FS_EMSA, FS_5GMS_Multicast, FS_5GMS_Ext, 5GMS3 maintenance, FS_NPN4AVProd and the new 5MBUSA WID)
    18 Mar., 25 Mar., 22 Apr., 6 May, 2 Jun., 10 Jun.
  Video SWG AH Telcos (8K_VR_5G, FS_XRTraffic, FS_VR_CoGui, FS_5GVideo)
    23 Mar., 4 May, 11 May, 8 Jun.
  MTSI SWG AH Telcos (ITT4RT, FS_FLUS_NBMP)
    24 Mar., 9 Jun.
  SQ SWH AH Telcos (HInT, HaNTE)
    23 Apr, 3 May
SA4 plenary meeting(s)
Meeting | Dates | Venue and Host
SA4#113-e | 6 – 14 April 2021 | Host: MCC, Electronic meeting
SA4#114-e | 19 – 28 May 2021 | Host: MCC, Electronic meeting

## Slide 5: Calendar of future meetings - 1
SWG conference calls
  MBS SWG AH Telcos (FS_EMSA, FS_NPN4AVProd and new WIDs)
    24 Jun., 8 Jul., 22 Jul. 5 Aug.
  Video SWG AH Telcos (8K_VR_5G, FS_XRTraffic, FS_VR_CoGui, FS_5GVideo)
    22 Jun. (inc. joint with MTSI), 6 Jul., 20 Jul. 3 Aug.
  MTSI SWG AH Telcos (ITT4RT, FS_FLUS_NBMP)
    23 Jun., 30 Jun.
  SQ SWH AH Telcos (HInT, HaNTE)
    30 Jul.
SA4 plenary meetings (2021)
Meetings in 2021 | Dates | Venue and Host
SA4#115-e | 18 – 27 August 2021 | Host: MCC, Electronic meeting
SA4#116-e | 105 – 19 November 2021 | Host: MCC, Electronic meetingEF3, Venue: Marbella, Spain

## Slide 6: Calendar of future meetings - 2
SA4 plenary meetings (2022)
Meetings in 2022 | Dates | Venue and Host
SA4#117/-e | F2F: 14-18 February 2022 OR, E-meeting: 14-23 February 2022 | Host: ETSI, Venue: Sophia-Antipolis, France OR Host: MCC, Electronic meeting
SA4#118-e | 6-14 April 2022 | Host: MCC, Electronic meeting
SA4#119/-e | F2F: 16-20 May 2022 OR, E-meeting: 11-20 May 2022 | Host: TBD, Venue: TBD
SA4#120/-e | F2F: 22-26 August 2022 OR, E-meeting: 17-26 August 2022 | Host: TBD, Venue: TBD
SA4#121/-e | F2F: 14-18 November 2022 OR, E-meeting: 9-18 November 2022 | Host: TBD, Venue: TBD

## Slide 7: Calendar of future meetings - 3
SA4 plenary meetings (2023) New!
Meetings in 2023 | Dates | Venue and Host
SA4#122/-e | F2F: 20-24 Feb. OR, E-meeting: 20 Feb.- 1 Mar. 2023 | Host: TBD, Venue: TBD
SA4#123 | F2F: 17-21 April 2023 | Host: TBD, Venue: TBD
SA4#124 | F2F: 22-26 May 2023 | Host: TBD, Venue: TBD
SA4#125/-e | F2F: 21-25 August 2023 OR, E-meeting: 16-25 August 2023 | Host: TBD, Venue: TBD
SA4#126/-e | F2F: 13-17 Nov. 2023 OR, E-meeting: 8-17 Nov. 2023 | Host: TBD, Venue: TBD

## Slide 8: SA4 meeting statistics

## Slide 9: SA4 progress highlights
Important Rel-16 corrections to Multimedia Telephony Data Channel, Spatial positioning of the chroma samples for TV Video Profiles and VR Video Profiles and consumption & metrics reporting and dynamic policies of 5G Media streaming.
Further resolution of pending IETF dependencies in TS 26.223 for IMS Telepresence;
Rel-17 Work Item on Operation Points for 8K VR 360 Video over 5G (8K_VR_5G) now complete; New WID on 8K Television over 5G (8K_TV_5G) for approval.
New WID on 5GMS AF Event Exposure (EVEX) for approval.
Feasibility Study on Multicast Architecture Enhancements for 5GMSA (FS_5GMS_Multicast) now complete with TR for approval. Corresponding New WID on 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA) for approval;
Feasibility Study on Streaming Architecture extensions For Edge processing (FS_EMSA) now complete with TR for approval. Corresponding New WID on Edge Extensions to the 5G Media Streaming Architecture (5GMS_EDGE) for approval;
Revised SID on Feasibility Study on 5G Video Codec Characteristics includes AV1 Codec in its scope.

## Slide 10: CRs to features in Rel-16 and earlier
IMS_TELEP_S4: SP-210536 CRs to TS 26.223 on IETF reference update (Rel-13)
5G_MEDIA_MTSI_ext: SP-210530 CRs to MTSI TS 26.114 Updates on data channel (Rel-16):
  The parameters to be determined in the session setup for data channel media are aligned to RFC 8841. It is allowed for a stream ID 0 data channel application to use additional data channels. It also includes editorial improvements.
MMCMH: SP-210531 CR to MTSI TS 26.114 on IETF Reference Update for MMCMH (Rel-17):
  Missing Rel-17 Mirror CR of Rel-14 correction SP-210178
TEI16/TEI17: SP-210532 and SP-210533 CRs to TS 26.116 and TS 26.118 on Spatial positioning of the chroma samples for TV Video Profiles and VR Video Profiles (Rel-16 and Rel-17 for mirror):
  For BT.2020 and BT.2100, the relative spatial positioning of the chroma samples is different than the default and for BT.709. Signaling this difference is important and if not set, may lead to unnecessary problems shifts in the chroma presentation.
5GMS3: SP-210535 CRs to TS 26.501 and TS 26.512 on consumption & metrics reporting, dynamic policies and other stage 3 aspects (Rel-16)
  In particular it clarifies the ClientId definition for Consumption and Metrics Reporting

## Slide 11: List of SA4 Work Items for Rel-17
Rel-17 Work Items
IVAS_Codec (EVS Codec Extension for Immersive Voice and Audio Services)
ITT4RT (Support of Immersive Teleconferencing and Telepresence for Remote Terminals)
HaNTE (Handsets Featuring Non-Traditional Earpieces)
HInT (Extension for headset interface tests of UE)
8K_VR_5G (Operation Points for 8K VR 360 Video over 5G) – 100% complete !

## Slide 12: IVAS_Codec (EVS Codec Extension for Immersive Voice and Audio Services)
The overall objective of this work item is to develop a single general-purpose audio codec for immersive 4G and 5G services and applications including the VR use cases envisioned in 3GPP TR 26.918. WID: SP-170611
Since SA#91-e, the following progress was achieved:
  New IVAS-6 permanent document on Selection Deliverables agreed as working draft (S4-210645). Includes working assumption about the selection and characterization funding with 1.2 M€ budget and funds collected with two LoIs.
  IVAS-1 permanent document was updated to include the appointed editor for IVAS-6 (S4-210646) and was agreed as the current working draft v.0.3.0
  IVAS proponents are invited to reconfirm their interest to submit a candidate in IVAS standardization. Re-confirmations and indications should be made no later than the next SA4#115e meeting in August 2021.
  11 companies have since long developed and in detail presented the concept of IVAS public collaboration. They reconfirmed their interest to submit an IVAS codec candidate and expressed their expectation that they will submit a single joint candidate resulting from the IVAS public collaboration.
  It was agreed to collect example test designs potentially relevant for IVAS testing in a Permanent document.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
IVAS_Codec (EVS Codec Extension for Immersive Voice and Audio Services) | New set of 8 TSs and 1 TR on Codec for Immersive Voice and Audio Services CR to 26.114 | 27% | SA#96 | None
Note: Progress since last SA is shown with blue colour.

## Slide 13: ITT4RT (Support of Immersive Teleconferencing and Telepresence for Remote Terminals)
The objective of this Work Item is to specify VR support in MTSI in TS 26.114 and IMS-based Telepresence in TS 26.223 to enable support of an immersive experience for remote terminals joining teleconferencing and telepresence sessions. WID: SP-180985
Since SA#91-e, the following progress was achieved:
  Agreed updates to the Work Item Description to extend the work until March 2022; produce a 26.8XX Technical Report to document key aspects of the Permanent Document; produce a 26.9XX Technical Report to Operational Guidelines; replace one of the rapporteurs and add supporting companies
  Agreed a CR to TS 26.114 on Addition of second block of features for the MTSI ITT4RT functionality.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
ITT4RT (Support of Immersive Teleconferencing and Telepresence for Remote Terminals) | CR to 26.114 and 26.223 on Support of Immersive Teleconferencing for Remote Terminals | 60% -> 75% | SA#92 -> SA#95 | SP-210377: Revised WID on 'Support of Immersive Teleconferencing and Telepresence for Remote Terminals' (ITT4RT; UID: 820003) SP-210537: CR on ITT4RT Features
Note: Progress since last SA is shown with blue colour.

## Slide 14: HaNTE (Handsets Featuring Non-Traditional Earpieces)
UEs supporting handset mode communication without a traditional earpiece to produce sound are becoming available in the market, and 3GPP specs require updates to allow for their appropriate testing. WID: SP-191212
Since SA#91-e, the round robin activity is now complete and a report of complete aggregated results has been presented. Results indicate very good reproducibility for the traditional non-HaNTE device example (DUT8) while results for HaNTE devices (DUTs 1 to 7) show some variability, it is not yet clear what is the reason for this observed problem (e.g. test method not reproducible, some DUTs with bad performance, lab mistake, etc.). Further analysis (e.g. subjective testing of DUTs) is foreseen to explain this lack of reproducibility, and labs were invited to crosscheck their data to be able to consolidate the analysis for the next meeting.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
HaNTE (Handsets Featuring Non-Traditional Earpieces) | CR to 26.131 on update of receive direction requirements CR to 26.132 on update of receive direction test methods CR to 26.801 on update with new findings | 40% -> 70% | SA#93 | None
Note: Progress since last SA is shown with blue colour.

## Slide 15: HInT (Extension for headset interface tests of UE)
HInT (Extension for headset interface tests of UE) Objective (summary): Update of TS 26.131 and TS 26.132 to include standardized analogue (wired) and digital (wired and wireless) headset interfaces definitions, setup of headset interface testing, new headset interface tests and new requirements and objectives of headset interface tests. WID: SP-200398
Since SA#91-e, the following progress was achieved:
  Updated draft CRs to TS 26.131 and TS 26.132 have been progressed as a basis for further editing.
  dCR to TS 26.131
  dCR to TS 26.132
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
HInT (Extension for headset interface tests of UE) | CRs to TS 26.131 CRs to TS 26.132 | 50% -> 70% | SA#93 | None
Note: Progress since last SA is shown with blue colour.

## Slide 16: 8K_VR_5G (Operation Points for 8K VR 360 Video over 5G) – complete !
The objective of this Work Item is to specify operation points in VR streaming specification TS 26.118 as well as new media decoding capabilities for 5GMS in TS 26.511 in order to enable support for up to 8K video. WID: SP-200667
Since SA#91-e, the following progress was achieved:
  Agreed CRs to TS 26.118
  Operation Points for 8K VR 360 Video: defines new 360-degree video operation point(s) for VR streaming to be used in conjunction with the Main Video Profile with conforming bitstream requirement based on H.265/HEVC Main-10 Profile Main Tier Profile beyond the existing level 5.1 decoding capability, supporting spatial resolutions up to 8K as well as frame rates up to 120fps.
  Addition of HLG transfer characteristics: adds support for Hybrid Log–Gamma (HLG) opto-electronic transfer function as part of the existing provision for High Dynamic Range colour encoding. HLG is expected to be especially useful in the production and distribution of live Virtual Reality experiences.
  This Work item is now complete.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
8K_VR_5G (Operation Points for 8K VR 360 Video over 5G) | CR to TS 26.118 CR to TS 26.511 CR to TR 26.925 | 85% -> 100% complete ! | SA#91 -> SA#92 | SP-210534: CRs on Operation Points for 8K VR 360 Video & addition of HLG Characteristics [26.118] (WI: 8K_VR_5G)
Note: Progress since last SA is shown with blue colour.

## Slide 17: Overview of work progress Rel-17 Work Items
Note: Progress since last SA is shown with blue colour.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
IVAS_Codec (EVS Codec Extension for Immersive Voice and Audio Services) | New set of 8 TSs and 1 TR on Codec for Immersive Voice and Audio Services CR to 26.114 | 27% | SA#96 | None
ITT4RT (Support of Immersive Teleconferencing and Telepresence for Remote Terminals) | CR to 26.114 and 26.223 on Support of Immersive Teleconferencing for Remote Terminals | 60% -> 75% | SA#92 -> SA#95 | SP-210377: Revised WID on 'Support of Immersive Teleconferencing and Telepresence for Remote Terminals' (ITT4RT; UID: 820003) SP-210537: CR on ITT4RT Features
HaNTE (Handsets Featuring Non-Traditional Earpieces) | CR to 26.131 on update of receive direction requirements CR to 26.132 on update of receive direction test methods CR to 26.801 on update with new findings | 40% -> 70% | SA#93 | None

## Slide 18: Overview of work progress Rel-17 Work Items
Note: Progress since last SA is shown with blue colour.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
HInT (Extension for headset interface tests of UE) | CRs to TS 26.131 CRs to TS 26.132 | 50% -> 70% | SA#93 | None
8K_VR_5G (Operation Points for 8K VR 360 Video over 5G) | CR to TS 26.118 CR to TS 26.511 CR to TR 26.925 | 85% -> 100% complete ! | SA#91 -> SA#92 | SP-210534: CRs on Operation Points for 8K VR 360 Video & addition of HLG Characteristics [26.118] (WI: 8K_VR_5G)

## Slide 19: List of SA4 Work Items for Rel-18
Rel-18 Work Items
ATIAS (Terminal Audio quality performance and Test methods for Immersive Audio Services)

## Slide 20: ATIAS (Terminal Audio quality performance and Test methods for Immersive Audio Services)
The overall objective of this work item is to develop a set of test specifications similar to TS 26.131 and 26.132 for objective characterization of terminals for 3GPP immersive services. This covers both conversational services based on MTSI / telepresence and non-conversational services. The tests will be limited to the use of an acoustic or a digital / analog audio interface. WID: SP-190040
Since SA#91-e, the following progress was achieved:
  Objective tests results with a conferencing scenario and headphone playback have been discussed.
  One input on motion to sound latency measurement has been discussed.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
ATIAS (Terminal Audio quality performance and Test methods for Immersive Audio Services) | TS 26.261 Terminal audio quality performance requirements for immersive audio services | 20% | SA#98 | None
Note: Progress since last SA is shown with blue colour.

## Slide 21: List of SA4 Study Items
Ongoing Study Items
FS_VR_CoGui (VR Streaming Conformance and Guidelines)
FS_5GMS_Multicast (Feasibility Study on Multicast Architecture Enhancements for 5GMSA) – 100% complete !
FS_XRTraffic (Feasibility Study on Typical Traffic Characteristics for XR Services and other Media)
FS_EMSA (Feasibility Study on Streaming Architecture extensions For Edge processing) – 100% complete !
FS_5GVideo (Feasibility Study on 5G Video Codec Characteristics)
FS_FLUS_NBMP (Feasibility Study on the use of NBMP in E_FLUS)
FS_5GSTAR (Feasibility Study on 5G Glass-type AR/MR Devices)
FS_5GMS_EXT (5G media streaming extensions)
FS_NPN4AVProd (Feasibility Study on Media Production over 5G NPN)

## Slide 22: FS_VR_CoGui (Feasibility Study on VR Streaming Conformance and Guidelines)
Objective: provide content generation and usage guidelines for the technologies defined in TS 26.118. WID: SP-190642
Since SA#91-e there was no progress. The timeplan was extended to allow for the consideration of further inputs.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_VR_CoGui (Feasibility Study on VR Streaming Conformance and Guidelines) | New TR 26.999 Virtual Reality (VR) streaming interoperability and characterization | 20% | SA#92 -> SA#94 | None
Note: Progress since last SA is shown with blue colour.

## Slide 23: FS_5GMS_Multicast (Feasibility Study on Multicast Architecture Enhancements for 5GMSA) - complete !
Objective: The goal of this study item is to identify and evaluate potential enhancements to the 5G Media Streaming Architecture to provide multicast-broadcast media streaming services. WID: SP-200055
Since SA#91-e, the following progress was achieved:
  TR 26.802 V2.0.0 titled, 'Multicast Architecture Enhancement for 5G Media Streaming' (Release 17) is presented to TSG SA for approval. This Technical Report identifies and evaluates key issues to enable 5MBS User Service Architecture, and, as one scenario, the potential enhancements to the 5G Media Streaming Architecture to provide multicast-broadcast media streaming services. The TR is now 100% completed. It has addressed various aspects of the following key issues and provided conclusions for each key issue. Lastly, the TR recommended normative work and next steps.
  A Corresponding Work Item was agreed.
  The Study Item is now complete.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_5GMS_Multicast (Feasibility Study on Multicast Architecture Enhancements for 5GMSA) | TR 26.802 | 60% -> 100% complete ! | SA#92 | SP-210379: TR 26.802 V2.0.0 titled, 'Multicast Architecture Enhancement for 5G Media Streaming' (Release 17)
Note: Progress since last SA is shown with blue colour.

## Slide 24: FS_XRTraffic (Feasibility Study on Typical Traffic Characteristics for XR Services and other Media)
Objective: Collect and document traffic characteristics for different services, and additional information, such as codecs and protocols in use. Identify additional relevant XR and other media services and document their traffic characteristics. WID: SP-210043
Since SA#91-e, the following progress was achieved:
  Introduction, scope and 3GPP references to relevant TRs were added to draft TR 26.926 V0.2.0 Traffic Models and Quality Evaluation Methods for Media and XR Services in 5G Systems.
  Several updates were made to the permanent document.
  An LS on Status Update on XR Traffic was sent to RAN1.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_XRTraffic (Feasibility Study on Typical Traffic Characteristics for XR Services and other Media) | CRs to TR 26.925 | 55% -> 65% | SA#93 | None
Note: Progress since last SA is shown with blue colour.

## Slide 25: FS_EMSA (Feasibility Study on Streaming Architecture extensions For Edge processing) - complete !
Objective: determine the processes for discovering, configuring, running, and managing media processing workflows on the 5G edge and network. Study the mapping of the new processes into the 5GMSA architecture. How to leverage architecture and functions defined by SA2 and SA6 for edge computing and applications. WID: SP-200056
Since SA#91-e, the following progress was achieved:
  TR 26.803 V2.0.0 titled, 'Study on 5G Media Streaming Extensions for Edge Processing' (Release 17) is presented to TSG SA for approval. This Technical Report provides a set of use cases for multimedia processing in the edge. It also documents existing 3GPP solutions and enablers for media processing at the edge. Finally, it identifies existing gaps in the 5G Media Streaming Architecture (5GMSA) and recommends a set of extensions to the 5GMSA to integrate edge media processing.
  A Corresponding Work Item was agreed.
  The Study Item is now complete.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_EMSA (Feasibility Study on Streaming Architecture extensions For Edge processing) | TR 26.803 | 60% -> 100% complete ! | SA#92 | SP-210380: TR 26.803 V2.0.0 titled, 'Study on 5G Media Streaming Extensions for Edge Processing' (Release 17)
Note: Progress since last SA is shown with blue colour.

## Slide 26: FS_5GVideo (Feasibility Study on 5G Video Codec Characteristics)
Objective: primarily to identify relevant interoperability requirements, performance characteristics and implementation constraints of video codecs in 5G services, and to characterize existing 3GPP video codecs, in particular H.264/AVC and H.265/HEVC in order to have a benchmark for the addition of potential future video codecs. WID: SP-200052
Since SA#91-e,
  Several items were progressed: HEVC bitstreams provided for screen content scenario, clarifications on quality metrics, description of the software package from the characterization framework, clarifications on reference software versioning, configuration files for EVC, HEVC external performance compared to AVC from JVET…
  A revision of the Study Item was agreed. This update includes the AV1 codec from AOM in its scope. It adds clarifications on expected information associated to codecs under consideration for characterization in this study, namely AV1, EVC and VVC.
  An LS on Cloud Gaming Efforts in 3GPP SA4 was sent to ITU-T SG12
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_5GVideo (Feasibility Study on 5G Video Codec Characteristics) | TR 26.955 | 55% -> 70% | SA#92 -> SA#94 | SP-210378: Revised SID on Feasibility Study on 5G Video Codec Characteristics (FS_5GVideo; UID: 870011)
Note: Progress since last SA is shown with blue colour.

## Slide 27: FS_FLUS_NBMP (Feasibility Study on the use of NBMP in E_FLUS)
Objective: to identify the workflow for NBMP (Network Based Media Processing ) media processing with the TS 26.238. Such workflow should start from a request for the establishment of a FLUS session and then include the instantiation, running and monitoring of media processing application requested by FLUS source on a FLUS sink. WID: SP-200053
Since SA#91-e, the following progress was achieved:
  The draft CR to TR 26.939 was progressed and now includes: references, assumptions and requirements, use-cases, example FLUS call flow with Network-Based Media Processing (NBMP) + NBMP with FLUS using AF, Gap analysis for each deployment scenario
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_FLUS_NBMP (Feasibility Study on the use of NBMP in E_FLUS) | CRs to TR 26.939 | 40% -> 96% | SA#93 | None
Note: Progress since last SA is shown with blue colour.

## Slide 28: FS_5GSTAR (Feasibility Study on 5G Glass-type AR/MR Devices)
Objectives (summary): Provide formal definitions for the functional structures of AR glasses, describe key use cases for AR services over 5G, describe the architecture for media flow relevant to the use cases identified and Identify necessary content delivery transport protocols and capability exchange mechanisms, as well as suitable 5G system functionalities (e.g., device, edge, network) and QoS. WID: SP-200399
Since SA#91-e, the following progress was achieved:
  Draft TR 26.998 v0.8.0 now includes edits on: how AR/MR service scenarios can be supported in 5G system architecture, Edge-assisted STAR support, Call Flow Updates for Streaming to STAR UE, Call Flow Updates for Streaming to EDGAR UE, Work related to AR Runtime (OpenXR, WebXR), Updates to Procedures for 5G Downlink Streaming using a STAR UE, Architecture updates, Content formats and codecs, Background on MPEG Scene Description, Update on Use Cases Mapping, Basic UE AR related Processes and Functions, Architecture mapping for AR conversational services and call flow.
  Completion of the study extended by 1 SA meeting cycle (Sept.2021).
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_5GSTAR (Feasibility Study on 5G Glass-type AR/MR Devices) | TR 26.998 Support of 5G glass-type Augmented Reality / Mixed Reality (AR/MR) devices | 20% -> 65% | SA#93 -> SA#94 | None
Note: Progress since last SA is shown with blue colour.

## Slide 29: FS_5GMS_EXT (5G media streaming extensions)
The objective of this study is in the context of the following potential improvements and extensions to 5G Media streaming: Content Preparation, Traffic Identification, Additional / New transport protocols, Uplink media streaming, Background traffic, Content Aware Streaming, Network Event usage, Per-application-authorization, Support for encrypted and high-value content, Scalable distribution of unicast Live Services.
Since SA#91-e, this Study Item progressed up to 40% completion. It is due to be completed in Sep. 2021. TR 26.804 Study on 5G media streaming extensions (Release 17) progressed to v0.4.0. Several additions were agreed on: Update on relevant architecture components for traffic identification; New transport protocols/Corrections and Improvements; Key Topic Scalable distribution of unicast Live Services; Candidate solution for Content Preparation format; Uplink streaming; Interfaces and Formats for AF Data Collection and Event Exposure
As a result of intermediate conclusions, further normative work was agreed in a New WID on 5GMS AF Event Exposure (EVEX).
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_5GMS_EXT (5G media streaming extensions) | TR 26.804 5G Media Streaming Extensions | 5% -> 40% | SA#93 | None
Note: Progress since last SA is shown with blue colour.

## Slide 30: FS_NPN4AVProd (Feasibility Study on Media Production over 5G NPN)
The study will identify the relevant media production use cases (professional, semi-professional, production, contribution); develop one or several reference media production architecture(s); identify relevant QoS requirements for media production workflows; identify relevant 5G System features like NPNs, Network Slicing, QoS classes, network event reporting and assistance, etc. that are useful for media production;
Since SA#91-e, the work was started. This Study Item progressed up to 15% completion. It is due to be completed in Mar. 2022. TR 26.805 Study on Media Production over 5G NPN Systems (Release 17) progressed to v0.2.0 with additions on Structure of the technical report; Description of existing media protocols in media production; Description of camera media flows in a Multi-Camera production; Overview of NMOS functionality; Utilizing Available Capacity in Multi-Camera Scenarios and Addition of different production types and addition of more information about existing workflows.
Work Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_NPN4AVProd (Feasibility Study on Media Production over 5G NPN) | TR 26.805 Study on Media Production over 5G NPN Systems | 0% -> 15% | SA#95 | None
Note: Progress since last SA is shown with blue colour.

## Slide 31: Overview of work progress Study Items
Note: Progress since last SA is shown with blue colour.
Study Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_VR_CoGui (Feasibility Study on VR Streaming Conformance and Guidelines) | New TR 26.999 Virtual Reality (VR) streaming interoperability and characterization | 20% | SA#92 -> SA#94 | None
FS_5GMS_Multicast (Feasibility Study on Multicast Architecture Enhancements for 5GMSA) | TR 26.802 | 60% -> 100% complete ! | SA#92 | SP-210379: TR 26.802 V2.0.0 titled, 'Multicast Architecture Enhancement for 5G Media Streaming' (Release 17)
FS_XRTraffic (Feasibility Study on Typical Traffic Characteristics for XR Services and other Media) | CRs to TR 26.925 | 55% -> 65% | SA#93 | None
FS_EMSA (Feasibility Study on Streaming Architecture extensions For Edge processing) | TR 26.803 | 60% -> 100% complete ! | SA#92 | SP-210380: TR 26.803 V2.0.0 titled, 'Study on 5G Media Streaming Extensions for Edge Processing' (Release 17)
FS_5GVideo (Feasibility Study on 5G Video Codec Characteristics) | TR 26.955 | 55% -> 70% | SA#92 -> SA#94 | SP-210378: Revised SID on Feasibility Study on 5G Video Codec Characteristics (FS_5GVideo; UID: 870011)

## Slide 32: Overview of work progress Study Items
Note: Progress since last SA is shown with blue colour.
Study Item | Expected output | Completion-% | Target completion | Input documents to SA
FS_FLUS_NBMP (Feasibility Study on the use of NBMP in E_FLUS) | CRs to TR 26.939 | 40% -> 96% | SA#93 | None
FS_5GSTAR (Feasibility Study on 5G Glass-type AR/MR Devices) | TR 26.998 Support of 5G glass-type Augmented Reality / Mixed Reality (AR/MR) devices | 20% -> 65% | SA#93 -> SA#94 | None
FS_5GMS_EXT (5G media streaming extensions) | TR 26.804 5G Media Streaming Extensions | 5% -> 40% | SA#93 | None
FS_NPN4AVProd (Feasibility Study on Media Production over 5G NPN) | TR 26.805 Study on Media Production over 5G NPN Systems | 0% -> 15% | SA#95 | None

## Slide 33: New WID on 8K Television over 5G (8K_TV_5G)
SP-210381: New WID on 8K Television over 5G (8K_TV_5G)
The work item will have the following objective:
  The objective of this Work Item is to specify an HEVC-based 8K TV operation point in TS 26.116 as well as the corresponding media decoding capabilities for 5GMS in TS 26.511 in order to enable support for up to 8K video
Output:
  CR to TS 26.116 on Operation Points for 8K Television over 5G (Rel-17)
  CR to TS 26.511 on Decoding Capabilities and Operation Points for 8K Television over 5G (Rel-17)
  CR to TR 26.925 on Typical traffic characteristics for 8K Television over 5G (Rel-17)
  CR to TR 26.955 on 8K TV Scenario: Reference Sequences and Anchors (Rel-17)
Target completion date: SA#95, Target Release: Rel-17

## Slide 34: New WID on 5GMS AF Event Exposure (EVEX)
SP-210374: New WID on 5GMS AF Event Exposure (EVEX)
The work item will have the following objectives:
  Define the media related data and formats for the media session data to be exposed by the 5GMS AF. The carriage in existing AF events or the definition of new AF Events will be subject to agreements with SA2.
  Enhance the 5GMS AF data collection to support direct and indirect collection of UE data pertaining to media sessions.
  Devise mechanisms to control the access to the collected media session data.
  Define a generic architecture within which media-specific solutions for the configuration and subsequent operation of data collection and data reporting (via event exposure) by the AF can be specified.
Output:
  New TS on Data Collection and Reporting; General
  CRs to TS 26.501 and TS 26.512.
Target completion date: SA#95, Target Release: Rel-17

## Slide 35: New WID on Edge Extensions to the 5G Media Streaming Architecture (5GMS_EDGE)
SP-210375: New WID on Edge Extensions to the 5G Media Streaming Architecture (5GMS_EDGE)
The work item will have the following objectives:
  Extend the 5GMS architecture to support edge media processing according to the recommended architecture in TR 26.803 clause 6.2.
  Enhance the procedures and services that are offered by the 5GMS AF and the 5GMS Client to enable establishment and management of media streaming sessions with edge processing.
  Define application context for media applications and specify relocation scenarios, conditions, triggers, information, and procedures for session continuity in edge media processing.
Output:
  CR to TS 26.501 on Extensions to the 5GMS Architecture to add support for edge media processing
Target completion date: SA#93, Target Release: Rel-17

## Slide 36: New WID on 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA)
SP-210376: New WID on 5G Multicast-Broadcast User Service Architecture and related 5GMS Extensions (5MBUSA)
The work item will have the following objectives:
  Specify the 5MBS User Service architecture
  Define relevant call flows and procedures to support 5GMS over 5MBS; 5GMS hybrid unicast/broadcast services; 5MBS usage independent of 5GMS.
  Extend the 5G Media Streaming architecture by providing a general description and architecture
  Note that there is a dependency on SA2’s work on Rel-17 TS 23.247.
Output:
  New TS e.g. TS 26.502 5G Multicast-Broadcast User Service Architecture
  CR to TS 26.501 on Extensions to 5G Media Streaming for 5GMS via 5MBS, 5GMS hybrid services, 5GMS via eMBMS and Multicast ABR with 5GMS and 5MBS.
Target completion date: SA#96, Target Release: Rel-17

## Slide 37: Dependencies on IETF drafts in SA4
No new dependency introduced
All dependencies removed
IETF dependencies in SA4: new ones with red colour, those removed with green colour, and other updates by blue colour:
IETF draft name | 3GPP spec. number | CR# which introduced the dependency | Responsible person (in SA4) | Feature (Release) | Comments
draft-ietf-clue-framework | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-clue-datachannel | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-clue-signalling | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-clue-data-model-schema | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-clue-protocol | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-clue-rtp-mapping | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-mmusic-sctp-sdp | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-mmusic-data-channel-sdpneg | 26.223 | - | Ozgur Oyman (ozgur.oyman@intel.com), Intel | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536
draft-ietf-mmusic-sdp-simulcast | 26.223 | - | Bo Burman (bo.burman@ericsson.com), Ericsson LM | IMS_TELEP_S4 (Rel-13) | Resolved by SP-210536

## Slide 38: Summary of action items
Action Points from SA#91-e to SA4:
  None
Action items from SA4 to SA#92-e:
  Approve all SA4 agreed CRs, TRs, new and revised WIDs.