## Slide 1
5GAA input to 3GPP SA Rel-18 Workshop
262306112
SP-210619

## Slide 2: Introduction
5GAA, the 5G automotive association, appreciates the opportunity to provide guidance to 3GPP on the important features for Rel-18 evolution.
Scope of 5GAA is focused on bringing connectivity solutions to market addressing technical, business, and regulatory challenges including technology, standards, spectrum, policy & regulations, testing, business models & go-to-market
It is important to note that C-V2X is in development in different countries, with several milestones in the US and active deployment in China.

## Slide 3: Introduction
5GAA already provided an input to the 3GPP RAN Rel-18 Workshop in June 2021 – RWS-210360
A list with eight topics in decreasing order of priority (see next slide) was submitted with corresponding motivation for each item (see annex)
Some of the 5GAA prioritized topics have End-2-End aspects and are related to Study Items currently discussed in SA2
This submission provides a potential correlation of 5GAA RAN relevant topics to 3GPP SA2 Rel-18 Study Item proposals
5GAA has also identified a list of topics and areas for enhancements of QoS Prediction/Sustainability

## Slide 4: 5GAA list of proposals according priority ranking submitted to 3GPP RAN Rel-18 Workshop*
5GAA features and requirements proposals | Priority ranking
Positioning enhancements | 1
LTE/NR-V2X sidelink co-channel coexistence | 2
Sidelink carrier aggregation (CA) | 3
Enhancements to sidelink power saving | 4
Predictive QoS | 5
UE-to-UE relay | 6
NR-V2X sidelink adjacent-channel coexistence with non-3GPP technologies | 7
Enhancements for vehicular distributed antenna system (DAS) UE transmission | 8
* See 5GAA contribution to 3GPP in: RWS-210360

## Slide 5: Potential Correlation of 5GAA prioritized 3GPP RAN topics* to 3GPP SA2 Rel-18 Study Item proposals
5GAA prioritized 3GPP RAN topic* | 3GPP SA2 Rel-18 Study Item proposals | Recent SA2 Tdoc (version) | 3GPP RAN**
Positioning enhancements | New SID on Enhancement to the 5GC LoCation Services Phase 3 New SID on Study on Ranging based services and relative positioning | S2-2106809 S2-2106376 | #10
Enhancements to sidelink power saving | New SID on Study on Proximity based Services in 5GS - Phase 2 | S2-2106806 | #06
Predictive QoS | Study on Enablers for Network Automation for 5G - Phase 3 | S2-2106808 | #16
UE-to-UE relay | New SID on Study on Proximity based Services in 5GS - Phase 2 New SID on Study of Architecture Enhancement for Vehicle Mounted Relays. | S2-2106806 S2-2106814 | #06
* See 5GAA contribution to 3GPP in: RWS-210360
262306112
262306112
** https://www.3gpp.org/news-events/2210-advanced_5g

## Slide 6: QoS Prediction & Sustainability analytics
5GAA has also some suggestions on enhancements on QoS Prediction & Sustainability analytics
  Next slide
The following use cases defined by 5GAA would benefit of those enhancements:
  Tele-operated Driving, Tele Operated Support, Automated intersection crossing, UC Awareness Confirmation, Cooperative Lateral Parking, HD maps, Cooperative Lane Merge, Coordinated, Cooperative Driving Maneuver, high density platooning, Emergency Brake Warning, Lane Change Warning, Cross-Traffic Left-Turn Assist
More details on the benefits for each enhancement is in the annexes for information

## Slide 7: Suggested enhancements on QoS Prediction & Sustainability analytics
Increase granularity of QoS predictions (e.g., below Cell level, more KPIs reporting, richer information) also by means of more input data to the analytics enabler (e.g. from core network, RAN, etc.)
Improve freshness of QoS predictions (e.g. notice period)
Enable QoS predictions also of the PC5/Sidelink Interface
Investigate QoS prediction in Multi-MNO/Cross-border environments
Investigate the need for coordination of notifications of QoS prediction amongst V2X Servers (e.g., ordering, prioritization)
Investigate harmonization of QoS change notifications for V2X application (e.g., QoS change notification sent to the UE via NAS/RRC)

## Slide 8: Conclusions
5GAA encourages 3GPP SA to consider the proposed correlation of the topics provided by 5GAA in its RAN Rel-18 WS contribution (RWS-210360) that have an end-2-end component (left column of slide 5) and the listed SA2 SI proposals (right column of slide 5) to ensure consistent e2e support in coordination with 3GPP RAN in Rel-18
Moreover, 5GAA encourages 3GPP SA to consider the suggested enhancements to the QoS prediction framework
5GAA will be able to provide more details in order to support the 3GPP SA2 studies

## Slide 9
Annexes

## Slide 10
Full 5GAA input to 3GPP RAN Rel. 18 Workshop
June 2021

## Slide 11: Introduction to 5GAA input to 3GPP RAN Rel. 18 WS
5GAA member companies submitted proposals for new features and requirements as input to 3GPP Rel.18 workshop
Via a survey, 5GAA companies:
  Rated the listed proposals in terms of priority
    (Score: 1 = Very low priority – 3 = neutral – 5 = Very high priority)
  Rated sub-topics of each proposal in terms of relevance
    (Score: 1= not at all relevant – 3 = neutral – 5 = Extremely relevant)
The survey results were consolidated and provided in their entirety, in a decreasing order according to the final ranking
The input is aligned amongst all sectors of 5GAA membership: Automotive OEM, Automotive suppliers, MNO, MNO suppliers

## Slide 12: 5GAA list of proposals according priority ranking
5GAA features and requirements proposals | Priority ranking
Positioning enhancements | 1
LTE/NR-V2X sidelink co-channel coexistence | 2
Sidelink carrier aggregation (CA) | 3
Enhancements to sidelink power saving | 4
Predictive QoS | 5
UE-to-UE relay | 6
NR-V2X sidelink adjacent-channel coexistence with non-3GPP technologies | 7
Enhancements for vehicular distributed antenna system (DAS) UE transmission | 8

## Slide 13: 1. Positioning enhancements
Motivation
  Advanced use cases require high level positioning accuracy and precision
  Advanced use cases include basic and advanced VRU protection, automated driving, teleoperated driving, dynamic intersection management, group start, etc.
Sub-topics
  Introduce mechanisms to enhance the positioning accuracy, regardless of the network coverage scenarios, i.e. in-coverage, partial coverage and out-of-coverage.
  For in-coverage scenarios, support a combined Uu and sidelink positioning mode.
  Include positioning enhancements for vehicular Distributed Antenna Systems (DAS) UE.
  To support positioning in unlicensed spectrum, thus avoiding any impact to existing V2X deployments.

## Slide 14: 2. LTE/NR-V2X sidelink co-channel coexistence
Motivation
  Dedicated V2X spectrum is scarce in some regions and LTE/NR-V2X need to co-exist even in the same channel
  Important across all basic and advanced use cases
  Improves overall system performance, increases deployment flexibility, enables technology migration path from IEEE technology
Sub-topics
  Introduce mechanisms for LTE/NR-V2X co-channel coexistence.
  Introduce mechanisms for LTE/NR-V2X co-channel coexistence taking into account existing NR-V2X Rel-16/17 solutions.

## Slide 15: 3. Sidelink carrier aggregation (CA)
Motivation
  Some advanced use cases require high data-rate and/or increased reliability
  In some regions V2X spectrum is fragmented
  Examples: High-definition sensor sharing, see through for passing,
Sub-topics
  Introduce mechanism to support NR-V2X intra-band non-contiguous CA.
  Introduce mechanism to support NR-V2X intra-band contiguous CA.
  Introduce mechanism to support NR-V2X inter-band CA FR1 + FR1. (e.g. combinations of ITS Band / Unlicensed / Licensed)

## Slide 16: 4. Enhancements to sidelink power saving
Motivation
  Some specific advanced use cases require modes of operation and/or UEs with diverse capabilities
  This includes, for example,
    reliable and sustainable operation of Automated Valet Parking (AVP), to allow maneuver and authentication of requested/activated vehicles,
    support the various types of VRU equipment and scenarios, e.g. use of on-board modem for e-Bike and micro-mobility also in battery charge mode
Sub-topics
  Further enhancements to sidelink power saving (e.g. Wake-up, go-to-sleep, adaptive DRX, etc.)
  Introduce UE reduced capabilities with sidelink.
  Introduce configurable UE sidelink power saving capabilities, e.g. different VRU types.

## Slide 17: 5. Predictive QoS
Motivation
  Advanced use cases will benefit from improved predictive QoS, including their safety enhancement goals
  Current and future QoS information such as latency, for example, is essential for safe and high quality teleoperated driving
Sub-topics
  Introduce more accurate sidelink and Uu Reporting.
  Improve E2E reporting e.g. signalling based latency, fine granular reporting.
  Introduce sidelink report equivalent information as MBB-UE (Mobile Broadband UE) in terms of MDT (Minimization of Drive Test) and NR QoE (Quality-of-Experience).

## Slide 18: 6. UE-to-UE relay
Motivation
  In some environments, e.g. urban, NLOS create challenges to meet the reliability requirements of some V2X use cases.
  For example, RSUs in intersection may serve as a relay to vehicles in challenging NLOS situations.
Sub-topic
  Introduce the definition of UE-to-UE Relay for V2X operation.

## Slide 19: 7. NR-V2X sidelink adjacent-channel coexistence with non-3GPP technologies
Motivation
  V2X spectrum is scarce in some regions and non-3GPP technology is already deployed in some of the available channels
Sub-topic
  Introduce mechanism for adjacent-channel coexistence of NR-V2X with other ITS technologies.
  Introduce mechanism for adjacent-channel coexistence of NR-V2X with non-3GPP ITS technologies also to existing NR-V2X Rel-16/17 by implementing corresponding CRs or by allowing early implementations.

## Slide 20: 8. Enhancements for vehicular Distributed Antenna System (DAS) UE transmission
Motivation
  Advanced use cases operating in sidelink unicast mode and also via Uu will benefit of enhanced vehicular DAS UE transmission due to the improved signal quality
  This includes HD sensor sharing for AVs, group start, coordinated, cooperative driving manoeuvre, etc.
Sub-topic
  Include enhancements for vehicular DAS UE. E.g. sending the SL/UL signal/channel only from the antenna panel achieving the best performance for the target receiver

## Slide 21
Requirements, use cases and benefits of the proposed enhancements on QoS Prediction/Sustainability analytics

## Slide 22: Motivation for identified enhancements on QoS Prediction/Sustainability analytics
Requirements | Example Use Cases | Benefits
Increase granularity of QoS predictions (e.g., below Cell level, more KPIs reporting, richer information, aware of the specific UE context) also by means of more input data to the analytics enabler (e.g. from core network, RAN, etc.) | Tele-operated Driving, Tele Operated Support, Automated intersection crossing, UC Awareness Confirmation, Cooperative Lateral Parking, HD maps. | More precise (in terms of space) prediction of the QoS is important, especially for safety related use cases. A cell level QoS prediction will not be precise enough for any UE within the cell, since in specific parts of a cells (i.e., streets) the experienced QoS will be less or higher than the current cell-level QoS prediction. Moreover, the QoS of two different UEs within the same cell can be different also because of other factors, such as the type of the UE (e.g. number of antennas, design of the radio modules,etc.), subscription data (e.g. PCC rules and configured QoS profiles). Therefore QoS predictions need to be able to consider those aspects in terms of input data (collected from OAM or other sources) and in the Analytics Filter Information that is used by the consumer when analytics are requested. Also, additional parameters e.g., delay, reliability should be considered to be predicted. For instance for the ToD use cases the DL latency and reliability are important.

## Slide 23: Motivation for identified enhancements on QoS Prediction/Sustainability analytics
Requirements | Example Use Cases | Benefits
Improve freshness of QoS predictions (e.g. notice period) | Tele-operated Driving, Tele Operated Support, Automated intersection crossing, Cooperative Lane Merge, “Coordinated, Cooperative Driving Manœuvre”, high density platooning, Emergency Brake Warning. | Many V2X use cases need to receive notifications about the expected changes of the real time QoS in the next seconds (i.e., short term QoS prediction). This is important for potential adaptations e.g., speed change, change application’s configuration or mode of operation, safe stop etc.

## Slide 24: Motivation for identified enhancements on QoS Prediction/Sustainability analytics
Requirements | Example Use Cases | Benefits
Enable QoS predictions also of the PC5/Sidelink Interface | Cooperative Lane Merge, “Coordinated, Cooperative Driving Manœuvre”, Automated intersection crossing, Intersection Movement Assist, high density platooning, Emergency Brake Warning, Lane Change Warning, UC Awareness Confirmation, Cross-Traffic Left-Turn Assist, Cooperative Lateral Parking | QoS prediction functionality is required also for the PC5 interface, since many use cases will be realised via the PC5 interface. It helps to enhance the transmission of functional safety related data and improve the overall quality of a function by boosting the availability of the function.

## Slide 25: Motivation for identified enhancements on QoS Prediction/Sustainability analytics
Requirements | Example Use Cases | Benefits
Investigate QoS prediction in Multi-MNO/Cross-border environments | Most of the use cases considered above (using Uu or PC5 interfaces) will be realised during the moment the vehicle moves to another country or changes MNO. | QoS prediction information should be provided during the handover from one MNO to another, considering requirements mentioned above about freshness and /or granularity of predicted QoS change. or at least notify early enough the vehicle about availability or not of the QoS prediction service. When a UE with a subscription of MNO A is roaming in the network of MNO B, prediction service should be available while in MNO B without interruption. However the MNO B network (in case the serving NWDAF is in the visited network) or the home network (in case the serving NWDAF is in the home network) may need to exchange information in order to provide reliable predictions. This because the prediction may depend from input data in the visited network as well as information available in the home network (e.g. subscription information). Other scenarios that require exchange of QoS prediction information across several MNO include the case of MEC resource sharing (e.g. a UE of MNO A may use MEC resources such as MEC platform or MEC application) deployed in the network of MNO B).

## Slide 26: Motivation for identified enhancements on QoS Prediction/Sustainability analytics
Requirements | Example Use Cases | Benefits
Investigate the need for coordination of notifications of QoS prediction amongst V2X Servers (e.g., ordering, prioritization). | Applies to all use cases mentioned above. | In case of distributed automotive applications there could be multiple consumers interested to receive QoS predictions and trigger related actions (e.g. vehicle change, change codec, change network, etc.) for the same predicted QoS change event. One example is the application instance running in the UE and the instance running in the cloud. However in general there could be multiple application servers that could trigger related actions in different domains (OEM, service provider, RTA, MNO). This requirement is needed in order to make sure that there is a predictable and predefined order in which notifications are received amongst the multiple consumers. At the same time NWDAF may also perform some level of coordination by deciding to trigger the notification to one consumer only after another consumer with higher priority. Different QoS prediction requests may have different priority that should be considered, since each notification may trigger an application adaptation that may affect the following/next QoS prediction notifications. Hence, the coordination of a notifications may increase the reliability of how the provided predictions are handled in the applications.

## Slide 27: Motivation for identified enhancements on QoS Prediction/Sustainability analytics
Requirements | Example Use Cases | Benefits
Investigate harmonization of QoS change notifications for V2X application (e.g., QoS change notification sent to the UE via NAS/RRC) | Applies to all use cases above | Ensure that different notifications related to QoS (e.g. Notification control with or without Alternative QoS profiles) are delivered in a similar/harmonized manner. This can help to avoid the increase of complexity for the application layer. Moreover in order to evaluate the performance of the service provided by the analytics enabler it may be required to be able to correlate the QoS change notification (that is sent by the network when the QoS change happens) with the potential QoS change (that is sent by the network when the same QoS change is predicted). In fact when QoS prediction is used for a GBR type QoS flow both notifications are produced by the network. However at the moment it is not possible (both for the application and the network) to correlate the two notifications that are related to the same QoS change event. This is particularly useful in order to calculate relevant metrics that can measure the effectiveness of the QoS prediction service (e.g. ratio of correct prediction or difference between what was predicted and what really happened).