3GPP TSG-S1 	Tdoc S1-99374

Hampton Court, UK

10-12 May 1999

| CHANGE REQUEST No : |  | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
| --- | --- | --- |
| 3GPP Technical Specification | 22.101 | Version: | 3.5.0 |  |
| Submitted to SA | 4 | for approval | x | without presentation ("non-strategic") |  |  |
| list SA plenary meeting no. here ( | for information |  | with presentation ("strategic") | x |  |
| PT SMG CR cover form is available from: http://docbox.etsi.org/tech-org/smg/Document/smg/tools/CR_form/crf28_1.zip |

| Proposed change affects: | SIM | x | ME | x | Network | x |
| --- | --- | --- | --- | --- | --- | --- |

(at least one should be marked with an X)

| Work item: |  |
| --- | --- |

| Source: | S1 | Date: | 25/5/99 |
| --- | --- | --- | --- |

| Subject: | Support of Emergency Calls in UMTS |
| --- | --- |

| Category: | F Correction |  | Release: | Phase 2 |  |
| --- | --- | --- | --- | --- | --- |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (one category | B Addition of feature | x |  | Release 97 |  |
| and one release | C Functional modification of feature |  |  | Release 98 |  |
| only shall be | D Editorial modification |  |  | Release 99 | x |
| marked with an X) |  |  |  |  |  |

| Reason for change: | Adds a requirement for the network to able to obtain the number that a user has input for an emergency call. This will allow the network to route the call to the appropriate emergency service if more than one emergency number is supported in a country |
| --- | --- |

| Clauses affected: | 8.4 |
| --- | --- |

| Other specs | Other releases of same spec |  | ( List of CRs: |  |
| --- | --- | --- | --- | --- |
| affected: | Other core specifications |  | ( List of CRs: |  |
|  | MS test specifications / TBRs |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |

| Other comments: |  |
| --- | --- |

<--------- double-click here for help and instructions on how to create a CR.

8.3	Security for the user

It should be possible for the user to authenticate the network when registering and before initiating a service if desired.

Steps shall be taken to ensure the privacy and integrity of sensitive information transferred between the user and all other entities; e.g. user identity and user traffic.

## 8.4	Emergency calls

UMTS shall support an emergency call teleservice as defined in GSM 02.03 which fulfils the following service requirements:

- It shall be possible to identify a particular speech call as an emergency call to the serving network. This may be based upon one or more numbers stored in either the USIM or UE, or some other method.

- It shall be possible to initiate an emergency call when  the USIM is not present (this may require a default number to be stored in the UE as above). The terminal shall be responsible for ensuring that only emergency numbers are attempted when no USIM is present to prevent the misuse of network resources. It will be left to the national authorities to decide whether the network should accept such calls. In addition networks may also validate that only emergency calls are accepted when no USIM is inserted in the terminal.

- It shall be possible for the serving network to obtain the number the user has input for the emergency call.

Note: This will allow the network to route the call to different emergency call centres if appropriate.